## Slide 1: MC2: Evolution and Future of Synchrotron Radiation Sources
RIKEN SPring-8 Center
Hitoshi TANAKA
2026/05/16@Deauville
History of synchrotron radiation source development
Diffraction-limited SR sources
Single-pass free-electron lasers
Future development direction with a few topics

## Slide 2: Brilliance enhancement over the past century
1st-gen
2nd-gen
3rd-gen
4th-gen
Linac-based FELs
Ring-based SRLs
Makina Yabashi and Hitoshi Tanaka, Nat. Photon. 11 (2017) 12-14
Notes: This shows the average brightness enhancement of SR sources to date. In the first generation, X-rays were used secondarily in lepton ring accelerators for high-energy physics. In the second generation, X-rays from bending magnets in dedicated storage rings were used, and in the third generation, undulators were used as the light source instead of bending magnets, enabling the generation of high-brilliant X-rays by utilizing single-electron interference conditions. We are now in the fourth generation, and brilliant X-rays with high transverse coherence are available. The average brilliance enhancement appears to have slowed down since 2000, which clearly indicates that beam emittance is approaching the diffraction limit condition. Blue symbols indicate linac-based FEL facilities.

## Slide 3: Brilliance enhancement over the past century
1st-gen
2nd-gen
3rd-gen
4th-gen
Linac-based FELs
Ring-based SRLs
Makina Yabashi and Hitoshi Tanaka, Nat. Photon. 11 (2017) 12-14
Notes: This shows the peak brilliance enhancement of SR sources to date. Peake brilliance enhancement looks almost saturated in the 3rd-generation. This is because, since the third generation, the beam emittance has decreased, making stable beam operation at high bunch currents difficult. On the other hand, linac-based FEL sources have achieved a significant performance improvement of several orders of magnitude by longitudinally coherent X-ray radiation. Next, let’s see the recent evolution of SR sources enclosed by red dashed line.

## Slide 4: Recent evolution of SR sources
X-ray
sources
Ring-based
Time axis
Pulse
Linac-based
SASE-type
XFEL
High Peak
Brilliance
CW
3rd gen.
SR
High
coherence
SR source
High
Average
Brilliance
Distinct operational domains
Performance index: Brilliance
Warm RF
Notes: Up to date, FELs and ring-type SR sources have been developed independently as pulse and CW sources, respectively as shown here.

## Slide 5: Recent evolution of SR sources
Performance index: Brilliance
X-ray
sources
Ring-based
Time axis
Pulse
Linac-based
SASE-type
XFEL
High Peak
Brilliance
+
High
Average
Brilliance
CW
3rd gen.
SR
High
coherence
SR source
High
Average
Brilliance
Warm RF
Coherent ring
source
High rep. rate FEL
FEL can provide not only “high peak brilliance” but also ”high average brilliance”
Cold RF
Notes: However, emergence of “super-conducting high-repetition-rate” FELs have changed the situation. This FEL system can provide not only high peak brilliance but also high average brilliance.

## Slide 6: Recent evolution of SR sources
Performance index: Brilliance
X-ray
sources
Ring-based
Time axis
Pulse
Linac-based
SASE-type
XFEL
High Peak
Brilliance
+
High
Average
Brilliance
CW
3rd gen.
SR
High
coherence
SR source
High
Average
Brilliance
Warm RF
Coherent ring
source
High rep. rate FEL
Multi-user dream facility with both high peak and average brilliance
Cold RF
Multi-
BLs
Notes: A dream machine composed of super-conducting linac with a high repetition rate of a few MHz, equipped with a pulse-by-pulse beam switching system and a few tens of FEL beamlines, can exceed than a ring-type SR in terms of peak and average brilliance, and can potentially provide the similar number of beam lines to that at ring-type SR.

## Slide 7: Role sharing between FELS and ring-based SRs
Performance index: Brilliance
.
.
Question:
Will a ring-based light source still be needed in the future?
FEL Beamlines
#1
#2
#3
#30
A few MHz SC RF Linac
Image of multi-user dream facility
Pulse-by-pulse switching system
Notes: This schematically shows the mentioned dream machine looks like. Here we naturally have the following question. Will a ring-based light source still be needed in the future? Of course, answer is yes!

## Slide 8: Role sharing between FELS and ring-based SRs
Performance characteristics of FELs
Limited photon energy from SX to X
High peak brilliance 1029 to1034
High coherence
Short pulse width sub to a few tens fs
Non-negligible shot by shot variations
P. Schmuser, M. Dohlus, J. Rossbach, C. Behrens,
Springer Tracts in Modern Physics 258 2nd ed., p167.
Peak Brilliance
Notes: Let’s see the performance characteristics of a FEL source. It is characterized by the high peak brilliance, high coherence, and short pulse duration. On the other hand, compared with a ring type SR source, available photon energy and stability are currently restricted.

## Slide 9: Role sharing between FELS and ring-based SRs
DI/I~0.02%
DE/E< 0.001%
Photon energy extended to a few 100 keV
Average brilliance from1018 to 1021
Low Coherence
Long pulse width a few tens ps
High stability and reproducibility
Photon Energy
Average Brilliance
Performance characteristics of ring-based light source
Notes: Compared with a FEL source, a ring-based SR source has extremely high stability and reproducibility. Its low peak intensity conversely enables a correlation experiment with the same sample, which is quite important for most of experimental users.

## Slide 10: Role sharing between FELs and ring-based SRs
s
1
Space
Time
ms
ms
ns
ps
fs
as
cm
mm
mm
nm
10-18
10-15
10-12
10-9
10-6
10-3
1
10-3
10-6
10-9
10-10
Multi-scale in time and space
FELs
Ring-based
SRs
High peak brilliance is not a universal solution
High transverse and longitudinal coherence such as a laser is not essential for all experiments
Correlation measurements using the same sample are extremely useful in various experiments
The utilization of higher photon energy becomes increasingly important for various applications
Systems to be studied by SRs are complex and multi-scaled in time and space
Notes: The necessity of light source is not simply determined in terms of brilliance only. Research objects of our experimental users are complex and multi-scaled systems in time and space as shown here on the left. Synergistic use of FELs and ring-type SR sources is crucial for fully research their multi-scaled objects across micro- to macroscopic phenomena.

## Slide 11
History of synchrotron radiation source development
Diffraction-limited SR sources
Single-pass free-electron lasers
Future development direction with a few topics
Notes: Next, we outline the diffraction-limited SR source, because this is a cutting-edge of a ring-based SR source.

## Slide 12: Diffraction limit
For a given wavelength l, the product of its size and angular divergence can not be less than l/4p (= . In the case of undulator radiation
1D phase space of light
1D phase space of
electron beam
angular divergence
size
x’(y’)
x(y)
: convolution of contributions from photons and electrons to parameter i
When the horizontal and vertical phase space volumes of “light source” are nearly l/4p, this radiation is called diffraction limited and it gives transverse full coherence.
Electron
Photon
Photon
Notes: Light with a wavelength of Lamda has an intrinsic volume in 2D phase space determined by the Heisenberg uncertainty principle. The brilliance of SR emitted from the electron beam is evaluated by the photon flux divided by the transverse phase volume. In the case where the transverse electron volume is negligibly small compared with photon volume, the transverse coherence becomes full and this condition, we call “diffraction limited”.

## Slide 13: Scaling of natural emittance
,
g: Lorentz factor
q: Bending angle
r: bending radius
H: H-function
Jx: Damping partition number
hx: Horizontal dispersion
: Horizontal dispersion angle
: Horizontal beta
: Horizontal alfa
As the number of bending magnets increases, natural emittance
decreases inversely proportional the cubic of that number.
Notes: To satisfy the diffraction limited condition in the X-ray wavelength range, we need an extremely small natural emittance. As shown here, natural emittance is expressed in terms of several beam and ring parameters. Of particular note is the fact that the emittance is proportional to the cube of the deflection angle. This scaling clearly shows that Multi-Bend Achromat configuration is an effective way to achieve low beam emittance.

## Slide 14: Suppression of radiation excitation to achieve lower emittance
2BA
bx, by
bx, by
hx
hx
The excited amplitude of a betatron oscillation is determined by the local energy dispersion.
The MBA lattice can effectively suppress the energy dispersion along the ring as shown below.
Notes: This strong nonlinear dependence of the emittance on the bending angle can be explained as follows. The excitation of betatron oscillations is determined by local linear energy dispersion. Square of energy dispersion in the H-function is proportional to the 4th power of the deflection angle, but the number of dispersive arcs depends on the inverse of the deflection angle. Consequently, the H-function integrated over the ring is proportional to the cube of the deflection angle.

## Slide 15: What breakthroughs made the MBA possible?
Narrow space issues
Strong nonlinearity from chromaticity correction sextupoles
Beam injection scheme applicable for a ring with a small dynamic aperture
Stable top-up beam injection compensating a short beam-lifetime and transparent against small emittance stored beam
The following issues need to be overcome:
Notes: Why could we successfuly introduce the MBA configuration to the ring recently? The answer is we could resolve the four critical issues in designing the MBA lattice shown here; narrow spacing, instability due to the strong nonlinear fields, beam injection applicable for a ring with poor stability, i.e., small dynamic aperture, and transparent top-up beam injection compensating an extremely short lifetime.

## Slide 16: What breakthroughs made the MBA possible?
Solving narrow spacing issues
Q1: The MBA lattice naturally requires the large number of focusing quadrupoles to focus the beam at each BM horizontally.
How can numerous magnets be accommodated within a limited space?
Q2: The shorter focal length and smaller energy dispersion increase the strength of both quadrupole and sextupole magnets.
How can extremely strong quadrupole and sextupole fields be achieved?
Notes: Among four critical issues, here we only pick up the narrow space issue. Two main problems are there.

## Slide 17: What breakthroughs made the MBA possible?
A1/A2: Adoption of the compact vacuum chamber w/wo NEG coating
Black: SPring-8 chamber designed 35 years ago
Red: SPring-8-II chamber designed recently
710
466
Bore radius
85 mm
Bore radius
34 mm
Notes: A solution to these problems is to introduce compact vacuum chamber with a small cross-section as shown here. The compact chamber allows to install multi-pole magnets with smaller bore radii. This smaller bore radius enables a smaller magnet size with a higher magnetic field strength. Behind the successful introduction of this compact vacuum chamber, in my assessment, two important achievements are there; establishment of transparent top-up beam injection and precise beam handling using BBF systems.

## Slide 18: What breakthroughs made the MBA possible?
A1/A2: Adoption of a single-yoke composite magnet with a spaghetti-type chamber
M. Johansson et. al., Proc. of NAPAC2016, Chicago, IL, USA (2016) pp. 1058-1066
Notes: Furthermore, as shown in this figure, a technique has been developed whereby different types of electromagnets—such as dipoles, quadrupoles and sextupoles—are integrated into a single magnetic yoke to maximize space efficiency. Of course, intermediate approaches between a discrete magnet system and an integrated single-yoke system are also employed. However, in such cases, significant magnetic field crosstalk occurs, which make system integration difficult and severely limits operational flexibility.

## Slide 19
History of synchrotron radiation source development
Diffraction-limited SR sources
Single-pass free-electron lasers
Future development direction with a few topics
Notes: Next, we move to another recent topic, single-pass FELs.

## Slide 20: Brief history
The development of a single-pass FEL originated from the TTF (TESRA Test Facility), the test-bed for ILC at DESY and 1.3 GHz superconducting RF system was developed. In 2000, First SASE (Self-Amplified Spontaneous Emission) lasing was observed at 109 nm [1]. TTF demonstrated the SESE scheme operating in the short-wavelength region, thereby establishing the foundation for X-ray FELs subsequently constructed worldwide.
[1] J. Andruszkow et. al., PRL 85(18) (2000) 3825-3829
[2] P. Emma et. al., Nat. Photon. 4 (2010) 641-547
In 2009, LCLS (Linac Coherent Light Source) at SLAC achieved first SASE lasing at 0.12 nm using normal conducting S-band linac ( a part of Stanford two-mile linac), out-of-vacuum undulator, RF gun system and so on.
Era of single-pass FEL in short wavelengths was open-up.
Notes: Let’s see the brief history.

## Slide 21: Self-Amplified Spontaneous Emission
Resonant wavelength of
undulator
Electron trajectory
Resonant Wavelength for Undulator
Notes: Resonant wavelength of undulator, in other words, a fundamental wavelength of undulator radiation satisfy the condition that the light of this wavelength overtakes electrons by one wavelength for every one undulation period of electron as shown here.

## Slide 22: Self-Amplified Spontaneous Emission
Light overtakes electrons by one wavelength for every one undulation period
Electron trajectory
Undulator
Acceleration
Deceleration
Light electric field
(transverse wave)
With the light of resonant wavelength, phase of acceleration and deceleration are maintained in the early stage of micro-bunching
Electron trajectory
Energy Modulation with Wavelength Interval
Notes: The vertical alternative magnetic fields along the undulator wiggle electron horizontally and this wiggling causes horizontal velocity components. Through these horizontal velocity components being parallel to light electric fields, electrons can exchange their energy with light of the resonant wavelength.
With the light of resonant wavelength, phase of acceleration and deceleration are maintained for electrons in the early stage of micro-bunching causing micro-bunches to form at intervals corresponding to the resonance wavelength, which in turn enhances the undulator radiation.

## Slide 23: Self-Amplified Spontaneous Emission
Electrons gaining and loosing energy gather towards at the field zero crossing points
Electron trajectory
Undulator
Electron deceleration side
Electron acceleration side
Design energy trajectory
Higher energy trajectory
Lower energy trajectory
Micro-bunching with Wavelength Interval
Notes: Electrons gaining energy from the light relatively advance in phase and Electrons losing energy relatively delay in phase. Finaly electrons gather towards at the field zero crossing points.

## Slide 24: Self-Amplified Spontaneous Emission
Energy exchange with gradually bunching electrons modulates the phase of light
Electron trajectory
Undulator
Peak(Phase) shifted
Electron deceleration side
Electron acceleration side
electric field
Phase Shift of Light Electric Field
Notes: In order to enhance the energy exchange between light and electrons, the converged phase should be moved from zero towards π over 2. As shown in the figure below, the energy exchange with electrons during the micro-bunching process shifts the phase of the light’s electric field due to an imbalance in electron density (bunching). Due to this phase shift, the electron bunches, which initially converge toward the zero-crossing point of the electric field, naturally begin to converge toward the electron deceleration region towards π over 2.

## Slide 25: Self-Amplified Spontaneous Emission
Gain~105
Undulator
E-beam
SASE
Micro-bunching
Energy modulation by
spontaneous
emission
Interaction with a built-up laser field
Log(Gain)
P(z)=P0exp(z/Lg)
Notes: Due to the formation of microbunching and the phase shift of the light electric field, the intensity of the electric field of light increases exponentially, as shown in the figure, and finally generate intense and spatially coherent SASE.

## Slide 26: 1D SASE gain length
The gain lengthrepresents the undulator length enhancing the laser power by a factor of e (approximately 2.7).
,
,
Peak current at the lasing slice
Emittance
at the lasing slice
Averaged beta over
the undulator
Notes: The gain lengthrepresents represents the undulator length enhancing the laser power by a factor of e is scaled by the peak current , inverse of emittance and inverse of transverse beam envelop function at the lasing slice as shown here. In order to shorten the gain length, high peak current, small beam size and small beam emittance are required.
The gain length〖 𝐿〗_𝐺 represents the undulator length enhancing the laser power by a factor of e is scaled by the peak current , emittance at the lasing slice, and transverse beam size as shown here. In order to shorten the gain length, high peak current, small beam size and small beam emittance are required.

## Slide 27: Single-pass FEL system
Electron
Gun
Buncher
Chirp
Lineariser
Multi-stage Bunch Compressor
Main Acceleration
System
Beam Switch
Yard
Undulator
Beamline
Experimental
Hutch
T. Ishikawa et. al., Nat. Photon. 6 (2012) 540-544
Notes: The system providing a highly brilliant electron beam is as following. An electron gun with a buncher generates a low emittance electron beam with a normalized emittance of 0.1 to 1 umrad. Because the initial electron beam density is not so high, the electron beam is compressed downstream by a multi-stage bunch compressor consisting of RF accelerators and magnetic chicanes. To compress linearly the bunch, the RF chirp linearizer, which is typically a third harmonic structure of the main RF frequency, is used to correct the nonlinear chirp upstream of the bunch compressor. The main accelerator system after the bunch compressor accelerates the beam up to the design beam energy. The beam is delivered to the undulator beam line via the beam switch yard and amplifies SASE XFEL.

## Slide 28: High repetition rate XFEL based on superconducting linac (mainstream)
W. Decking et. al., Nat. Photon. 14 (2020) 391-397
Notes: The recent mainstream is a XFEL facility using a superconducting RF acceleration system, enabling a MHz XFEL pulse. Pioneer of this system is TTF and the developed technology has been taken over by its successor of European XFEL in Hamburg, Germany.

## Slide 29: SPring-8 Compact SASE Source (SCSS)
T. Ishikawa et. al., Nat. Photon. 6 (2012) 540-544
Lower Beam Energy
Efficient Acceleration
Size Reduction
Further Size Reduction
Smaller Normalized
Beam Emittance
Short period
in-vacuum
undulator
C-band high
gradient
acceleration
system
Thermionic
gun based
low emittance
injector
Notes: This is a completely different approach to a compact XFEL using a normal conducting C-band accelerators and in-vacuum short period undulators.

## Slide 30: Variety of XFELs
Two-color FEL
Self-seeded FEL
Circular-/liner-polarized FEL
Extremely short-pulsed FEL
Notes: Here, I would like to introduce variety of XFELs. Regarding the short-pulsed FELs, I will explain later as a future research subject for younger generation.

## Slide 31: Two-color XFEL with wide tunability
T. Hara et. al., Nat. Commun. 4 (2013) 2919
K1
K1
K2
K2
Notes: Currently, two-color XFELs are widely available for user experiments. A schematic drawing illustrates a configuration that enables a two-color XFEL with a wide range of adjustable photon energy and timing differences. In this configuration, two undulator sections are separated by an electron beam delay line, which adjusts the timing of the two colors. The two photon energies can be adjusted independently by changing the gap between each undulator.

## Slide 32: Self-seeding with reflective geometry
I. Inoue et. al., Nat. Photon. 13 (2019) 319-322
Notes: In the X-ray wavelength range, we do not have an intense laser system available. Therefore, we usually use a self-seeding scheme in which SASE XFEL is purified into monochromatized laser and then, this monochromatized SASE is back to the electron beam to interacts the beam as a seed laser starting laser amplification. We have two kinds of schemes, reflective and transmission types and this slide shows the reflective geometry type self-seeding scheme.

## Slide 33: Circular-polarization XFEL
M. Suzuki et. al., JSR 21 (2014) 466-472
s-polarization
p-polarization
90 deg phase
difference
at the exit
XPR(X-ray phase retarder)
Notes: Circular-polarized FELs are also available in SX and HX wavelength range. In the SW wavelength range, Circular-polarized FELs are generated with circular polarized undulator. In the X-ray wavelength range, horizontally polarized XFELs are converted to arbitrary polarized XFEL such as a circular-polarization by using a diamond phase retarder as shown here. This system can generate arbitrary polarized XFELs, namely, elliptical polarization, right/left-hand circular polarization, vertical polarization, etc by adjusting retarder phase delay between σ and π polarization.

## Slide 34
History of synchrotron radiation source development
Diffraction-limited SR sources
Single-pass free-electron lasers
Future development direction with a few topics

## Slide 35: Post diffraction limited SR - Longitudinally coherent x-ray generation-
The diffraction limited condition means the X-ray brilliance by undulator radiation is no longer enhanced even when natural emittance is reduced.
To dramatically increase the brilliance, paradigm-shift from “spontaneous radiation” to “longitudinally coherent radiation” is required.
Notes: A big challenge in a ring-based SR source is to develop a scheme generating longitudinally coherent X-rays. This is because we have currently reached the level of diffraction limited condition at X-ray wavelength range and we can not dramatically enhance the brilliance by reducing the beam emittance further.

## Slide 36: Cavity-based FEL in a diffraction-limited SR
Patrick Rauer et. al., Nature 650 (2026) 93-96
The first proof-of principle Experiment was performed at the SASE1 undulator line of the European XFEL. The X-ray cavity consists of two diamond crystals in Bragg reflection working close to backscattering geometry. The elements in the retro-reflector are aligned such that the beam after reflection returns at a distance of 2.67 mm from the incident beam inside the same vacuum pipe. The downstream retro-reflector unit (on the right) is adjustable to tune the cavity length. The electron beam (blue) is injected from the left using a magnetic chicane, and the X-ray pulse (red) is circulating in the cavity, overlapping with electron bunches that pass the undulator at 2.23 MHz.
Notes: Recently, the DESY group achieved epoch-making result by using SASE XFELs with a MHz repitition rate at EuroXFEL. This result showed that a clear evidence of building-up SASE power in the optical cavity consisting of two diamond crystals. Although several challenges remain relating to the performance improvements, this result might be a first step towards at realization of a cavity-based XFEL in the ring.

## Slide 37: Towards brilliant atto-second X-ray generation
A frontier of practical “single” atto-second brilliant X-rays remains.
Tuesday 19th afternoon: “Attsecond FEL Physics” by Agostino Marinelli (SLAC)
Thursday 21st, morning: “Generation of tunable sub-femtosecond XFEL pulses by electron bunch recompression using reverse-energy chirp” by Kenji Yasutome (RIKEN)
Notes: Another big challenge is to generate FEL with a short pulse duration of atto-second, which is quite hot topic now. In this IPAC, two talks will be presented. One is an overview talk by Agostino on atto-second FEL physics. Another by Kenji Yasutome on generation of tunable sub-femtosecond XFEL by extra-compression using reverse energy chirp. Prior to these talks, I will give you a simple overview on approaches to the atto-second FEL generation.

## Slide 38: Towards brilliant atto-second X-ray generation
A frontier of practical “single” atto-second brilliant X-rays remains.
ESASE(Enhanced SASE) scheme
A. Zholents and W. Fawley, PRL 92, 224801 (2004); A. Zholents and G. Penn, PRAB 8, 050704 (2005); A. Zholents, PRAB 8, 040701 (2005); E. Saladi et. al., PRAB 9,050702 (2006); Y. Ding et. al., PRAB 12, 060703 (2009); J. Duris et. al., Nat Photon 14, 30-36 (2020)
Slotted foil scheme
  P. Emma et. al., PRL 92, 074801 (2004); A. Marinelli et. al., APL 111, 151101 (2017)
ESASE seeding scheme T. Tanaka, PRL 110, 084801 (2013)
Hard bunch compression scheme
S. Huang et. al., PRL 119, 154801 (2017); E. Prat et. al., APL Photonics 8, 111302 (2023); E. Prat et. al., PRRes 7, L042060 (2025)
Scheme using a reverse-chirp due to a space charge force
  J. Yan et. al., Nat Photon 18, 1293-1298 (2024)
Scheme using slippage over the undulator T. Tanaka, PRL 114, 044801 (2015)
Notes: Previous research works are roughly divided into these 6 categories. The researches of about 40% are on Enhanced SASE schemes. From now, we will see concept of each scheme.

## Slide 39: ESASE(Enhanced SASE) scheme
A. Zholents, PRAB 8, 040701 (2005).
E=2 GeV
lL= 800 nm, PL= ~6 GW, tL= ~5 fs
E=14.35 GeV
en=1.2 mmrad
sg0/gx=0.8E-4
I0=3.4 kA
lw=16cm
Kw =29 (Bp~2T)
Energy modulation by a high-power short-pulsed laser at the wiggler section
Converting the energy modulation to the density modulation at the chicane with help of R56(bunch compression)
Extracting a sub-femtosecond XFEL pulse from the largest current spike
Energy boosting
from 2 to 14,35 GeV
Compression of
current modulation
Energy modulation
SASE radiator
Notes: This shows schematically the idea of an enhanced SASE scheme. By interacting a high-power short-pulsed laser with an electron beam through the wiggler section, energy modulation is generated. Then, this large energy modulation is converted to the density spike as shown here, generating sub-femtosecond to a few hundred attosecond FEL pulses.

## Slide 40: Slotted foil scheme
P. Emma et. al., PRL 92, 074801 (2004).
Simple scheme
Control the lasing beam slice into a short pulse duration
Low electron charge -> difficult to access high peak power
Reversed taper
Notes: This is a quite simple scheme to cut out electron beam into a sub-femtosecond time slice by using Energy and time correlation as shown here. The weak point is not to provide an intense short pulse.

## Slide 41: ESASE seeding scheme
Generating a seed laser by a undulator radiator
Adjusting seed laser timing to the tail electron peak
Enhancing seed laser intensity
Adjusting the next upstream peak timing to seed laser
T. Tanaka, PRL 110, 084801 (2013).
E=8 GeV
en=0.7 mmrad
sg0/gx=1 E-4
I0=3.5 kA
lL= 800 nm, PL= ~1GW, Dg/sg= ~5
10 periods
lw=18 mm
Kw =2.18
Lu= 5 m
Generating a series of electron density spikes by a
ESASE process with slotted foil
This scheme enables 1) high peak laser power up to several TW and 2) pure single attosecond XFEL pulse
Demerit: too complicated system
Notes: This scheme combines ESASE with slotted foil and seeding schemes to generate high-power atto-second XFEL. However, scheme is complicated as shown here. At first, a series of electron density spikes are generated here by a ESASE process with slotted foil. Then, these density spikes generate a series of seed laser pulses. Next, adjust the seed laser timing to the tail electron by the optical delay and increase seed laser power. Then, by using electron delay line, the enhanced seed laser timing is adjusted to the next upstream density peak as shown here.

## Slide 42: Hard bunch compression scheme
S. Huang et. al., PRL 119, 154801 (2017).
Low charge of 20 pC -> difficult to access high peak power
Nonlinear hard bunch compression -> peaky peak
Shortening XFEL pulse by limiting lasing only at the reverse chirp part by using the undulator reverse taper
Reversed taper
After BC2
L3 exit
DL2 exit
Simulated attosecond XFEL
Notes: This scheme is also simple using a longitudinal space-charge effect. Since the lasing charge is quite limited, the laser peak power is not high enough. The high electron peak current after hard bunch compression at BC2 develops a reverse chirp due to the longitudinal space charge effect in the main energy acceleration process L3 and generates a strong reverse energy chirp at the electron current spike. Only this high peak current with a reverse chirp can contribute to laser amplification under the revers undulator taper condition.

## Slide 43: Scheme using a reverse-chirp due to a space charge force
J. Yan et. al., Nat Photon 18, 1293-1298 (2024).
Self-energy chirp modulation due to SPC -> rather stable operation
Reverse-energy chirped electron bunch compressed using a positive R56 dogleg
Small emittance degradation by bunch compression at higher electron energy
Not optimized dogleg-> difficult accelerator parameter tuning
Normal energy chirp
Reverse energy chirp
Positive R56
Additional bunch compression with positive R56
Notes: This scheme utilize the reverse chirp in the previous scheme for the extra-bunch compression using a positive R56 at the dogleg.

## Slide 44: Scheme counteracting the slippage effect towards “single attosecond pulse”
Invited talk(TUZD1) at IPAC2025 given by T. Tanaka.
Limit of FEL pulse length determined by a period number of “radiator”
How do we generate a shorter-pulsed, single attosecond FEL?
Notes: This is only the scheme potentially generating a single attosecond XFEL pulse so far. To this end, we have to suppress the slippage effect. Even when we introduced a high-power single cycle femtosecond laser in the seeding process, amplified laser is not a single cycle, but N cycle reflecting the period number of radiator.

## Slide 45: Scheme counteracting the slippage effect towards “single attosecond pulse”
Chirped micro-bunching with the separation varied from l1 to l10
Ten period tapered undulator with the slippage changing from l1 to l10
Dramatic pulse shortening effect by the phase cancellation
T. Tanaka, PRL 114, 044801 (2015).
Chirped micro-bunching beam
10 period tapered
undulator
with slippages
of l1, l2, l3…l10
Radiation from #1
Radiation from #1+2
Radiation from #1+2+3
Radiation from #1+2+3+4
Radiation from #1+2+3+4
…..+10
Damped by phase cancellation
Notes: As the duration of the laser pulse decreases, the spectral bandwidth increases. To reproduce this relationship using seeding, we have to introduce a new concept of "spatially chirped micro-bunching". This slide shows that such a chirped microbunching electron beam, when interacting with a suitably tapered undulator, can generate a single cycle FEL radiation.

## Slide 46: Scheme counteracting the slippage effect towards “single attosecond pulse”
T. Tanaka, PRL 114, 044801 (2015).
Generating single cycle
density modulation
Single cycle
seed laser
Generating chirped
radiation seed pulse
Converting chirped
radiation pulse to
chirped micro-bunching
A few cycle short
pulsed radiation
Notes: The system that puts this concept into practice is shown here, but it’s incredibly complex. It would be wonderful if it could be made a bit simpler.