## Slide 1: Advanced Acceleration Techniques and Novel Particle Sources
Edda Gschwendtner, CERN
IPAC’26 Student Tutorials
Deauville, France
17 May 2026

## Slide 2: Advanced Acceleration Techniques and Novel Particle Sources
Tue, 19 May 2026
Wed, 20 May 2026
Thu, 21 May 2026
Talks at IPAC2026, Deauville, France
 Topics on recent results and first applications

## Slide 3: Outline
Introduction to plasma wakefield acceleration
State-of-the-art
Plasma wakefield acceleration applications

## Slide 4
Introduction to plasma wakefield acceleration
State-of-the-art
Plasma wakefield acceleration applications

## Slide 5: Conventional Acceleration Technology
5
E. Gschwendtner, CERN
Very successfully used in all accelerators (hospitals, scientific labs,…) in the last 100 years.
LHC cavity
  (invention of Gustav Ising 1924 and Rolf Wideroe 1927)
Typical gradients:
  LHC: 5 MV/m
  ILC: 35 MV/m
  CLIC: 100 MV/m
In metallic structures, a too high field level leads to break down of surfaces, creating electric discharge. Fields cannot be sustained; structures might be damaged.
Accelerating fields are limited to <100 MV/m
 More than 30000 accelerators worldwide!

## Slide 6: Linear Accelerators
 48 km
CLIC, electron-positron collider with 3 TeV energy
Favorable for acceleration of low mass particles to high energies.
Limitations to linear colliders:
Linear machines accelerate particles in a single pass.
Accelerating cavities
Stanford Linear Collider
50 GeV  3.2 km
The higher the required particle energy, the longer (and more costly) is the accelerator.

## Slide 7: Plasma Wakefield Acceleration
Plasma is already ionized or “broken-down”
Can sustain electric fields up to three orders of magnitude higher gradients.
order of 100 GV/m.
~1000 factor stronger acceleration!
 makes this technology very interesting for reducing the size (and cost) for future linear colliders.

## Slide 8: Plasma Wakefield Acceleration
PLASMA is the 4th state of matter
Quasi-neutrality: the overall charge of a plasma is about zero. Collective effects: Charged particles must be close enough together so that each particle influences many nearby charged particles.
Electrostatic interactions dominate over collisions or ordinary gas kinetics.
Plasma WAKEFIELDS are the fields created by collective motion of plasma particles are called.
ACCELERATION of charged particles when they experience an electric field.
Strength of the acceleration:
‘Accelerating gradient’ : ~MV/m

## Slide 9: How to Create a Plasma Wakefield?
Analogy:
lake  plasma
Boat  particle beam (drive beam)
Surfer  accelerated particle beam (witness beam)
E. Gschwendtner, CERN

## Slide 10: Principle of Plasma Wakefield Acceleration
e-drive bunch
Drive beam:
Laser drive beam  LWFA
Charged particle drive beam  PWFA

## Slide 11: Principle of Plasma Wakefield Acceleration
Drive beam:
Laser drive beam  LWFA
Charged particle drive beam  PWFA
Plasma wave excited by relativistic particle bunch.
Plasma e- are expelled by space charge force.
Plasma e- rush back on axis.
Acceleration physics identical for LWFA, PWFA.
plasma wavelength λpe = mm-scale

## Slide 12: Where to Place the Witness Beam?
Accelerating for e-
Decelerating for e-
Focusing for e-
Defocusing for e-
e-
Longitudinal and transverse wakefields are π/2 out of phase.
 Only ¼ of the electron oscillation length is focusing and accelerating for charged particles!

## Slide 13
Plasma Wakefield, Density Scaling
Drive bunch traveling inside a plasma perturbs the plasma electron distribution.
oscillation with
c
ωpe
2π
λpe
=
 Maximum accelerating gradient increases with increasing plasma density.
  Advantage of PWFA
  LWFA: dephasing: laser group velocity depends on plasma density, is slower than c.
    Electron energy reach is limited by dephasing:  move to lower densities and longer accelerators
    Lower density needs higher laser power.
The plasma oscillation leads to a longitudinal accelerating field:
The maximum accelerating field (wave-breaking field) is:
Example: npe = 1x1018 cm-3  EWB = ~100 GV/m  λpe = ~30 µm
Example: npe = 7x1014 cm-3 (AWAKE)  EWB = 2.5 GV/m  λpe = 1.2 mm
 Plasma electron wavelength decreases with increasing plasma density.

## Slide 14: Linear Theory
When drive beam density is smaller than plasma density (nb << np)  linear theory:
Peak accelerating field in plasma resulting from drive beam with Gaussian distribution:
kpe σz ≈ √2
kpe σr ≤ 1
Wakefield excited by bunch oscillates sinusoidally with frequency determined by plasma density.
Fields excited by electrons and protons/positrons are equal in magnitude but opposite in phase.
The accelerating field is maximized for a value of
 eEz ≈ N/σz2
B.E. Blue 2003
Example: npe = 7x1014 cm-3 (AWAKE), kpe = 5 mm-1  drive beam: σz = 300µm, σr = 200µm
(R. D. Ruth, P. Chen, SLAC-PUB-3906, 1986)

## Slide 15: Linear Theory
Accelerating for e-
Decelerating for e-
Focusing for e-
Defocusing for e-
Linear Theory: Maximum accelerating electric field reached with drive beam of N and σz:
Eacc=
N/(2 x 1010)
(σz / 0.6mm)2
MV
m
110
Examples of accelerating fields for different beam parameters and plasma parameters fields:
N = 3x1010, σz = 20µm, npe= 2x1017 cm-3  Eacc = 15 GV/m
e-
 Driver must be short compared to plasma wavelength, easy for laser and electron bunches.

## Slide 16: Different Regimes, Quality
Linear regime: nbeam << npe
lower wakefields
transverse forces not linear in r
Symmetric for positive and negative witness bunches
Well described by theory
z = s -ct
Ez
Narrow sheaths of excess
plasma electrons
Accelerating
cavity
Typical bubble length scale:
fraction of a mm
Ions only
Blow-out regime: nbeam >> npe
Higher wakefields
transverse forces linear in r (emittance preservation)
High charge witness acceleration possible
Requires more intense drivers
Not ideal for positron acceleration
Reduce energy spread
Sufficient charge in the witness bunch to flatten the accelerating field
Beam loading (Simon van der Meer, 1985)

## Slide 17: Plasma Acts Like a Transformer
 Drive beam deposits energy, witness beam gains energy
driver
witness
Depletion: The drive bunch/pulse running out of energy.
 Solution: couple in a new driver or use a more energetic driver.
driver
witness
Dephasing: The witness bunch outruns the driver.
 Solution: couple in a new driver or change plasma parameters.
driver
witness
Diffraction: (mainly for laser pulses): Drive beam evolution.
 Solution: Guiding.
Acceleration distance (and witness energy) typically limited by one of the
3 Ds

## Slide 18
Introduction to plasma wakefield acceleration
State-of-the-art
Plasma wakefield acceleration applications

## Slide 19: Seminal Paper 1979, T. Tajima, J. Dawson
Use a plasma to convert the transverse space charge force of a beam driver into a longitudinal electrical field in the plasma.

## Slide 20: Electron-Driven, SLAC
85cm Lithium vapour source, 2.7x1017cm-3
 Accelerated electrons from 42 GeV to 85 GeV in 85 cm.
 Reached accelerating gradient of 52 GeV/m
Final Focus Test Beam Facility, FFTB at SLAC
I. Blumenfeld et al, Nature 455, p 741 (2007)

## Slide 21: Laser-Driven, BELLA, Berkeley
BELLA, Berkeley Lab, USA
A. Picksley et al., PRL 133, 255001 (2024)
9.2 GeV in 30 cm of plasma
 30.6 GeV/m
40 J, 30 fs  1.2 PW Focused to σr = 50 μm
Laser guiding

## Slide 22: Quality
Transfer efficiency 42+/-4% with 0.2% energy spread, up to 70% with energy spread increase
C.A. Lindstrøm et al., Phys.Rev.Lett. 126, 014801 (2021)
FLASHForward, DESY
A. Maier et al., Phys. Rev. X 10, 031039 (2020)
Stable 24hr operation
LUX laser plasma accelerator, DESY
Up to 1 MHz repetition rate

## Slide 23: FEL Demonstration
FEL lasing amplification of 100 reached at 27 nm wavelength
Laser Driven based FEL: First demonstration
500 MeV electrons from LWFA
W.T. Wang, K. Feng, et al., Nature, 595, 561 (2021)
Since then several more groups: Soleil/HZDresden, Berkeley
SIOM, Shanghai, China
Electron Driven based FEL: First demonstration
R. Pompili et al., Nature 605, 659-662 (2022)
94 MeV electrons from PWFA, FEL lasing at 830 nm
Sparc-Lab, INFN Frascati, Italy

## Slide 24: State of the Art and Goals towards HEP Collider
 Requires international, multi-dimensional R&D efforts.
ESPP 2020:
Plasma R&D Roadmap
US Snowmass and P5
R&D Efforts

## Slide 25
Introduction to plasma wakefield acceleration
State-of-the-art
Plasma wakefield acceleration applications

## Slide 26: Plasma Wakefield Acceleration Applications
First Applications
Particle physics applications
HEP colliders
O (~5 GeV)
O (~10s GeV)
250 GeV
10 TeV
Light Sources, FEL
Medical applications
National security
Radiation generation
Fixed target experiments
Injector for a synchrotron/collider
Collider components
Test beams
Higgs factories
Energy frontier linear collider (10 TeV)
Short-term
Mid-term
Long-term

## Slide 27: EuPRAXIA
European Plasma Research Accelerator with eXcellence in Applications
Today: 54 institutes in Consortia
Construction has started.
TDR published in Feb 2026.
First FEL user operation in 2031.
Combining X-band linac with beam-driven plasma acceleration.
EuPRAXIA@SparcLAB in Frascati
Site 1: EuPRAXIA FEL in Frascati LNF-INFN (beam-driven)
Site 2: EuPRAXIA FEL (laser-driven) at ELI-ERIC, Czech Republic.
EuPRAXIA is a design and an ESFRI project for a distributed European Research Infrastructure based on novel plasma-acceleration concepts (1-5 GeV), building two plasma-driven Free Electron Lasers, FELs, in Europe.
Aims at offering a significant reduction in size and possible savings in cost over current state-of-the-art RF-based accelerators.
Notes: Parameter (AQUA)
Units
PWFA
Full RF
Electron Energy
GeV
1
1
Repetition Rate
Hz
100
100
Bunch charge
pC
30
200
Peak current
kA
3.3
3.4
RMS bunch length
μm
1.4
16.9
RMS norm.emitt. (x,y)
mm mrad
0.7,0.7
2.1,1.0
Radiation wavelength
nm
4.06
4.06
Photon per pulse
×10¹¹
3.2
31.3
Ph. pulse length (FWHM)
fs
2.33
33.0
Photon bandwidth
%
0.4
0.5

## Slide 28: Plasma Wakefield Acceleration Applications
First Applications
Particle physics applications
HEP colliders
O (~5 GeV)
O (~10s GeV)
250 GeV
10 TeV
Light Sources, FEL
Medical applications
National security
Radiation generation
Fixed target experiments
Injector for a synchrotron/collider
Collider components
Test beams
Higgs factories
Energy frontier linear collider (10 TeV)
Short-term
Mid-term
Long-term

## Slide 29: Towards Higher Energies
Lasers or electron bunch drivers: ~10s of J/bunch
Staging of 2 plasma cells demonstrated at 100MeVs level (laser driven).
Experiments ongoing at GeVs level.
Matching between stages with plasma lenses/conventional magnets.
No beam-driven staging yet demonstrated (no facility).
S. Steinke et al., Nature 530, 190 (2016)
BELLA, Berkeley, LBNL
 Staging

## Slide 30: Towards Higher Energies
Proton bunch driver:
~SPS 19 kJ/bunch, LHC 112 kJ/bunch
 Immediate use of SPS proton bunch for driving strong wakefields!
 Rely on self-modulation of the proton-bunch
 Micro-bunches resonantly drive strong wakefields
~1.2mm
z ~6cm
p bunch
 single plasma cell
With existing proton beams: reach energy frontier with electrons
SPS p+ (450 GeV): accelerate to 200 GeV electrons.
LHC p+ can yield to 3 TeV electrons.

## Slide 31: AWAKE at CERN
E. Gschwendtner, CERN
The only proton driven plasma wakefield acceleration experiment worldwide.
High energy gain possible because the high-energy driver is available today.
Advanced WAKEfield Experiment
Accelerator R&D experiment.
International collaboration with 19 institutes.
Unique facility driving wakefields in plasma with 400 GeV proton bunch from the SPS.
Accelerating externally injected electrons to GeV scale.
AWAKE Collaboration, PRL 122, 054802 (2019)
M. Turner et al. (AWAKE Collab.), PRL 122, 054801 (2019)
AWAKE Collaboration, Nature, 561, 363 (2018)
F. Pannell, UCL
All milestones achieved.
More than 23 high-level publications such as Nature (1), Phys. Rev. Lett. (7), Phys.Rev. E (1), Physics of Plasmas (1), Phys. Rev. A&B (2),…

## Slide 32: First Applications of AWAKE Technology
In AWAKE facility, could conceive of O(50 GeV) electrons.
Requirements on emittance are moderate for first applications.
    First applications to high energy physics for 50 GeV beam:
      Use for collider, e.g. ep collider, which would be like a low-luminosity LHeC.
      Beam-dump experiments to e.g. search for dark photons.
      Interaction with high-power laser to investigate strong-field QED.
Laser intensity →
Beam energy →
High energy, ~50 GeV
Nonlinear Breit–Wheeler
Credit: B. King
Strong-field QED could be the obvious first experiment.
  Can investigate new region with high energy.
  Currently no competitors.
  Only modest laser needed.
  Increasing laser power  probe more phase space.

## Slide 33: PETRA-IV Plasma Injector
4th generation SR source:
PETRA III to PETRA IV upgrade
(6 GeV, 20 pm emittance)
Final decision for PETRA IV in 2026
DESY/Hamburg
PETRA IV Plasma Injector:
Alternative proposal to DESY IV injector
Dedicated injector
PW-drive laser
6 GeV HOFI-guiding assisted laser-plasma accelerator
Active energy compression scheme (X-band)
Demonstrate full technology chain:
injection studies into DESY II ongoing (350 MeV)
A. Martinez de la Ossa et al., PETRA IV Injctor CDR

## Slide 34: Plasma Wakefield Acceleration Applications
First Applications
Particle physics applications
HEP colliders
O (~5 GeV)
O (~10s GeV)
250 GeV
10 TeV
Light Sources, FEL
Medical applications
National security
Radiation generation
Fixed target experiments
Injector for a synchrotron/collider
Collider components
Test beams
Higgs factories
Energy frontier linear collider (10 TeV)
Short-term
Mid-term
Long-term

## Slide 35: Higgs Factory Based on Plasma Wakefields - HALHF
250 GeV c.o.m., asymmetric collisions
  Electrons at 375 GeV accelerated in electron driven plasma wakefields
  Positrons at 42 GeV using conventional RF linacs
Estimated luminosity: ~1 x 1034 cm-2 s-1
Length: 5 km
Technology choice: CLIC (power source) + PWFA (transformer) + cool copper technology (positrons)
PWFA Stages: 48 stages, 1 GV/m gradient, higher driver charge 5x1010 (8nC)
 Several key challenges still to be solved for PWA: staging, repetition rate, plasma temperature, cooling, beam jitter
New Baseline:
B Foster et al 2023 New J. Phys. 25 093037 (2023)
Electron driven plasma wakefield accelerator

## Slide 36
Proton drive bunches from fast cycling synchrotron (HTS magnets) or FFAG to reach competitive luminosity.
Short proton driver (sz =150 µm); density gradient in plasma.
Electron and positron acceleration to very high energy in one single plasma (100s meter).
ALiVE: Advanced Linear collider for Very high Energy
Proton-driven plasma wakefield accelerator
Key challenges: Short (sub-mm) driver, high (kHz) rep rate, positron acceleration in plasma.
Fewer challenges for e−p/e−A collider or asymmetric scheme.
e.g. SPS
Higgs Factory Based on Plasma Wakefields - ALiVE
 These are exploratory studies
Low repetition rate of high-energy proton bunches at CERN  limiting luminosity
ALiVE:
Collision energy: 250 (125 + 125) GeV, with upgrade to TeV range
Estimated luminosity: 1.7 x 1034 cm-2 s-1
J Farmer, A. Caldwell, A. Pukhov, 2024 New J. Phys. 26 113011 (2024)
Electron injector for the EIC based on p+ driven plasma wakefield acceleration
H. Jaworska et al., IPAC2026

## Slide 37: 10 TeV pCM Collider
Laser-plasma LC: C.B.Schroeder et al., 2023, JINST 18 T06001, arXiv:2203.08366
Ongoing design effort: 10 TeV parton-center-of-mass (pCM) collider based on wakefield accelerator (WFA) technology.
Delivery of an end-to-end design concept, including cost scales, with self-consistent parameters throughout.
International effort - working group conveners from the US and Europe are organizing the study, partner with ALEGRO and other R&D efforts.
Collision:
e+e-
e-e-
γγ
Laser-driven
Beam-driven

## Slide 38: Summary
1. Plasma wakefields offer a ~1000 × gradient advantage over conventional RF.
  Allows smaller, potentially cheaper machines.
2. The field is moving from proof-of-principle to first applications.
  Short-term applications at the O(5 GeV) scale – FELs, medical, radiation sources – are within reach now.
  Mid-term particle physics applications (fixed-target experiments, synchrotron injectors) are the next step.
  Concrete collider concepts at the energy frontier (HALHF, ALiVE, 10 TeV pCM) are under active design study.
3. Key R&D challenges remain, and investment is essential.
  Continued support for high-gradient wakefield R&D is needed for this technology to contribute meaningfully to future particle physics programmes.