## Slide 1: Beam Dynamics in ElectroMagnetic Field Very first BASICS
Nicolas PICHOFF
CEA-Saclay
France

## Slide 2: Contents
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 2
Particle representation
Accelerator representation
Beam representation
Longitudinal dynamics
Linear dynamics (6D)
Periodic structures
Matching
Mismatching

## Slide 3: Particle representation
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 3
1’

## Slide 4: Particle definition
(considered as known)
Position :
In 3D-dynamics world, the particle is a dot at :
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 4
A rest mass
and a charge
Motion : change of with respect to an independent variable (time: )
Kinetic energy :
Total energy :
Momentum :
c m/s
Energy :
Momentum :
Velocity :
Velocity :
Reduced
Motion

## Slide 5: Particle Motion (Lorentz)
and are the electromagnetic fields produced by external sources and the particles (position and motion) themselves.
At a given t , a particle is represented by a 6-coordinates vector :
=
With :
The evolution (with independent variable t) of these vectors are given by :
(considered as known)
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 5

## Slide 6: Energy gain
The energy gain is the path integral of the electric field

The energy evolution with time t is :

Only the electric field gives (kinetic) energy to the beam
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 6

## Slide 7: Particle accelerator
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 7
4’

## Slide 8: Acceleration/deviation
Acceleration is produced (generaly) by time varying electric field
Guiding is produced (generaly) by static magnetic field
RF cavities
Plasma
Exception @ low energy : Electrostatic
Deviation with Dipoles
Focalisation with Quadrupoles or Solenoids
Stabilisation with higher-order Multipoles
Exception @ low energy : Electrostatic
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 8
An accelerator is a set of technological components producing ElectroMagnetic fields allowing to accelerate and guide particles.

## Slide 9: Reference trajectory
The beam dynamics is computed along the reference trajectory as a function of the curved abscissa : s, replacing t as the independent variable.
Linac
line
~spiral
Cyclotron
~circle
Synchrotron
- A strait line in drift, focusing or accelerating elements,
- An arc of circle in dipole magnets.
s
s
s
s
An accelerator is designed around a reference trajectory (design orbit in circular accelerators), which is:
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 9

## Slide 10: Synchronous particle
The synchronous particle is an hypothetical particle propagating along the reference trajectory.
It is used to synchronize the time-varying (RF) components.
It represents the accelerator and not the beam.
It gives the nominal arrival time and energy at a given s, by design.
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 10
All the beam particles will be represented with respect to this synchronous particle.

## Slide 11: Moving frame
Particle motion is described in a moving frame, centered on the orthogonal projection of the particle on the reference trajectory.
: tangent to the reference trajectory
: in vertical direction (pointing to the top)
: in rotation plan (pointing to the left)
M is the particle point at time t
s is absissa of the transverse plan, orthogonal to the reference trajectory containing M
In this plan, the particle position is :
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 11
transverse
plan

## Slide 12: Moving frame change
The moving frame depends on s.
is the curvature radius in (x, s) plane of the reference trajectory at position s.
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 12
with :
On a curved trajectory, moving frame vectors are not constant

## Slide 13: Derivative with s
Independent variable : t  s
ds
r=1/h
s-ds/2
s+ds/2
s
l
x
More generally :
If there is bending in (, ) plan with curvature radius:
One has :
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 13
On a curved trajectory, depends also on

## Slide 14: New particle representation
In this new frame and independent variable, a particle vector becomes:
t

IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 14

s


(x, y) are (still) the particle transverse coordinates
-
and
are the particle transverse slopes
-
is the particle phase, the arrival time at normalized wrt a frequency (generaly RF)
-
K is the particle kinetic energy
-

## Slide 15: RF acceleration & Longitudinal dynamics
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 15
9’30

## Slide 16: Longitudinal phase-space
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 16
j
Each beam particle is represented relatively to the synchronous particle
=
=
The longitudinal dynamics describes particle trajectories in 2D phase-space
Energy:
Phase or time:
Late particles
Early particles

## Slide 17: RF cavity
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 17
Goal : Give kinetic energy to the beam
Basic principle
Cavity
- Conductor enclosing a close volume,
- Maxwell equations + Boundary conditions allow possible electromagnetic field En/Bn configurations each oscillating with a given frequency fn : a resonant mode. The field is a weighted superposition of these modes.
The phase of the electric field is adjusted to accelerate the beam.
- The wanted (accelerating) mode is excited at the good frequency and position from a RF power supply through a power coupler,
RF power supply
Wave guide
Power coupler

## Slide 18: Energy gain
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 18
Energy gained by a particle in a cavity :

with :
The cavity effective voltage
The particle effective phase in the cavity
* Sometime (for example linac), one can find :
with :
The field phase when the particle is at position
*

## Slide 19: Energy gain in a multicell cavity
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 19
Field seen by an optimal velocity particle
Cavity Oscillating field
Field seen by a non-optimal velocity particle
Energy gained by the optimal velocity particle
Hypothetical max energy gain :
Energy gained by a non-optimal velocity particle
Energy gain
Electric field

## Slide 20: Relative phase change in drift (no bending)
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 20
First order simplification :


One gets (at first order) :

## Slide 21: Relative energy change in RF cavity
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 21
One gets (at first order) :
is the average phase seen by synchronous particle in each cavity

## Slide 22: Specificity for circular machine
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 22
is the relative variation of revolution frequency with respect to the relative momentum


is the momentum compaction
It is specific to circular machine (0 in linac)
The beam revolution frequency.
Velocity dominated : A higher energy particle turns faster
 linacs and low energy synchrotrons.
Trajectory dominated : A higher energy particle turns slower
 high energy synchrotrons.

## Slide 23: Specificity for circular machine
In cavity, the electric field is oscillating with time :
‼ In some convention, one can have
Case 1: Velocity dominated
0°
180°
90°
late
early
late
The late particle shall gain more energy
(to increase its speed)
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 23
Case 2: Trajectory dominated
0°
180°
90°
late
The early particle shall gain more energy
late
early
(to elongate its trajectory)

## Slide 24: Correction in circular machine
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 24
+
In linac
In general


Replace
by

## Slide 25: Phase-space trajectories
In cavities
In accelerator
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 25
Between cavities
>0
<0

## Slide 26: Longitudinal motion equation
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 26
is the motion Hamiltonian :

## Slide 27: Hamiltonian
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 27
The particle motion can be described using a function of phase and energy: the motion Hamiltonian
iso-Hamiltonan cuves : = Cste
Hamiltonian definition:
The Hamiltonian gives the particle trajectory in phase-space

## Slide 28: Phase-space trajectories
: no acceleration (storage), maximum stability
: acceleration, but reduced stability
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 28

## Slide 29: Linear dynamics
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 29
27’30

## Slide 30: Particle motion in an accelerator
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 30
=
(p. 13)
+
=

## Slide 31: Motion equations
With :
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 31
Centrifugal force
EM force
Acceleration damping

## Slide 32: Linearisation
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 32
These equations are :
Non-linear
Damped
Coupled
In order to solve the particle dynamics, one shall compute (generally numerically) these complex equations.
Nevertheless the computation can by simplified (and understood) by linearising the forces around the synchronous particle and using a “simple” matrix formalism.

## Slide 33: Longitudinal dynamics linearisation
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 33


## Slide 34: Matrix formalism
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 34
Linearised differential motion equations :


6×6 Matrix

## Slide 35: Transfer matrix
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 35
From an abscissa to an abscissa :
is the transfer matrix from to .
Each accelerator element can be modeled (at first order) by a transfer matrix.

## Slide 36: Accelerator matrix
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 36
from to
from to
from to
For an accelerator from an abscissa to an abscissa
component 1
component 2
component n

## Slide 37: Transfer matrix of a drift
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 37
0
L
s
Drift length : L
The drift is a length with no field.
in
out

## Slide 38: Transfer matrix of a magnetic thin length
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 38
=
> 0 : focusing
< 0 : defocusing
A thin length with focal lengths : and
0
s

## Slide 39: Periodic transport
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 39
31’

## Slide 40: Periodic uncoupled focusing
In the highest simplification level, the external force along direction w (x, y or dj) can be considered periodic, linear, uncoupled and undamped over one period :
Giving :
and:
Hill equation :
=
constant,
with:
In the (w, w’) phase-space, the particle is moving on an ellipse of equation :
with :
and
Courant-Snyder parameters
The phase advance of the particle in a lattice is then :
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 40

## Slide 41: Courant-Snyder parameters from matrix
is the lattice phase advance and , and are the Courant-Snyder at :
The 2D (decoupled) transfer matrix of one lattice from to can be written :
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 41

## Slide 42: Example : motion in FODO lattice
Particle trajectory
Particle
Particle ellipse maximum size
Particle ellipse
Phase-space trajectory
Phase-space periodic looks
Foc. Quad. middle
Foc. Drift. middle
Defoc. Drift. middle
Defoc. Quad. middle
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 42
Ellipsis’ shapes are given by courant-Snyder parameters
Period after period, the particle is turning by an angle given by the phase advance (here 72°)

## Slide 43: Beam
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 43
37’30

## Slide 44: Beam distribution
A beam is a set of charged particles
2D projected phase-space distribution
1D projected phase-space evolution
- Each dot is a (macro) particle
- The colour represents the particle density
- Statistics properties can be calculated from these distributions
It is represented by a distribution in 6D phase-space :
is the average number of particles in phase-space cell.
is the total number of particles in the beam
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 44

## Slide 45: Beam statistics simplification
100 mA  = 6 1017 charges/s
1 nC  = 6 109 charges
A beam should be represented by 6 times this huge number of particles.
Moreover, the exact 6D positions of each particle cannot be known precisely
 The beam distribution can be simplified by its momenta
The average value of a quantity , , in the beam is defined by :
can be a number, a vector, a matrix… the average applies to all components of .
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 45

## Slide 46: Beam momenta
, the bunch charge [C] or beam current [C/s]
Order 0 :
, the beam center of mass 6D vector
Order 1 :
 Order 0-2 are the most useful models of the beam
, the beam 6×6 sigma matrix
Order 2 :

IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 46

## Slide 47: RMS and 2D Ellipsis model
RMS sizes
- RMS coupling
RMS emittance
is the equation of an ellipsis fitting the distribution
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 47
are the Twiss parameters of the beam distribution

## Slide 48: Matching
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 48
45’30

## Slide 49: Accelerator vs Beam
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 49
In non-linear forces, particles are moving in 6D phase-space following curves where motion Hamiltonian is (locally) constant
In periodic linearised forces, these curves are oscillating 6D ellipsoids
Accelerator
Beam
A beam can be described by a sigma matrix whose coefficients correspond to a description of a 6D ellipsoid

## Slide 50: Matched beam
The beam is matched to the accelerator when its sigma matrix fits the ellipsoid describing the particle linearised motion.
Phase-space trajectory
Phase-space periodic looks
Matched beam
Bigger input beam
Smaller input beam
Phase-space scanned by the mismatched beams
beam
accelerator
50% mismatched beam
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 50

## Slide 51: Beam matching
The matching is done between sections by changing focusing force with quadrupoles (transverse) and cavities (longitudinal).
Non matched beam
Calculations are made with « envelope codes » where the beam is modelled by its rms dimensions. This type of code calculates automatically the focusing strength that match the beam.
Matched beam
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 51

## Slide 52: Mismatching
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 52
50’

## Slide 53: Non linear force
This phenomenon is known as the tune spread.
When the confinement force is non linear (multipole, longitudinal, space-charge), the particle oscillation period depends on the oscillation amplitude A.
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 53
Particle do not rotate at the same speed in the phase-space : possible filamentation
Linear force
Non linear force

## Slide 54: Emittance growth
Mismatching :
Emittance growth & Halo formation through :
non linear-forces (external or space-charge),
resonance (out of the scope here) of some particle motion with core oscillation.
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 54
Matched beam
Mismatched beam

## Slide 55: Conclusion
Particle representation
IPAC2026 – Deauville, France - Beam Dynamics in EM Fields (1h) - Nicolas Pichoff (CEA-Saclay) 55
Accelerator representation
Beam representation
Longitudinal dynamics
Linear dynamics (6D)
Periodic structures
Matching
A synchronous particle
(Phase, Energy) - Hamiltonian
Matrix formalism
Courant-Snyder periodic parameters
Distribution + momentum (sigma, Twiss)
Twiss = Courant-Snyder parameters
Mismatching
Emittance growth
A 6D vector (position, motion)








54’