## Slide 1: Accelerator Technology and Sustainability
Mike Seidel
Paul Scherrer Institute and EPFL, Switzerland
IPAC’26, Student Tutorials
May 16, 2026
Deauville

## Slide 2
energy related research
use of materials and resources
grid energy consumption
energy procurement
waste management & recycling
water consumption
research infrastructure system efficiency
mobility &
business travel
heating & waste heat recycling
office/lab energy consumption
efficient technologies
Sustainability = Meeting the needs of the present without compromising the ability of future generations.
(one of many debated formulations)
green house gas emissions

## Slide 3: Energy Consumption - Motivation
The world energy consumption has been continuously rising, reaching ca 21 TW today.
As a science community we rather want to contribute to solutions and not be part of the problem.
School Strike for Climate
Wikipedia
Earth
Moon
Tides
example from nature:
the Earth-Moon system dissipates 3.8 TW power from the rotation energy of earth
[Williams, Boggs, 2016]
includes all power uses
Notes: p45: 655EJ: 21TW

## Slide 4: Community Activities on Sustainability
2014-17: EUCARD-2, WP Energy Efficient Accelerator Technologies
https://www.psi.ch/enefficient
2017–21: ARIES, Work Package Efficient Energy Management
https://www.psi.ch/aries-eem
2021–25: I.FAST, Work Package Sustainable Concepts
https://www.psi.ch/scat
2024– : LDG, Sustainability Working Group
https://ldg.web.cern.ch/working-groups/sustainability-assessment-of-accelerators
ICFA panel on sustainable accelerators, chair: Thomas Roser (BNL)
https://icfa.hep.net/icfa-panel-on-sustainable-accelerators-and-colliders/

## Slide 5: Accelerator driven Research Infrastructures (RI)
grid power
primary beam
auxiliary systems
conversion target
undulators/magnets
colliding beam insertion
…
primary beam production
conversion to specific secondary radiation
electrons
protons
ions
X-rays
neutrons, muons, neutrinos
exotic particles
high level goal:
Science output per grid power, per operating/investment cost.
radiation to
experiments
accelerator

## Slide 6: Accelerator Concepts and Technologies [with emphasize on energy efficiency]
Proton Drivers with high intensity applications
Synchrotron Light Sources and FELs
Particle Colliders
Resonators and high Power RF Systems
Accelerator Magnets and Power Supplies
Cryogenic Systems
Component Cooling, Air Conditioning, Vacuum, Instrumentation … and other aux. systems
concepts, RI‘s
technologies

## Slide 7: Efficient Accelerator Technologies

## Slide 8: Accelerator Magnets with Permanent Magnet Material
B = 1.35 T g = -40.6 T/m
Dipole and Quad for SLS2.0, S.Sanfilippo et al (PSI)
permanent magnets:
extremly compact  low emittance lattices
no power consumption
no cooling, thus no heat introduced, no vibrations from cooling loop
field tuning difficult
use of rare earth materials

## Slide 9: Accelerator Magnets with High Temperature Superconductor Coils
magnets with High Temperature Superconductor (HTS) coils:
medium fields for all applications (high fields in block config.)
ReBCO and Bi-2212 materials are studied
no ohmic losses, can replace power hungry large aperture dipoles/quads
cryogen free conduction-cooling possible (no He)
much improved cryogenic efficiency at elevated temperatures (e.g. 4.5K…15K instead 2K)
today expensive materials
field ramping and field quality difficult (wide tapes)
solenoid test magnet, 18T @ 12K
PSI/CHART, B.Auchmann et al

## Slide 10: Efficient RF Power Sources
Example: SSA for Isotope production Cyclotron, 98.5MHz, 12x1kW units, D=93% (90% with regulation overhead)
Uppsala group, WP in I.FAST program
Magnetron, R&D at various groups, =60-80% within reach
e.g. Wang et al, J-Lab, IPAC 2019; A.Dexter, Lancaster U., LINAC-2014; B.Chase, Fermilab, JINST-2015
Klystrons, >70% within reach
e.g. CLIC two stage multi-beam klystron, J.Cai, I.Syratchev, IEEE Trans, 2020
Solid state amplifiers (SSA) at various groups, =60-90% depending of freq.
Example: study 1GHz for CLIC drive beam; 6 cavities, 30 beamlets; 25+140kV; sat=82%
https://indico.cern.ch/event/1407353/
I.FAST efficient RF workshop, July 23-25, 2025, Toledo:

## Slide 11: Technology R&D: Superconducting RF at higher temperature
promising R&D: Nb3Sn coated cavities at Cornell
4.2 vs. 2.0K  efficiency
[M.Liepe, Cornell, IPAC‘19]
S Posen et al 2021 Supercond. Sci. Technol. 34 025007
record cw gradient in Nb3Sn-coated, Eacc = 24 MV/m
Cornell, FERMILAB
 simplicity, cost, efficiency, smaller size
To be published
DESY, Hamburg U.
aim for sustained SRF accelerator technology
10y Goal: >70 MV/m with a Q0 of 1x1010 and at 4K
contact: M.Wenskat, DESY
G. Deyu et al., „Al2O3 coating of Superconducting Niobium Cavities with thermal ALD“, in preparation
SMART recipe leads to a Tc of 15.4 K on Nb-samples coated with 15 / 25 nm of AlN / NbTiN

## Slide 12: Proton Driver Accelerators or: Best attainable Grid-to-Beam efficiency?

## Slide 13: Comparison: Megawatt p-Drivers
Yakovlev, FNAL, invited talk, IPAC 2017
facility | accelerator type | Economy | Energy Reach | Power Reach | operational complexity | grid-to-beam Efficiency
SNS | superconducting linac | -- | ++ | ++ | ++ | 9%
J-PARC | rapid cycling synchrotron | ++ | ++ | - | - | 3%
PSI | isochronous cyclotron | + | -- | + | - | 18%
Workshop: Efficiency of Proton Driver Accelerators, 2016, PSI
https://indico.psi.ch/event/3848/
Megawatt class facilities operating today:
optimized for application, not efficiency
590 MeV, 1.4 MW

## Slide 14: Superconducting Linac : High Efficiency Potential example: PIP-II design of Fermilab
operating regime | avg. RF power | cryogenic power | avg. beam power | grid-to-beam Efficiency
PIP-II pulsed operation | 1.44MW | 1.19MW | 17.6kW | 0.7%
PIP-II CW operation | 9.10MW | 1.83MW | 1.60MW | 15%
PIP-II base parameters:
H-, 800MeV, 2.0mA, part of Fermilab complex
aim: neutrino production (1MW @ 60..120GeV)
CW operation as upgrade path
highest efficiency
[from presentation B.Chase, Y.Yakovlev, 2018]
not efficient in pulsed operation:

## Slide 15: Low Loss Superconducting Resonators
3‘000 church bell
50‘000 Cu resonator
21010 s.c. resonator
1
105
1010
Q0 = quality factor
 e-folding decay and resonance width
high Q resonators, 1.3GHz, 2K, FNAL
[A.Grassellino, A.Romanenko et al, 2013]
example:
Ua = 20MV, (R/Q) = 609, Q0 = 21010, Ib=2mA
Pdissip = 33 W
Pbeam = 40.000 W
dissipated power:
but: cryogenic efficiency!

## Slide 16: Cryogenic Efficiency
best possible coefficient of performance (COP):
Wc = amount of work required to remove heat Qin at cold temperature T
T0 = 293K
T = 2K
Qin
Wc
[S.Claudet et al, CERN 2013]
factor 3!

## Slide 17: Powerflow s.c. Linac – Minimum System Example for a Single Cavity
GRID
AC/DC/RF/guide
RF  0.4 .. 0.6
cryogenics
COP  1000
beam
Pdissip
PRF
power balance:
regime | Ib [mA] | Q0 | RF | Pbeam [kW] | grid-to-beam Efficiency
TDR, CW | 2.0 | 21010 | 0.44 | 40.0 kW | 30%
high Q | 2.0 | 31010 | 0.44 | 40.0 kW | 33%
high current | 4.0 | 31010 | 0.65 | 80.0 kW | 50%
considered:
one 650MHz cavity
Ua = 20MV
l = 1.1m
ignored: cavity detuning, <1, regulation overhead, aux. systems …
extrapolation

## Slide 18: Light Sources

## Slide 19: Synchrotron Light Sources and Free Electron Lasers
GRID
AC/DC/RF/beam
magnets, AC, aux.systems…
radiation for users
unwanted radiation
over the history ring light sources have improved the brilliance by more than 10 orders of magnitude, the last step is made using multi bend achromat lattices and miniaturization using permanent magnets
power consumption of ring light sources is in the range of a few Megawatt and often not a critical factor; however, s.c. FELs might use O(20MW)
the production of tailored radiation – spectral distribution, coherence, ultrashort pulses etc. is in the focus today
possible efficiency measure:
SLS2.0 magnet structure

## Slide 20: Example Swiss Light Source SLS and its Upgrade
More radiated X-ray power for users Less electricity consumption SLS  SLS2.0 Ee- 2.4 GeV  2.7 GeV PSR 310 kW  365 kW Welec/y 24 GWh  17 GWh Key savings: Electromagnets  Permanent magnets Klystrons  Solid state amplifiers standard pumps  modern pumps for cooling
main RF power flow SLS2.0 | 
AC power | 816 kW
DC power | 772 kW
RF power to beam | 488 kW
power to beam | 366 kW
dipole/undulator radiation | 275 kW / 91 kW
95%
63% SSA
75%
-29 %
[M.Jörg, PSI]

## Slide 21: Free Electron Laser
longitudinal,  z², O(30m)
energy loss, E/E
streaked beam, SwissFEL
no lasing lasing
O(10-3)
best demonstrated energy extraction: E/E = 30%
(Ek=65MeV, Laser seeded FEL)
Facility | Technology | Pgrid (typ) | Pbeam (typ) | Photon Power
SwissFEL | n.c., 6 GHz, pulsed |  3.0 MW | 100 W | up to 0.2 W
EXFEL | s.c., 1.3 GHz, pulsed |  10 MW | 40‘000 W | up to 40 W
FEL process
 ?
RF, Linac
Grid Power Consumption
(order of magnitude)
examples: n.c. / s.c.
FEL: P  N2 (coherence length)

## Slide 22: Particle Colliders

## Slide 23: Colliders - Concepts
MuonC
+/-
1
10
100
1000
m [MeV]
e

p
Next generation: high Luminosity, high Energy reach needed
Energy Efficiency: Luminosity per Grid Power
Ring
p/p
Linear
e+/e-
Ring
e+/e-
particle mass impacts synchrotron radiation and beamstrahlung (collision)
 scaling laws and grid power drivers are quite different for the concepts under discussion

## Slide 24: Colliders Types and Power Drivers
MuonC
+/-
Ring
p/p
Linear
e+/e-
Ring
e+/e-
FCC-ee 240GeV:
Pgrid = 273MW
CLIC 380GeV (3.0TeV):
Pgrid = 252MW (589MW)
ILC 250GeV (1TeV):
Pgrid = 111MW (300MW)
FCC-hh 100TeV:
Pgrid = 580MW
MAP 6.0TeV:
Pgrid = 270MW
+ beam recirculation
- synchrotron radiation
+ no synchrotron radiation
- no recirc., small beam needed
power drivers: cryo (ILC) vs RF (CLIC)
+ no Beamstrahlung-Limitation
- inefficient RCS, complexity
+ high energy reach
- SR deposited @50K, cryogenics

## Slide 25: Ring Collider
energy recirculated, thus efficient concept
however, SR losses at higher energies
comment: for LHC burnup dominates beam loss (no SR)
= „decay time of beam energy in number of turns due to SR“
quality factor storage ring:
bending radius
classical particle radius

## Slide 26: FCC-ee – Optimized Lepton Ring Collider
A. Milanese, Efficient twin aperture magnets for the future circular e+/e- collider,
Phys. Rev. Accel. Beams 19, 112401 (2016)
91km
K.Oide at al
Ecm = 240 GeV (H)
Pgrid = 273 MW
Egrid/y = 1.33 TWh
 dominated by RF (compensating SR losses)
similar as CERN total today
conceptual measures:
crab waist scheme (specific luminosity)
4 IP‘s instead 2
maximise bending field fill factor (next talk)
technology measures:
high-efficiency klystrons (HEIKA collaboration)
4.5 K s.c. cavities, high Q (400 MHz Nb/Cu)
twin apertue dipoles (50% savings of bends)
HTS quads and sextupoles, nested combined function magn.

## Slide 27: Overview Lepton Proposals
energy specific luminosity production:

## Slide 28: Ring vs. Linear Collider
Ring Collider
beams circulate
Linear Collider
beams collide once
beam reused
synchrotron radiation dominated
equilibrium beamsize  collision parameters limited
beam used only once
no synchrotron radiation
ambitious collision parameters possible (no ring dynamics)
 | FCC-ee 365GeV | CLIC 380GeV
x [nm] | 39‘000 | 150
y [nm] | 69 | 2
z [m] | 2‘950 | 70
N [109] | 264 | 5,2
fb [kHz] | 118 | 17,6
Pb[MW] | 912 | 2.8

## Slide 29: Combining Linear- and Ring-Collider using the ERL Concept
ERL
power circulates
P
P
acceleration
deceleration
I
I
power recirculated, beam recirc. at low E
benefit from better collission parameters
 high L per grid power, but higher investments & complexity
two ERL proposals published:
1) Circular Energy Recovery Collider
V. Litvinenko, T. Roser, M. Llatas, Physics Letter B 804 (2020) 135394
multi turn ERL, modification FCC-ee
2) Energy Recovery Linear Collider
V.I. Telnov 2021 JINST 16 P12025
twin s.c. linacs, beam recirculation, wiggler damping

## Slide 30: Muon Collider – Efficient at Highest Energies
Muon: E0 = 106 MeV,  = 2.2 s
mass x 200 compared to electrons:
low SR, low beamstrahlung during collisions!
Beamstrahlung in e+/e- collider, mitigation results in limitation of IP beam parameters and flat beams: x>>y

## Slide 31: Energy scaling of the Muon Collider
particle physicists demand a fixed relative energy spread during collisions, across varying collision energies
with given longitudinal emittance the product of bunch length and energy spread is constant across energies
hourglass effect: length of IP waist and bunch length are of same order of magnitude (beta-function at IP)
the beam can be made smaller with increasing energy
thus L/P is increasing with energy*:
* the grid power is assumed roughly proportional to beam power

## Slide 32
other aspects of sustainability - rare earths, critical materials - carbon footprint of components, construction, operation - heat recovery - carbon footprint of tunnel dominates

## Slide 33
Topics:
rare earths: benefits and issues
assessing carbon footprint, env. impact, societal impact …
supply chains and certification
recycling
https://indico.desy.de/event/35655/

## Slide 34: Petra Zapp (IEK-STE), excerpt: Comparison of Wind Generator Types
0,0E+00
5,0E-05
1,0E-04
1,5E-04
2,0E-04
2,5E-04
DFIG
DDSG
BO
magnet
MP
magnet
DDPMSG DDPSMG DDPSMG
MW
magnet
normalized impacts [PE]
aluminum
concrete
permanent magnet
copper
cast iron, steel
stainless steel
plastics & chemicals
transport, energy & waste
A. Schreiber, J. Marx and P. Zapp: Comparative life cycle assessment of electricity generation by different wind turbine types; Journal of Cleaner Production 2019 Vol. 233 Pages 561-572
example of complex assessment: Influence of RE origin (ore type, mining location, specific site conditions) on environmental impacts per 1 kWh electricity generated by 3 MW wind power
DFIG: DDSG:
doubly-fed induction generator direct driven synchronous generator
DDPMSG: electrically excited and direct drive permanent
magnet synchronous generator
Electricity generation by DDPMSG with
magnet produced
(Bayan Obo) has
from
higher
environmental
impacts
permanent Chinese RE normalized compared to
U.S. Mountain Pass (→ 20%)
Mt. Weld (Aus) (→ 33%)

## Slide 35: Critical Materials: Niobium for Superconducting Cavities, B.List, DESY
RRR (Residual Resistivity Ratio) is an indicator of purity
is defined as the ratio of its electrical resistivity at room temp 273 K to its resistivity at cryogenic temperature
RRR>=300 achieved by 6x vacuum remelting
estimate by B.List (DESY):
  Niobium RRR>300, from China: 98kg CO2-e / kg;
  (stainless steel ca 5..7 kg CO2 / kg) -> 10% of total GHG for ILC250 accelerator! -> large impact reduction potential
M. Hörmann, J. Less-Common Met. 139(1988)1 DOI:10.1016/0022-5088(88)90324-4
electron beam melting machine
impurities after n melting cycles
cavities based on thin film superconductor can reduce CO2 footprint (and operate at higher temperature), but technology is not ready for large scale deployment today

## Slide 36: B.Shepherd (STFC): Electromagnet Operation vs. Manufacturing Footprint
Power usage at nominal operating point
  CLARA 1: 385 W
  CLARA 2: 2.01 kW
  FEBE: 3.72 kW
UK electricity carbon intensity 2022: 193 gCO₂e / kWh
(and improving every year!)
Highly dependent on fuel mix:
Sweden 21g; France 102g; USA 432g; Germany 481g; Switzerland 153g (source: Electricity Maps)
Assume operated for 5 years, 250 days per year, 16 hours per day
Total impact of operation (note: cooling not included)
CLARA 1: 1.49 tCO₂e
CLARA 2: 7.76 tCO₂e
FEBE: 14.4 tCO₂e
Much greater than manufacture impact
600
500
400
300
200
100
0
2000
2005
2010
2015
2020
2025
Carbon intensity
[gCO₂e/kWh]
Year
 |  |  | ma
0
2
4
total impact over 5 years [tCO₂e]
6 8 10
12
14
16
CLARA 1
CLARA 2
FEBE
nufacture operation
Ben Shepherd • Electromagnets vs Permanent Magnets • Rare Earth LCA workshop, 6-8 Feb 2023

## Slide 37: Supporting measures to increase sustainability of accelerators
photovoltaic energy production
Option: direct injection of DC power for accelerator systems
heat pumps at MAX-4
[Björn Eldvall / E.ON,
Martin Gierow / Kraftringen]
concept idea
DC injection of PV power
[C.Martins, ESS, I.FAST]
use of waste heat for heating, often limited by low temperature of cooling water
 Use heat pumps to provide higher T at the expense of some additional grid power

## Slide 38: B.List et al: CLIC CO2 Footprint, Tunnel Cross Sections
5
CLIC tunnel (drive beam option), 5.6m diameter
My estimate: 12.4m2 concrete
-> 31 t/m concrete
CLIC tunnel (klystron option), 10m diameter
My estimate: 44.8m2 concrete
-> 112 t/m concrete

## Slide 39: The Future – Fluctuating Energy Sources
courtesy: FRAUNHOFER-INSTITUT FÜR SOLARE ENERGIESYSTEME ISE, Karlsruhe (2020)
residual power
production of power
solar, wind
release from storage
variation: x5!
use of power
industry, traffic etc
energy storage
simulation: April 2050, sustainable energy system, Germany
full collider operation at times of high grid production
reduced operation or standby modes with fast L recovery otherwise

## Slide 40: Summary Particle Accelerators
Grid to Beam
State of the art 20%, up to 50% reachable for s.c. linacs & high beam power; cyclotrons provide solutions for E<1GeV, e.g. ADS systems
Colliders
e+/e- ring collider is a powerful yet simple scheme; advanced efficient schemes include energy recovery collider and muon collider
fluctuating sustainable energy: E management / dynamic operation
 use surplus energy for RIs
Technology
s.c. magnets & high Q cavities are efficient, higher temperature operation (HTS)
efficient RF sources, permanent magnets, heat recovery & photovoltaics
other: water & He consumption, critical materials, managed lifecycle, carbon footprint, energy procurement, advanced energy production