## Slide 1: Applications of accelerators, engagement with industry, technology transfer and outreach
16 May 2026
Sam Posen
IPAC 2026 – Normandy, France

## Slide 2: Introduction
1

## Slide 3: Colliders
Images from CERN, google, nobelprize.org, arXiv:1207.7214v2
The Large Electron-Positron Collider (LEP)
The Large Hadron Collider (LHC)

## Slide 4: Light Sources
Images from LCLS-II and the European XFEL
youtu.be/t7jUZwhZdd0
Notes: Recently there has been significant interest from the X-ray science community in XFELs, such that two major new projects are underway, the European XFEL in Hamburg, Germany, and LCLS-II at Stanford.

## Slide 5: Neutron Sources
Images from Spallation Neutron Source, Oak Ridge National Laboratory and European Spallation Source

## Slide 6: Nuclear Physics
Images from FRIB (Michigan State University), RISP (RAON, Korea), CEBAF (Jefferson National Laboratory, Virginia), Brookhaven National Laboratory, New York)

## Slide 7
Particle accelerator technology is used in many exciting applications beyond accelerator-based science

## Slide 8
Slides from S. Sheehy, U. Melbourne, CERN Accelerator School and P. Buaphad

## Slide 9: Ion Implantation
Eaton HE3 High Energy Implanter, showing the ion beam hitting the 300mm wafer end-station.
Slide from Bo Cui, University of Waterloo

## Slide 10
Slide from P. Buaphad, Chiang Mai University, ISBA24

## Slide 11: Outline
01
Introduction
02
Compact SRF Accelerators
03
Quantum Computing
04
05
Technology Transfer
06
Summary
07
Technology Transfer
08
Some of what we didn’t cover today
09
Summary
“Beyond-the-Standard-Model” Physics with Accelerator Technology

## Slide 12: Compact SRF Accelerators
2

## Slide 13: Advantages of Nb3Sn Cavities: Higher Q0 at High Temperature
Nb3Sn has substantially higher Tc than Nb (18 K vs 9 K)
High Q0 at relatively high temperatures
  Potential for high Q0 > 1010 in ~4.5 K operation in liquid helium
  Potential for replacing cryoplant with cryocoolers
  Even eliminating liquid helium via conduction cooling
Impacts for high duty factor applications, especially small and medium-scale
High Q0 even at 4 K
f = 1.3 GHz
G = 270 Ω
Notes: The other key advantage of Nb3Sn is that […] This means that the cryogenic systems can be simpler and less expensive. […] This is a big deal for small scale applications, as it would significantly reduce the footprint, maintenance, and operator expertise required for the cryoplant. One could even imagine eliminating the liquid helium entirely and using conduction cooling only. …

## Slide 14: Potential Near-Term Applications of Nb3Sn Cavities
S. Kutsaev et al, IEEE Trans. App. Superc. 30, 8, 2020
Y. Morikawa et al, New industrial application beamline for the cERL in KEK, IPAC’19, THPMP012
R.C. Dhuley et al, ﻿Phys. Rev. Accel. Beams. 25, 041601 (2022).
Nb3Sn is a potentially enabling technology for CW accelerator applications that could be realized in the near future:
  Stand-alone cryomodules (e.g. isotope separator, harmonic cavities)
  Turnkey/high MTBF energy recovery linacs (e.g. isotope production, EUV sources)
  Compact high power accelerators (e.g. water treatment)
Cryocoolers
SRF cavity (Quarter-wave resonator)
Liquid helium reservoir
Thermal and magnetic shielding
Notes: And to give you an idea of where this could be impactful, here are some examples of applications where it could be an enabling technology. On the left, stand-alone cryomodules. These would be especially useful in an accelerator facility where a small number of SRF cavities are needed, but either it’s in a location that's far away from an existing cryogenic distribution system, or it’s in a facility without a cryosystem. Examples include isotope separators in radioactive beam facilities and harmonic cavities, for example in light sources. You can read more about this idea in the paper I'm listing below from Radiabeam and Argonne. In the middle, there is a compact high power accelerator concept from Fermilab, aimed at generating 10ish MeV electrons with 100s of kW-scale powers. Ideas for industrial applications to grow into include wastewater treatment, crosslinking of materials, and security applications. And on the right, you can see a compact energy recovery linac, in this case, one that is built at KEK using niobium cavities, but which could also be realized with Nb3Sn to serve applications that want a system that is turnkey with high mean time between failures, such as isotope production for medical applications and extreme UV sources for the semiconductor industry.

## Slide 15: Coating Mechanism: Vapor Diffusion
Sn vapor arrives at surface
Sn diffusion
Nb
Sn Vapor
Heater
Coating chamber in HV furnace
Nb cavity substrate
Sn
Nb3Sn
Ts = Sn source temperature
=~1200 C
Tf = furnace temperature
=~1100 C
Technique development: Saur and Wurm, Die Naturwissenchaften 1962, Hillenbrand et al. IEEE Transactions on Magnetics 1977, Peiniger et al, SRF’88.
Notes: Here is a schematic of the vapor diffusion technique. It starts with a Nb cavity. We make the Nb3Sn as a thin layer on the inner surface. The Sn comes from high purity metal which we evaporate. The process takes place in a high vacuum furnace, which we heat to about 1100 C. The tin source is heated even further, to 1200 C or higher, where it melts and has a reasonably high vapor pressure. The tin vapor comes up and coats the cavity and alloys with it. We try to control the temperature of the tin source and the furnace vs time to control the rates of tin arrival and tin diffusion.

## Slide 16: Electron Beams for Industrial Applications
Current End-use Market Distribution of Electron Beam Industrial Applications
87% of these e-beam processes involve crosslinking, represented by the applications in blue segments
Grdanovska, S., and Cooper, C, “Electron Beam Driven Industrial Chemistries”. Fermi National Accelerator Laboratory, U.S. DOE Office of Science, 2018 https://inspirehep.net/files/ebe712e944f15ba044ed86b93556aa33
Slide courtesy C. Thangaraj, FNAL
High power compact SRF accelerators based on Nb3Sn can open new applications in the near future

## Slide 17: Compact SRF Accelerators – an Emerging Tool for Industrial Applications
Because of Nb3Sn and cryocooler technology, there is an emerging opportunity to build industrial accelerators with:
  The advantages of SRF: high wall-plug efficiency, simultaneous high energy and high duty factor, high power
  But now with: small footprint, turnkey operation, low operating costs
Vacuum vessel
Magnetic shield
4 K cooling link
Cryocoolers
Thermal shield
SRF cavity
RF power
coupler port
e-gun port
e-beam outlet
port
Section view of a FNAL Conduction Cooled SRF Accelerator prototype
Slide courtesy C. Thangaraj, FNAL

## Slide 18: Application: Remediation of Mixed Waste
E-beam can break down:
  Toxic chemicals to allow for safer handling and easier transportation;
  Volatile substances to help prevent build-up of explosive gas mixtures over time;
  Corrosive substances that can breakdown containers and allow leaching.
E-beam treatment can potentially remediate the hazardous component of mixed waste, leaving it only radioactive.
  Could reduce overall cost and regulation, hence, simplify transport.
  Could improve safety of handling mixed waste.
Slide courtesy C. Thangaraj, FNAL

## Slide 19: Remediation of Mixed Waste: Modular system at 100+ kW
System is made up of three primary parts:
Injector (10-25 mA)
Cryomodule (650 MHz, 5-cell)
Beam Delivery System
Beam Delivery System
Cryomodule
Injector
Slide courtesy C. Thangaraj, FNAL

## Slide 20: Application: PFAS Destruction
Persistent: C–F bond energy > 480 kJ/mol → resists thermal, chemical, biological degradation.
Ubiquitous: Detected in > 98 % of U.S. population and global water sources.
Toxic: Associated with immune and developmental effects.
Opportunity: High-energy electrons = direct molecular-bond cleavage → true destruction.
Some popular products that contain PFAS
Known PFAS impact areas in the U.S.
Slide courtesy C. Thangaraj, FNAL

## Slide 21: What are “Forever Chemicals”? – PFAS
these days used synonymously with forever chemicals
per- and polyfluoroalkyl substances
  de facto (long) chains of C atoms, many F’s & a functional group
recent proposed drinking water restrictions by EPA (US)
  PFOA, PFOS, PFNA, PFHxS, PFBS, HFPO-DA (GenX)
  proposed limits basically as low as detection limits
big challenge for wastewater treatment plants
  current approach often filter & concentrate (GAC) deal with filter (incinerate …?)
  cost & energy intensive
©HBO
https://www.youtube.com/watch?v=9W74aeuqsiU
Slide courtesy J. Vennekate, JLab

## Slide 22: How does ebeam treatment of water work?
don’t attack contaminants directly
  “activate” water with beam
create oxidants and reductants (not just any, some of the strongest)
those react with contaminants
big benefit no addition of further chemicals required
very cost-effective generation of free radicals
And no, we don’t (radio)activate your water!
  stay below 10 MeV neutron activation threshold
  Yet, public acceptance oft an issue – “treatment” vs “irradiation”
e-
©Fox Broadcasting Company
Slide courtesy J. Vennekate, JLab

## Slide 23: Low Frequency Cavity – 650 MHz Single Cell
~1 W dissipation at 10 MV/m, 4.4 K
e.g. Cryomech PT420 has cooling capacity of 2.0 W at 4.2 K
Multipacting (limitation that was overcome during testing)
650 MHz cavity B9AS-AES-002
Notes: What I showed you on the previous slide was a 1.3 GHz single cell cavity. A second type of cavity that we’ve been working on is a lower frequency 650 MHz single cell cavity. Actually this the cavity shape used in PIP-II, but this also would be useful in other applications where you want a big aperture, like low energy high power industrial accelerators. This slide shows an example of a 650 MHz cavity that we coated with a shiny surface. It too exceeded 18 MV/m, reaching as high as 20 MV/m. And on the way, we encountered multipacting, this time without quenching. We again were successful in processing. We measured the curve at 4.4 K and at 2 K. And I’ve added heat dissipation curves in black. Even at the maximum gradient, the cavity is only dissipating about 10 W at 4.4 K. And it gets really interesting if you look at the dissipation at about 10 MV/m. There the dissipation is only about 1.1 Watts. Compare that to the capacity of a cryocooler, for example this PT420 cryocooler can remove 2 watts of heat at 4.2 K. So it really looks feasible to operate a cavity like this one at 10 MV/m accelerating field or higher using only cryocooler based cooling. And with multiple cryocoolers, you could cool a multicell cavity with performance like this.

## Slide 24: Cryocooler-Based Cooling
Nb3Sn-coated 650 MHz single cell cavity reaches gradient ~10 MV/m with a single cryocooler
No liquid helium – conduction cooling only
High purity aluminum cooling links between cavity and cryocooler
Nb3Sn-coated cavity with welded Nb rings for attaching cooling links
R. Dhuley
Notes: So along these lines of thinking, we actually coated another cavity very similar the one I just showed you, except this one had niobium rings welded to it during manufacturing. You can see the Q curves in vertical test at 4.4 K in the plot on the bottom right. After we coated and tested this cavity, Ram Dhuley’s team in Fermilab’s IARC set up a cryocooler-based conduction cooling experiment for it, using high purity aluminum links between the cavity and the cryocooler. The cavity reached gradients as high as 6 MV/m running on a single cryocooler in the first test, and we managed to get up to 10 MV/m after some improvements.
//30

## Slide 25: Jlab+GA Cryomodule Demonstration
Different approach, using thick copper coating on outside of Nb cavity instead of welded Nb rings
G. Ciovati et al., arXiv: 2302.07201 (2023)

## Slide 26: Status and Next Steps
Recent demonstrations include high performance practical multicell cavities and low beta geometries, beam operation with Nb3Sn
Soon, expect first demonstrations where compact SRF accelerators provide advantage – making possible applications that didn’t exist before
Engineering challenges, not fundamental science problems

## Slide 27: Quantum Computing
3

## Slide 28
“Nature isn't classical, dammit, and if you want to make a simulation of nature, you'd better make it quantum mechanical, and by golly it's a wonderful problem, because it doesn't look so easy”
Slide courtesy A. Grassellino, FNAL

## Slide 29
Growing field of science and technology, combining and drawing on the disciplines of physics, mathematics, computer science, and engineering
Its aim is to understand how certain fundamental laws of quantum physics – superposition, entanglement - can be harnessed to dramatically improve the acquisition, transmission, and processing of information
The exciting scientific opportunities offered by QIS are attracting the interest of a growing community of scientists and technologists, and are promoting unprecedented interactions across traditional disciplinary boundaries
Quantum Information Science
Slide courtesy A. Grassellino, FNAL

## Slide 30
The world is excited about Quantum
Slide courtesy A. Grassellino, FNAL

## Slide 31: Quantum Efforts Worldwide 2025
Slide courtesy A. Grassellino, FNAL

## Slide 32
Classical Computer
Supercomputer
Quantum Computer
Classical Computer vs Quantum Computer
Slide courtesy A. Grassellino, FNAL

## Slide 33
Slide courtesy A. Grassellino, FNAL

## Slide 34
The first vacuum tube computer, ENIAC, was developed by US army to calculate artillery firing tables in 1945
The First Classical Computers
Slide courtesy A. Grassellino, FNAL

## Slide 35
Evolution of the Classical Computer
Slide courtesy A. Grassellino, FNAL

## Slide 36
Exponential speed advantage for certain applications – minutes vs millions of years!
3 bits vs 3 qubits:
010 vs a|000> + b|001> + c|010> + d|011> + e|100> + f|101> + g|110> + h|111>
300 bits vs 300 qubits:
010001010110101001001110100010100101110100101001001010100100000001010111101001010100101010101110100101010010010100101011101001010101010010010101001010101110100100100101001010101001001010010100100101000001001010100101000101010110101001000100100010000100010101111010100100101001011010010100100101010111
2300 = 2x1090
vs
More than the estimated 10⁷⁸ to 1082 atoms in the observable universe!
Physically impossible to simulate with classical computers
Exponential Computational Advantage
Slide courtesy A. Grassellino, FNAL

## Slide 37
In 1994 Peter Shor showed that factorization of a product of large prime numbers can be done on a quantum computer exponentially faster than a classical computer
This will eventually be the doom of RSA encryption – expect quantum encryption to grow in the future
Shor’s Algorithm
Slide courtesy A. Grassellino, FNAL

## Slide 38
Basic Requirements for a Quantum Computer
Quantum two level systems
0
1
Couple multiple qubits
Create arbitrary states
Measure quantum states
Scalable architecture
Slide courtesy A. Grassellino, FNAL

## Slide 39
Challenges: Decoherence
Noise
Relaxation ()
Decoherence
Incoherent mix of and
Dephasing ()
Slide courtesy A. Grassellino, FNAL

## Slide 40: Qubit challenges
Need a qubit that you can manipulate and not confuse with other possible states of the system
Maintain the quantum coherence of superpositions long enough to perform a large number of gate operations
Slide courtesy A. Grassellino, FNAL

## Slide 41
Different Platforms
phys.org
Quantum dots
NV centers
sciencemag.org
NMR
chemie.tu
Neutral atoms
NIST
Superconducting circuits
Trapped ions
phys.org
laserfocusworld.com
SQMS
Photonic crystals
Slide courtesy A. Grassellino, FNAL

## Slide 42: SRF Cavity in Liquid Helium
Can this be the basis for a qubit?

## Slide 43: SRF Cavity in Liquid Helium
Can this be the basis for a qubit?
Well, there’s a problem – the cavity might seem cold at 4 K or 2 K, but it’s still teeming with thermal photons

## Slide 44
Photos from: Wikipedia, freefoodphotos.com
T ~ 400 C
T = 20 C
T ~ 77 K
~ 6x103
T = 20 mK
T = 2 K
~ 0.1
~ 41
~ 2x103
~ 1x104
How many photons of added thermal noise at f = 1 GHz?

## Slide 45: SRF Cavity in Liquid Helium Dilution Refrigerator
Are our SRF-based qubits protected from thermal photons in a dilution refrigerator at 20 mK?

## Slide 46: SRF Cavity in Liquid Helium Dilution Refrigerator
Are our SRF-based qubits protected from thermal photons in a dilution refrigerator at 20 mK?
We still need to be very careful – for example, the RF input lines can be low impedance connection to room temperature that can transport thermal photons into our nice cold cavity

## Slide 47: SRF Cavity in Liquid Helium Dilution Refrigerator
Are our SRF-based qubits protected from thermal photons in a dilution refrigerator at 20 mK?
We still need to be very careful – for example, the RF input lines can be low impedance connection to room temperature that can transport thermal photons into our nice cold cavity
Cold attenuators on the input line will help block thermal photon
We can increase the input power to still have a strong signal at the cavity even with the attenuation

## Slide 48: SRF Cavity in Liquid Helium Dilution Refrigerator
We also have to be careful with the transmitted power line
If we send a few photons to room temperature, they’ll get washed out by thermal photons
Cold amplifiers will raise the transmitted power signal above the thermal background

## Slide 49: Nonlinearity
We still don’t have a qubit yet
Need to distinguish different quantum states
E.g. having 0, 1, or 2 photons in the cavity looks really similar to our diagnostics
Slide courtesy A. Grassellino, FNAL

## Slide 50: Nonlinearity
Now let’s add a nonlinear element: a Josephson junction! (aka JJ)
Frequency of readout mode is now dependent photons in storage mode
Even better: it’s a quantum non-demolition (QND) measurement
Can use multiple modes as multiple qubits, and entangle their states
| 0 ＞
| 1 ＞
| 2 ＞
B. Vlastikas, Science, Vol 342, Iss 6158, pp. 607-610 (2013).

## Slide 51: Scaling up…
What could a large-scale quantum computer implementation look like?
Example of 2D architecture - IBM
Example of 3D architecture – SQMS Center @ Fermilab
Slide courtesy A. Grassellino, FNAL

## Slide 52
Quantum Information Science
Quantum Sensing & Metrology
Quantum Computing
Quantum Cryptography
Quantum Communication
Quantum Simulation
Superconducting materials and RF cavities Cryogenics
Electronics and Microwave Controls
Precision Timing
…
ħ
ħ
Leveraging accelerator technologies
for advancing quantum information science
Slide courtesy A. Grassellino, FNAL

## Slide 53: “Beyond-the-Standard-Model” Physics with Accelerator Technology
4

## Slide 54: Searching for Tiny Signals with RF Cavities
We’ve done a lot of work relevant to studying tiny signals
  Suppressed thermal photons, achieved high Q at mK temperatures and small photon numbers, developed quantum tools for studying single photon signals
It turns out that this is useful for more than just quantum computing
High energy physics wants this type of thing for detectors
That’s right! RF cavities have long been a means of accelerating particles so that people with detectors can do science with the beams – but we can use the cavities themselves as high sensitivity detectors
What high energy physics motivation is there to look for small microwave signals?
Image from: BestClipArt

## Slide 55: Searching for Tiny Signals with RF Cavities
The Standard Model of Physics describes our best understanding of the universe based on experimental evidence (e.g. from colliders)
Beyond-the-standard-model (BSM) physics theories address questions not addressed by the Standard Model, like what is the origin of dark matter, and why is there so much more matter than antimatter in the universe?
Theorists have developed a number of ideas for BSM physics that would result in a signal that is detectable but still small enough that it wouldn’t have yet been observed
Image from: BestClipArt

## Slide 56: Searching for Tiny Signals with RF Cavities
Theories of BSM physics are designed to solve key problems (they aim to be “well-motivated”) but there is so little information to base theories on that many possibilities can fit the data
BSM theories sometimes involve many orders of magnitude of parameter space to search through (e.g. axions)
High value experiments in BSM physics exclude a wide range of parameter space with high sensitivity (they “search wide and deep”)
Exclusion is a good result! Don’t expect to find something, and in fact expect NOT to! If you see something, your first instinct should be that it’s probably a false signal
Image from: triz.co.uk

## Slide 57: Quantum Sensing: new windows into fundamental physics
Dark Matter
Gravitational Waves
Precision Measurements
Quantum Physics
Quantum devices are extremely sensitive to small effects – sensors!
New ways to search for dark matter?
Searches for new BSM particles?
Precision tests of the SM or of QM?
New ways to look for gravitational waves?

## Slide 58: Conversion of Axion in Magnetic Field to Microwave Photon
Axion haloscope: axion converts to photon in magnetic field; if cavity frequency matches axion mass it can detect it
Sensitivity improves with higher magnetic field, higher cavity Q0
  Need a multi-tesla magnetic field and cavity that maintains high Q0 in magnetic field
Multi-Tesla Magnetic field
Dark Matter Axion
Notes: To understand why these are important goals, we can quickly review the axion haloscope. This device consists of a microwave cavity immersed in a large magnetic field. The idea is that in the large magnetic field, an axion can convert to a microwave photon, and if the cavity frequency is matched to that of the photon produced, it can be detected. The sensitivity of this device improves with higher magnetic field and higher Q for the cavity. So for maximum sensitivity, we want a cavity that maintains high Q in a multi-tesla magnetic field. So far people have been using copper cavities for these haloscopes. But we think that we can do better with superconducting cavities. Very much fitting with the themes of our center, we think that we have a really good opportunity to use our advanced materials to generate a transformational improvement in this physics and sensing tool.

## Slide 59: Current State of the Art Axion Searches
Operating haloscopes like ADMX (axion dark matter experiment) use normal conducting cavities (e.g. copper)
They have reached desired exclusion limit for a small range of masses, but a very wide mass range remains
Scan rate scales as dν/dt ∝ B4V2Q/2Tsys
  B (magnetic field), V (cavity volume), Q (cavity quality factor), Tsys (system noise temperature)
Q improvement is promising path to improving rate of scanning substantially
Superconductors with very high upper critical field can help (e.g. Nb3Sn, REBCO)
Copper cavity
8 T magnet
Dilution fridge
From ADMX
https://arxiv.org/pdf/1405.3685.pdf & https://indico.cern.ch/event/606690/contributions/ 2655459/attachments/1498473/2332791/Axion_Overview_TAUP_2017_Final.pdf

## Slide 60: Exclusion Plot for the Axion
https://cerncourier.com/introducing-the-axion/

## Slide 61: New Cavities built and deployed as novel physics tools at Fermilab SQMS
SHADE (Superconducting Heterodyne Axion Dark matter Experiment)
SERAPH Plunger Cavity
Dark photon dark matter search
MAGO – built by INFN
Gravitational Wave Search
Nb3Sn B-field cavity
Axion dark matter studies
Slide courtesy B. Giaccone, FNAL

## Slide 62: Technology Transfer
5

## Slide 63: Technology Transfer
What is Technology Transfer?
  Technology transfer moves innovations from research labs to vendors, which can lead to commercial and societal benefits
Intellectual Property (IP) Protection
  IP products include patents, copyrights, and trademarks. These protect inventions developed in research institutions. If you invent something exciting, consider your IP options.
Licensing Agreements
  An inventor can license IP to a company, which defines terms for their use of the IP, including specifications for rights, royalties, and milestones.
Institutional Support
  Your institution may have a dedicated office to guide patent filings and licensing to foster IP protection and partnerships with industry
Image from https://proceedings.jacow.org/SRF2003/papers/mop37.pdf
Example: Cornell University’s 500 MHz cavity licensed to Accel/RI, installed in Taiwan Light Source, Canadian Light Source, and more

## Slide 64: Summary
6

## Slide 65: Final Notes
There are brilliant and wonderful vendors here at IPAC that support accelerators at all our labs – vacuum, RF, magnets instrumentation, and a million other technologies – go visit the vendors around the conference – they will happily give you swag and chat with you about careers in the accelerator industry
There are exciting and relatively new startups in large-accelerator-based industrial applications (semiconductor lithography, isotopes, subcritical reactors) – keep an eye on these – potential to grow in the coming years

## Slide 66: Summary
What are some exciting uses of particle accelerator technology other than accelerator-based science?
Existing
  Industrial accelerators for medical applications
  Industrial accelerators for ion implantation and cross-linking polymers
  Many more
Emerging
  Industrial accelerators for treating mixed low-level radioactive waste, PFAS
  Quantum computing, sensing for fundamental physics
  Many more
If these are interesting topics to you, consider seeking opportunities in universities, labs, & industry!