## Slide 1
Hosting institutions

## Slide 2
Overview of history and types of accelerators
Na Wang
Institute of High Energy Physics, CAS, China

## Slide 3
Acknowledgements
Referred to many reports or articles of others.
Courtesy of Y. Zhang, Y. Jiao, H.X. Xu, Q. Qin, Z. Duan, J. Peng, etc. for helping prepare the slides.

## Slide 4
What is an accelerator?
+
+
+
Protons
Electrons
Atoms (like gold or uranium)
…
    
    
    
    
Linac
Synchrotron
Cyclotron
…
+
+
+
…
stationary target
Colliding with another high speed beam
Producing synchrotron radiations
Electric field
Magnetic field

## Slide 5
Why accelerators?
Verify and improve the Standard Model
Huge microscopes for particle physics
(Study smallest constituents of matter and basic forces governing the behavior)
SSRF
Material Research
(Photon Sources/Neutron Sources
Chemistry, biology, medicine…)
CSNS
Industrial and medical applications
Varian medical systems
Container Scanning Machine

## Slide 6
How did everything begins?
Ernest Rutherford
The father of nuclear science
Rutherford atomic model
“I have long hoped for a source of positive particles more energetic than those emitted from natural radioactive substances”
Starts the race to build accelerators of ever increasing energy, as well as ever higher beam current
Reporting to the Royal Society in London:
Nobel price, 1908
Before accelerators, experiments on subatomic particles were largely based on natural radioactive sources and cosmic rays.

## Slide 7
Different types of accelerators
Also many other fancy accelerators not included.
Livingston plot
Originally produced by M. Stanley Livingston in 1954
Electrostatic Accelerators
Betatrons
Cyclotrons
Linear accelerators
Synchrotrons
Colliders

## Slide 8
Electrostatic Accelerators
Static voltage accelerator
Simple concept is using electric field to increase the speed of a charged particle
Energy gain of an elementary charge: 1eV=e*1Volt

## Slide 9
Early Electrostatic Accelerators
In the 1930s, Cockcroft, Walton and Graaff pushed this simple idea to high voltages.
Cockcroft-Walton accelerator
Single passage: 160~700keV
Based on the idea of voltage multiplying column.
Normal alternating current was first rectified
Apply the current to a number of condensers
Connect the condensers in series
Connect to an accelerating column
Accelerate particles

## Slide 10
Early Electrostatic Accelerators
Van de Graaff generator
Tandem Van de Graaff generator
(clever idea to use the voltage twice)
Cheap and clean.
Energy limited due to voltage breakdown, less used in modern particle physics experiments.
Continue to provide a useful source of low energy particles, applied to a wide range of scientific and industrial tasks.
Charge sprayed on a moving belt
Transported to a upper terminal and removed
Build up voltage on the terminal
Apply to an accelerating column
Accelerate particles

## Slide 11
Oscillating field accelerators
~ V sint

Linear accelerators
- Repetitive acceleration in a straight line
cyclotrons
Synchrotrons
Repeatedly pass through an accelerating structure
Less space for acceleration
Need bending magnet
Loss energy by SR
Applying smaller voltages that oscillate in direction

## Slide 12
Cyclotrons
Ernest Orlando Lawrence
Inventor of the cyclotron
Nobel prize, 1939
E. Lawrence’s 1934 patent
Constant magnetic field, alternating voltage, increasing particle orbit radius
Constant revolution frequency  particles in time with the accelerating voltage
Compact design, huge dipole, low energy
Centripetal force
Lorentz force
First circular accelerators
Work for particles whose velocity was much less than c

## Slide 13
Classical Cyclotron
Milton Stanley Livingston
Constructed the cyclotron
First 4-inch cyclotron, 80keV protons
A number of cyclotrons of increasing size followed.
Relativistic limitation: As velocity increases, the protons began to feel the effect of relativity the revolution frequency varies and couldn't match the accelerating frequency anymore
Not a easy task to built a real machine.
By the end of 1930, Milton Livingston constructed the first cyclotron.

## Slide 14
Synchro-Cyclotron (Phase focusing)
Interrupt steady stream of particles into bunches.
Accelerating frequency decreases with the beam revolution frequency  keep the particles in synchronism with the RF by “phase focusing”
t
eV
eVs
Synchronous particle
Gets more energy
Gets less energy
Important concept also for synchrotrons and linacs
Allow cyclotrons to overcome the relativistic limitation and accelerate to much higher energies.
Proposed by Ed McMillan and V. Veksler independently in 1940s.

## Slide 15
Modern cyclotrons
Spiral sector cyclotrons for nuclear physics
  With separated magnets and resonators
  Introduce additional focusing with alternating contribution at entry and exit of the sector fields.
  Raise the average magnetic field with .
TRIUMF
PSI Ring
88-inch cyclotron at LBNL

## Slide 16
Other applications
Cancer therapy
IBA S2C2
Compact cyclotrons for isotope production or dating purpose
Synchro-cyclotrons for medical applications
PET Cyclotron and Radiopharmacy Facility

## Slide 17
Linear accelerators (Linacs)
In 1924, Gustav Ising proposed the linac idea
In 1928, Rolf Wideroe demonstrated RF acceleration for the first time with radio frequency oscillator limited by the low frequency radio transmitters
Avoided the breakdown problems of electrostatic machines and opened the door to all modern accelerators
A drawing from Ising’s paper in 1924
Particles passing through a sequence of cylindrical metal “drift tube”, hosted in a vacuum tube of nonconducting material.
Energy gain with a rather modest voltage.
n gaps: the particle reaches an energy of neV.
Pulses vs. oscillating voltages with one powered drift tube
Condition for Synchronicity:

## Slide 18
Proton Linac
Lius W. Alvarez
Constructed the first proton linac – a 32-MeV drift tube linac (DTL)
DTL (Alvarez structure 1945)
A new linear accelerator by using the powerful high frequency radio sources developed for radar.
Drift tubes suspended in a copper cylinder – a kind of waveguide.
The length of the tubes was chosen so that the particles arrive at each gap just right and gain energy from the oscillating electric field between the tubes.
Many proton linacs constructed in the years followed Alarez’s work.
Today still serve as the first stage in many accelerator complexes.
Limited by energy due to length and single pass.

## Slide 19
Radio Frequency Quadrupole (RFQ)
Invented in 1970 by I.M. Kapchinskii and V.A. Teplyakov and promoted by Los Alamos.
With four-vaned with appropriately spaced radial modulations, instead of drift tubes.
Focuses, bunches and accelerates the beam at the same time.
Fine periodicity specially suited to low-velocity, high current beams (keV~ MeV).
Soon replaced the large electrostatic injectors of synchrotrons.
CSNS RFQ accelerate the proton from 50 keV to 3 MeV
Excited in an electrical quadrupole mode
Natural transverse focusing
Bunching and acceleration from radial van modulation

## Slide 20
Story begins with klystron
Klystron, invented in 1937, high frequency power tubes (GHz range) available, and linacs for relativistic particles became feasible.
frequency 200 MHz (radar)  1~3 GHz (klystron)
wavelength 1.5m  30 cm~10 cm
Practical electron linacs were first developed at Stanford University.
A WW2 3 GHz klystron
Sketch of SLAC 3 m section
Distance travel in one cycle barely change.
Conducting tube with periodic diaphragms with central holes – fulfill the function of drift tubes of Alvarez structure.
Washers ensure ccelerating wave in phase with the particles.

## Slide 21
Circular accelerator accelerate electrons.
Rising magnetic field serve for both acceleration and bending.
With constant obit radius.
Insensitive to relativistic effects.
Robust and simple.
First circular machines to have a rising field in step with the rising energy.
Betatrons
Cyclotron was for heavy particles but not work with electrons due to the relativistic effect.
At early times, electrons are not very interesting for physics, and mainly used to produce X-rays with energy of hundred keV (within the range of electrostatic generator).
Later needs for intense, higher energy electron beams to treat tumors  Betatrons
Magnet
Electrons
Vacuum chamber

## Slide 22
In 1940, Donald William Kerst operated the first successful betatron.
The popularity was shortly lived in 1940s, in the energy range 5MeV~300MeV, soon replaced by the more compact and less expensive synchrotrons and linacs.
Widely used for medicine applications in the early days.
Nowadays, mainly used for portable x-ray sources up to 6 MeV.
First betatron of Danald Kerst, 1940.
Development of Betatrons
Compact betatrons to produce X-rays for defect detection

## Slide 23
Synchrotrons
For cyclotrons and betatrons, their size and cost grew with their output energy.
Solution:
  Use only the outer rim of the magnet for all energies
  Particles injected into the machine in pulses
  Keep the radius constant and to ramp B to match the momentum of beam
  Synchronize both the rise in field and the accelerating frequency
Beam momentum
Bending magnetic field
Bending radius
Suitable for hadron and lepton
Large size, small magnets
High energy
Fixed target
Paved the way to colliders

## Slide 24
Early history of Synchrotrons
1943: Marcus Oliphant proposed the idea:
“Particles should be constrained to move in a circle of constant radius thus enabling the use of an annular ring of magnetic field … which would be varied in such a way that the radius of curvature remains constant as the particles gain energy through successive accelerations by an alternating electric field applied between coaxial hollow electrodes.”
1947: Frank Goward converted the Betatron into the first “proof of principle” synchrotron.
The first purpose-built synchrotron was built one or two month later - first to produce synchrotron radiation in a visible form.

## Slide 25
Early Proton Synchrotrons
Oliphant’s machine reached just short of 1 GeV for the first time in 1953.
A few month later, Cosmotron at Brookhaven reached 3 GeV.
Closely followed Bevatron at Berkeley reached 6 GeV (found the antiproton).
Cosmotron, BNL
3GeV, 1953
Bevatron, Berkeley
6 GeV, 1954

## Slide 26
Wake focusing  Strong focusing
1952, Stan Livingston proposed the idea of alternating the yokes of the Cosmotron.
Later, Courant, Livingston and Snyder published the Alternating Gradient focusing idea.
Then it was found that the strong focusing scheme had actually been patented earlier by Nick Christofilos.
Nicholas Christofilos
More compact  lower cost

## Slide 27
Strong focusing Synchrotrons
1950s, ~30GeV
CERN’s PS
Brookhaven’s AGS
1970s, ~500 GeV, separate function of quad & dipole squeeze more bending power
CERN’s SPS
Fermilab
1980s, Tevatron, 1 TeV, superconducting higher magnetic field

## Slide 28
Find the new particle by firing one beam at another.
Measure its property and test the validity of the theory.
Colliders – Science motivation
Particle physicists
Theorists
Experimenters
Seek mathematical descriptions of elementary particles and the interaction forces governing them.
Often predict a new particle as the model improves.
New particle discovered 
Nothing found 
(missed from analysis? not exist? energy not equate?)
Build a new machine with high enough energy!
Choice of collider species
  Proton – Proton/antiproton (higher energy, one of the three quarks involved in the interaction)
  Electron – Positron/electron (Lower energy, full energy involved in the interaction)
  Heavy ions
  Gamma rays
 All contribute to a full picture of the forces that govern the interaction of particles

## Slide 29
Colliders
Proton-proton collider with Ek of 2×100 GeV
= proton beam with Ek of 20000 GeV heat a stationary target
Fixed target，Ucm ~ (2Ua × Ub)1/2
Colliding beams, Ucm ~ 2Ua
Needs from the atomic nucleus study:
  Sufficient energy to allow two nuclei to be brought close enough to interact.
The collider concept was first proposed by Rolf Wideröe in1940s.
Circular (double/single ring) or linear
Maximize center-of-mass energy
Luminosity: the likelihood of seeing something interesting from a collision

## Slide 30
Early Colliders
First successful e-e+ collider, ADA, at Frascati, Italy, proposed by Bruno Touschek (1960)
Discovered Touschek lifetime
CBX e-e- collider, Stanford
Stored 1 A/beam
Beam-beam tune shift observed
VEP-1 e-e- collider, Novosibirsk
Beam-beam effects found
Beam-beam tune shift observed

## Slide 31
Hadron Colliders
Developed since 1970s, with increasing energy and luminosity.
Discovery reach determined by the beam energy (dipole magnetic field, size of machine).
Likely to determine the pace of particle-physics progress and essential for establishing the standard model of particle physics.
Hadron collider peak luminosity as a function of year
Luminosity vs. center-of-mass energy

## Slide 32
Z Colliders
Asymmetric Energy B Factories
Intermediate Energy Colliders
Phi-Tau-Charm Colliders
Low Energy Colliders
These facilities essentially shaped modern particles physics.
Electron-Positron Collider Family

## Slide 33
Future Electron-Positron Colliders
CLIC
ILC
SuperKEKB

## Slide 34
Keep construction of bigger and better machines, not a given type, for particle physics research.
Show evolution of accelerator energy in the over 70 years  12 orders of magnitudes increase on the accelerator energy.
Accelerators have become indispensable in the quest to understand nature at smaller and smaller scales.
Livingston chart
Examine at the scale of atom: keV
At the scale of nucleus: MeV
Fine structure of the basic constituents of matter: GeV
Livingston plot
Higher energy  shorter wavelength  probe deeper into the structure:

## Slide 36
Accelerator related subjects
Physics
Technologies
Vacuum
Radio frequency
Magnet
Power supply
Mechanics
Superconducting
Electronics
Computers
…
Relativistic dynamics
Electrodynamics
Plasma physics
…
Hinge upon many different physics subjects and advanced technologies

## Slide 37
Recommended books

## Slide 38: Thank you for your attention!