## Slide 1
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS, Xavier Buffat, Angeles Faus-Golfe
Thursday 6 of March 2025
Work funded, in parts, by the EU under Horizon-Europe Grant agreement nr. 101086276 (EAJADE)

## Slide 2
Impedance and beam-beam effects for FCC-ee
Thursday 6 of March 2025
Table of contents:
Introduction
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
  Mitigation methods
Horizontal plane instability driven by beam-beam
Summary and outlook
Roxána SOÓS
Motivation: Study intensity limitations due to beam-beam and wakefields effects in FCC-ee to understand limiting parameters and find mitigation methods.

## Slide 3
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Introduction
All following simulations will be given for FCC-ee, September 2024 parameters table at Z energy.
All simulations have been carried out by either multiparticle tracking using Xsuite [1], or a linear algebraic model: the Circulant Matrix Model (CMM) [2].

## Slide 4
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Introduction
Xsuite is using element by element tracking, nonlinear forces included
  Transverse wakefields
  Simulation of a quarter ring
  exploiting the four-fold symmetry
Linear transfer map
(avoid complicated effects from the non-linear lattice)
SEXTUPOLE
SEXTUPOLE
  Crab sextupoles
  as thin multipole elements
  Strong-strong beam-beam
  model at the IP

## Slide 5
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Introduction
Xsuite is using element by element tracking, nonlinear forces included
  Transverse wakefields
  Simulation of a quarter ring
  exploiting the four-fold symmetry
Linear transfer map
(avoid complicated effects from the non-linear lattice)
SEXTUPOLE
SEXTUPOLE
  Crab sextupoles
  as thin multipole elements
  Strong-strong beam-beam
  model at the IP
Notes: For PDF export only

## Slide 6
The Circulant Matrix Model (CMM) [2] is a linear mode analysis method based on the discretisation of the longitudinal phase space.
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Introduction
Linearized forces in the transverse plane applied to:
Linear transfer matrix
Beam-beam force
Transverse impedance force
Space charge
Longitudinal impedance force
Diagonalisation gives eigenvalues
Real part = oscillation mode
Imaginary part = growth rate
One can highlight
instable modes

## Slide 7
The Circulant Matrix Model (CMM) [2] is a linear mode analysis method based on the discretisation of the longitudinal phase space.
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Introduction
Linearized forces in the transverse plane applied to:
Linear transfer matrix
Beam-beam force
Transverse impedance force
Space charge
Longitudinal impedance force
Diagonalisation gives eigenvalues
Real part = oscillation mode
Imaginary part = growth rate
One can highlight
instable modes
Notes: For pdf export only

## Slide 8
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Introduction
The dominant instability due to beam-beam and transverse wakefields for the FCC-ee at Z energy, in the vertical plane, is the transverse mode repulsion instability (TMRI).
-1 mode
0mode
0mode
-1 mode
Phase advance
Strong hourglass
Large crossing angle
See [3,7], for more details
TMRI is a very low order instability.
CMM
CMM

## Slide 9
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
Interaction point (IP)
y1,B1
y2,B1
y2,B2
y1,B2
Vertical coordinates of two charges per beam, at a given turn n.
Vertical linearised coherent beam-beam kick matrix for two charges per beam. No phase advance considered.
Arc matrix with synchro-betatron motion.
  (2 particles model)

## Slide 10
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
Diagonalise and get the eigenvalues . One can vary the weight of the charges (~ N particles) in the beam-beam force.
Real part of the eigenvalues give the tune shift
  Mode 0 and -1 can be extracted to a 4x4 matrix.
  Mode 0 (= mode ) stays constant with variation of N.
  Mode -1 shifts and crosses mode 0
Imaginary part of the eigenvalues give the growth rate
  No coupling, no instability induced
  (2 particles model)

## Slide 11
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
Interaction point (IP)
y1,B1
y2,B1
y2,B2
y1,B2
Vertical coordinates of two charges per beam, at a given turn n.
Vertical linearised coherent beam-beam kick matrix for two charges per beam. No phase advance considered.
Arc matrix with synchro-betatron motion.
Transverse wakefield matrix with dipolar and quadrupolar wakefields.
  (2 particles model)

## Slide 12
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
Diagonalise and get the eigenvalues . One can vary the weight of the charges (~ N particles) in the beam-beam force and the wake functions
Real part of the eigenvalues give the tune shift
  Mode 0 and -1 can be extracted to a 4x4 matrix.
  Mode 0 (= mode ) stays constant with variation of N.
  Mode -1 shifts and couples to mode 0.
Imaginary part of the eigenvalues give the growth rate
  Coupling induces an imaginary part.
  Mode coupling instability appears
  (2 particles model)

## Slide 13
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
Interaction point (IP)
y1,B1
y2,B1
y2,B2
y1,B2
Vertical coordinates of two charges per beam, at a given turn n.
Phase advance at the interaction point considered using the kick and drift model [4].
Arc matrix with synchro-betatron motion.
  (2 particles model)

## Slide 14
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
Diagonalise and get the eigenvalues . One can vary the weight of the charges (~ N particles) in the beam-beam force.
Real part of the eigenvalues give the tune shift
  Mode 0 and -1 can be extracted to a 4x4 matrix.
  Mode 0 (= mode ) no longer constant with variation of N.
  Mode -1 repulse each other with mode 0.
Imaginary part of the eigenvalues give the growth rate
  No coupling, no instability induced
  (2 particles model)

## Slide 15
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
Interaction point (IP)
y1,B1
y2,B1
y2,B2
y1,B2
Vertical coordinates of two charges per beam, at a given turn n.
Arc matrix with synchro-betatron motion.
Transverse wakefield matrix with dipolar and quadrupolar wakefields.
Phase advance at the interaction point considered using the kick and drift model [4].
  (2 particles model)

## Slide 16
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
Diagonalise and get the eigenvalues . One can vary the weight of the charges (~ N particles) in the beam-beam force and the wake functions
Real part of the eigenvalues give the tune shift
  Mode 0 and -1 can be extracted to a 4x4 matrix.
  Mode 0 (= mode ) no longer constant with variation of N.
  Mode -1 repulse each other with mode 0.
Imaginary part of the eigenvalues give the growth rate
  Repulsion now induces an imaginary part.
  Mode repulsion instability appears.
  (2 particles model)

## Slide 17
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Transverse mode repulsion instability mechanism
Phase advance
Strong hourglass
Large crossing angle
beam-beam, NO phase advance
beam-beam + wakes, NO phase advance
Instability can be analytically described!
beam-beam, phase advance
beam-beam + wakes, phase advance
Transverse mode repulsion instability (TMRI) has no clear threshold because there is no coupling!
  (2 particles model)

## Slide 18
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Mitigation methods
CMM
Xsuite, crab sextupoles
Tracking: crab sextupoles have an impact on the tune shift, but instability growth rate is correct. If no crab sextupole is set, tune shift is correctly predicted. Growth rate cannot be extracted because of instant blow up.

## Slide 19
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Mitigation methods
CMM
Xsuite, crab sextupoles
Tracking: crab sextupoles have an impact on the tune shift, but instability growth rate is correct. If no crab sextupole is set, tune shift is correctly predicted. Growth rate cannot be extracted because of instant blow up.
Xsuite, NO crab sextupoles
Growth rate not available because of blow up due to the missing crab sextupole

## Slide 20
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Mitigation methods
CMM
Xsuite
Chromaticity was studied in Xsuite and CMM. Both agree that chromaticity is a mitigation method to consider. However, tracking is necessary to carry out studies on mitigation.
Different chromaticity value was found, could be explained by the Landau damping (not present in CMM), [5].
Tune shift variation versus the chromaticity identical.
Tune shift is different due to the Crab sextupoles.
A chromaticity > 5 was find to be enough to mitigate effectively the instability.
FCC-ee (Z) chromaticity scan at nominal intensity N0 = 2.16x1011

## Slide 21
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Mitigation methods
Chromaticity (needed to stabilise the vertical motion) needs to be highly increased if impedance is doubled.
Too high chromaticity can practically unacceptable due to its impact on beam quality.
Impedance is therefore an intensity limiting contributor, a careful design is necessary to limit instabilities.
Xsuite
Chromaticity was studied in Xsuite and CMM. Both agree that chromaticity is a mitigation method to consider. However, tracking is necessary to carry out studies on mitigation.

## Slide 22
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Vertical plane instabilities due to impedance and beam-beam
  Mitigation methods
FCC-ee (Z), with Damper (gx=1, phi = 0)
FCC-ee (Z), no Damper
The impact of a purely resistive damper seems limited.
Damper was studied in CMM. Resistive damper’s impact visible on the most unstable mode but is very slight. Reactive damper must be investigated too.
Ongoing study on different types of dampers!

## Slide 23
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Horizontal plane instability driven by beam-beam
CMM is a fast (~few hours on cluster) and adequate tool to simulate <x-z> instabilities.
The effect of different parameters such as the Qs , bunch length, energy spread, … on the <x-z> can be studied with CMM
The longitudinal wakefields are being implemented in the model so that their effect can also be studied.
Mitigation methods (damper, chromaticity, …) can be studied with CMM
FCC-ee (Z) at VRF = 79MV (Table s.3)
CMM
Horizontal plane is dominated by the beam-beam driven, coherent <x-z> instability. [5,6]

## Slide 24
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
Conclusion and outlook
The mode coupling instability of the colliding beams driven by impedance becomes a Transverse mode repulsion instability (TMRI) in the presence of strong hourglass.
  Mitigation methods have been discussed. Chromaticity is a good candidate; the corresponding impedance budget is tight. Further investigation involves various setup of transverse dampers.
  The mechanism of damping with chromaticity is not reproduced by the linear model; tracking simulations must be used to determine precise threshold (Landau damping).
CMM shows to be efficient for the study of the coherent <x-z> instabilities in the horizontal plane.
  Longitudinal impedance is being added to the CMM model and will be used to study its impact on the coherent <x-z> instability. (Further information available soon at IPAC 2025)
Possibility to simulate asymmetric beam-beam interaction requires an adjustment in CMM. Concurrent studies could be conducted for SuperKEKB in the future.

## Slide 25
Work funded, in parts, by the EU under Horizon-Europe Grant agreement nr. 101086276 (EAJADE)
THANK YOU FOR LISTENING!

## Slide 26
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
REFERENCES
[1] X. Buffat, The Circulant Matrix Model and the Role of Beam-beam Effects in Coherent Instabilities, CERN Yellow Reports: Conference Proceedings , 25 Pages (2018), artwork Size: 25 Pages Publisher: CERN.
[2] Iadarola et al., Xsuite: An Integrated Beam Physics Simulation Framework, JACoW , 8 pages, 1.757 MB (2023), artwork Size: 8 pages, 1.757 MB ISBN: 9783954502530 Medium: application/pdf Publisher: JACoW Publishing, Geneva, Switzerland.
[3] https://indico.global/event/9305/contributions/90666/
[4] Hirata et al., A symplectic beam-beam interaction with energy change, Part. Accel. 40, 205 (1993)
[5] Ohmi, K., N. Kuroo, K. Oide, D. Zhou, and F. Zimmermann. ‘Coherent Beam-Beam Instability in Collisions with a Large Crossing Angle’. Physical Review Letters 119, no. 13 (26 September 2017): 134801. https://doi.org/10.1103/PhysRevLett.119.134801.
[6] Lin, Chuntao, Kazuhito Ohmi, and Yuan Zhang. ‘Coupling Effects of Beam-Beam Interaction and Longitudinal Impedance’. Physical Review Accelerators and Beams 25, no. 1 (24 January 2022): 011001. https://doi.org/10.1103/PhysRevAccelBeams.25.011001.
[7] Lin, Chuntao, Kazuhito Ohmi, and Yuan Zhang. ‘Coupling Effects of Beam-Beam Interaction and Longitudinal Impedance’. Physical Review Accelerators and Beams 25, no. 1 (24 January 2022): 011001. https://doi.org/10.1103/PhysRevAccelBeams.25.011001.

## Slide 27
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
BACKUP

## Slide 28
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
BACKUP
CMM
CMM
FCC-ee (Z), Maximum growth rate at N0 = 2.16x1011
FCC-ee (Z), Minimum growth rate at N0 = 2.16x1011
Damper has an impact on the most stable mode too
Damper has effect on the most unstable mode!
Reactive damper could be used?
Work in progress: Investigation to be done on wider areas, on mode evolutions etc!!!

## Slide 29
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
BACKUP
CMM
CMM
FCC-ee (Z), Maximum growth rate at N0 = 2.16x1011
FCC-ee (Z), Minimum growth rate at N0 = 2.16x1011
Damper has effect on the most unstable mode!
Reactive damper could be used?
Damper has an impact on the most stable mode too
Work in progress: Investigation to be done on wider areas, on mode evolutions etc!!!

## Slide 30
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
BACKUP

## Slide 31
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
BACKUP

## Slide 32
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
BACKUP
mode (out of phase oscillation)

## Slide 33
Impedance and beam-beam effects for FCC-ee
Roxána SOÓS
Thursday 6 of March 2025
BACKUP