## Slide 1
Impedance Budget and Single-Bunch instabilities at FCC-ee
Dora Gibellieri1,2,3, Carlo Zannini1, Adnan Ghribi2,3, Mauro Migliorati4,5 and Mikhail Zobov4,5
1CERN 2University of Caen Normandy 3GANIL 4Sapienza University of Rome 5INFN
- 70th ICFA Advanced Beam Dynamics Workshop on High-Luminosity Circular e⁺e⁻ Colliders

## Slide 2
Introduction
FCC-ee main ring Impedance Model
  Criticality of collimator model
  Effect on single-bunch instabilities
FCC-ee booster stability considerations
Conclusion and next steps
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Outline
02

## Slide 3
Introduction
FCC-ee main ring Impedance Model
  Criticality of collimator model
  Effect on single-bunch instabilities
FCC-ee booster stability considerations
Conclusion and next steps
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Outline
Introduction
03

## Slide 4
FCC-ee main parameters for Z configuration
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Introduction
Parameter | Value
Circumference (km) | 90.658816
Beam energy (GeV) | 45.6
Bunch population (1011) | 2.14
RF frequency (MHz) | 400
RF voltage (MV) | 79
Energy loss per turn (GeV) | 0.0391
Longitudinal dumping time (turns) | 1158
Momentum compaction factor 10-6 | 28.6
Horizontal tune/IP | 54.5395
Vertical tune/IP | 55.55
Synchrotron tune | 0.0288
Emittance Hor (nm)/Vert (pm) | 0.71/1.9
Bunch length (mm) (SR/BS)* | 5.6/15.4
Energy spread (%) (SR/BS)* | 0.039/0.109
Piwinsky angle (BS)* | 26.4
/ | 0.022/0.097
β* Hor (m)/Vert (mm) | 0.11/0.7
Luminosity/IP (1034/cm2s) | 141
Parameter | Value
Circumference (km) | 90.658816
Beam energy (GeV) | 45.6
Bunch population (1011) | 2.14
RF frequency (MHz) | 400
RF voltage (MV) | 79
Energy loss per turn (GeV) | 0.0391
Longitudinal dumping time (turns) | 1158
Momentum compaction factor 10-6 | 28.6
Horizontal tune/IP | 54.5395
Vertical tune/IP | 55.55
Synchrotron tune | 0.0288
Emittance Hor (nm)/Vert (pm) | 0.71/1.9
Bunch length (mm) (SR/BS)* | 5.6/15.4
Energy spread (%) (SR/BS)* | 0.039/0.109
Piwinsky angle (BS)* | 26.4
 | 0.022/0.097
β* Hor (m)/Vert (mm) | 0.11/0.7
Luminosity/IP (1034/cm2s) | 141
*SR: synchrotron radiation, BS: beamstrahlung
04

## Slide 5
FCC-ee main parameters for Z configuration
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Introduction
Parameter | Value
Circumference (km) | 90.658816
Beam energy (GeV) | 45.6
Bunch population (1011) | 2.14
RF frequency (MHz) | 400
RF voltage (MV) | 79
Energy loss per turn (GeV) | 0.0391
Longitudinal dumping time (turns) | 1158
Momentum compaction factor 10-6 | 28.6
Horizontal tune/IP | 54.5395
Vertical tune/IP | 55.55
Synchrotron tune | 0.0288
Emittance Hor (nm)/Vert (pm) | 0.71/1.9
Bunch length (mm) (SR/BS)* | 5.6/15.4
Energy spread (%) (SR/BS)* | 0.039/0.109
Piwinsky angle (BS)* | 26.4
/ | 0.022/0.097
β* Hor (m)/Vert (mm) | 0.11/0.7
Luminosity/IP (1034/cm2s) | 141
Parameter | Value
Circumference (km) | 90.658816
Beam energy (GeV) | 45.6
Bunch population (1011) | 2.14
RF frequency (MHz) | 400
RF voltage (MV) | 79
Energy loss per turn (GeV) | 0.0391
Longitudinal dumping time (turns) | 1158
Momentum compaction factor 10-6 | 28.6
Horizontal tune/IP | 54.5395
Vertical tune/IP | 55.55
Synchrotron tune | 0.0288
Emittance Hor (nm)/Vert (pm) | 0.71/1.9
Bunch length (mm) (SR/BS)* | 5.6/15.4
Energy spread (%) (SR/BS)* | 0.039/0.109
Piwinsky angle (BS)* | 26.4
 | 0.022/0.097
β* Hor (m)/Vert (mm) | 0.11/0.7
Luminosity/IP (1034/cm2s) | 141
*SR: synchrotron radiation, BS: beamstrahlung
Since the transverse impedance of RW is proportional to , this reduction causes the increase of RW impedance by 60%
From 2023 change of bunch population :
 particles per bunch
  Change of beam pipe radius :
    35 mm  30 mm
Necessity of having a highly flexible model to account for all changes during the feasibility study development phase
05

## Slide 6
Introduction
FCC-ee main ring Impedance Model
  Criticality of collimator model
  Effect on single-bunch instabilities
FCC-ee booster stability considerations
Conclusion and next steps
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Outline
FCC-ee main ring impedance model
06

## Slide 7
Identify main
impedance contributors:
Collimators
Resistive Wall etc.
3D EM Simulations
(CST, Wakis, Echo3D etc.) and Analytical Model (equations, IW2D, etc.)
Building I/W Model (Xwakes integration)
Beam Dynamics Simulations (Xsuite) with feedback system
Output:
Assessment of beam stability
Goal: keep improving the Model
Constant I/W Model Optimization
Reminder: because of the short bunch, simulations are very challenging
I/W Model for FCC-ee
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Beam coupling impedances studies
FCC-ee main ring impedance model
07

## Slide 8
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Identify main
impedance contributors:
Collimators
Resistive Wall etc.
3D EM Simulations
(CST, Wakis, Echo3D etc.) and Analytical Model (equations, IW2D, etc.)
Building I/W Model (Xwakes integration)
Beam Dynamics Simulations (Xsuite) with feedback system
Output:
Assessment of beam stability
I/W Model for FCC-ee
Beam coupling impedances studies
08

## Slide 9
What is the impedance model of a machine?
Is the collection of the impedance contributions of the different elements of the machine
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
FCC-ee impedance model
09

## Slide 10
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Impedance elements studied
The beam pipe is evaluated with IW2D which considers a 90 km-long circular NEG-coated copper pipe. By incorporating numerical form factors, we account for the winglets shape.
10

## Slide 11
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Impedance elements studied
Beam halo collimators and synchrotron radiation collimators were evaluated using CST simulations, considering a 15-degree taper angle.
11
Notes: Tot CST simulations= Imp. Resistiva dovta al gap che puo essere calcolata analicamnete + geometrica . Dal imp taper.
Per convenienxa (metti formula)

## Slide 12
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Name | Length (m) | gap/2 (mm) | Material | (m) | (m)
tcp.h.b1 | 0.25 | 6.7 | MoGr | 517.98 | 755.84
tcp.v.b1 | 0.25 | 2.4 | MoGr | 519.09 | 756.98
tcs.h1.b1 | 0.3 | 3.7 | Mo | 117.58 | 789.74
tcs.v1.b1 | 0.3 | 2.5 | Mo | 421.47 | 587.39
tcs.h2.b1 | 0.3 | 5.1 | Mo | 214.69 | 759.20
tcs.v2.b1 | 0.3 | 2.9 | Mo | 32.80 | 827.50
tcp.hp.b1 | 0.25 | 4.2 | MoGr | 72.05 | 125.94
tcs.hp1.b1 | 0.3 | 4.6 | Mo | 64.12 | 186.88
tcs.hp2.b1 | 0.3 | 16.7 | Mo | 855.10 | 368.74
tcr.h.wl.2.b1 | 0.1 | 17 | W | 2056.83 | 8840.68
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h.c2.1.b1 | 0.1 | 16 | W | 2099.51 | 5012.40
Name | Length (m) | gap/2 (mm) | Material |  | 
tcp.h.b1 | 0.25 | 6.7 | MoGr | 517.98 | 755.84
tcp.v.b1 | 0.25 | 2.4 | MoGr | 519.09 | 756.98
tcs.h1.b1 | 0.3 | 3.7 | Mo | 117.58 | 789.74
tcs.v1.b1 | 0.3 | 2.5 | Mo | 421.47 | 587.39
tcs.h2.b1 | 0.3 | 5.1 | Mo | 214.69 | 759.20
tcs.v2.b1 | 0.3 | 2.9 | Mo | 32.80 | 827.50
tcp.hp.b1 | 0.25 | 4.2 | MoGr | 72.05 | 125.94
tcs.hp1.b1 | 0.3 | 4.6 | Mo | 64.12 | 186.88
tcs.hp2.b1 | 0.3 | 16.7 | Mo | 855.10 | 368.74
tcr.h.wl.2.b1 | 0.1 | 17 | W | 2056.83 | 8840.68
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h.c2.1.b1 | 0.1 | 16 | W | 2099.51 | 5012.40
Impedance elements studied
Total collimator impedance obtained from CST simulations is considered as the sum of the resistive contribution associated with the collimator gap, which can be analytically evaluated using IW2D and the contribution related to the influence of the taper. From this point onward, we will refer to this as “geometric”.
12
tcp: primary, tcs: secondary, tcr: synchrotron radiation, h: horizontal, v: vertical, , , .
Notes: Tot CST simulations= Imp. Resistiva dovta al gap che puo essere calcolata analicamnete + geometrica . Dal imp taper.
Per convenienxa (metti formula)

## Slide 13
Beam Pipe
Collimators
Polarimeter
RF fingers
RF cavities
BPMs
Photon stoppers
Bellows
It is essential to emphasize that the design of these elements is continuously evolving.
Developing a highly flexible model enables informed design decisions, to ensure beam stability.
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Impedance elements studied
13

## Slide 14
High flexibility
Crucial when frequent updates are foreseen
The developed impedance model easily interfaces with IW2D, allowing us to quickly estimate the impedance by changing for example resistive parameters, such as the material type and, in this case, the thickness of the NEG coating.
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Highly flexible I/W model
14

## Slide 15
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
FCC-ee main ring impedance evaluation
Using the developed impedance model, the total transverse and longitudinal impedance contributions, including all considered elements, can be easily extrapolated.
15

## Slide 16
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
FCC-ee main ring impedance evaluation
The visualization of certain parameters, such as the imaginary part of the y-dipolar and longitudinal impedance of various contributors, enables the identification of the primary impedance sources.
16

## Slide 17
tcp.v.b1
Coll. length = 250 mm
Taper length = 110mm
Taper angle = 15 degrees
tcp.v.b1
Coll. length = 250 mm
Taper length = 630 mm
Taper angle = 2.5 degrees
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Criticality of the collimator model
Since the geometrical contribution of the collimators has been identified as the primary source of impedance, an optimization of the taper angle for all vertical collimators has been proposed, reducing it from the initially proposed 15 degrees to 2.5 degrees.
17

## Slide 18
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Criticality of the collimator model
Thanks to the optimization of the taper angle for all vertical collimators by reducing it from 15 degrees to 2.5 degrees, the y-transverse impedance drastically reduces.
Horizontal and vertical collimator taper angle of 15 degrees
Horizontal collimator taper angle of 15 degrees and vertical taper angle of 2.5 degrees
18

## Slide 19
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Criticality of the collimator model
Thanks to the optimization of the taper angle for all vertical collimators by reducing it from 15 degrees to 2.5 degrees, the y-transverse impedance drastically reduces.
Horizontal and vertical collimator taper angle of 15 degrees
Horizontal collimator taper angle of 15 degrees and vertical taper angle of 2.5 degrees
19

## Slide 20
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Criticality of the collimator model
Thanks to the optimization of the taper angle for all vertical collimators by reducing it from 15 degrees to 2.5 degrees, the y-transverse impedance drastically reduces.
Horizontal and vertical collimator taper angle of 15 degrees
Horizontal collimator taper angle of 15 degrees and vertical taper angle of 2.5 degrees
There is significant potential for optimizing collimators.
20

## Slide 21
The importance of a highly flexible model
The design of the vacuum chamber and the machine devices continue to evolve
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
Continuous model updates
The design of various elements is constantly evolving. For example, a new proposal suggests using the KEK design for collimators.
21

## Slide 22
Identify main
impedance contributors:
Collimators
Resistive Wall etc.
3D EM Simulations
(CST, Wakis, Echo3D etc.) and Analytical Model (equations, IW2D, etc.)
Building I/W Model (Xwakes integration)
Beam Dynamics Simulations (Xsuite) with feedback system
Output:
Assessment of beam stability
I/W Model for FCC-ee
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Beam dynamic simulations and stability assessments
FCC-ee main ring impedance model
22

## Slide 23
Overview of different scenarios with and without chromaticity and with and without feedback system.
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
TMCI threshold
23
Feedback, chroma 0
Feedback, chroma 5
No feedback, chroma 0
No feedback, chroma 2
With chromaticity and feedback on (4 turns) intra-bunch motion at
More details in: M. Migliorati et al., FCC-ee single beam collective effects - FCC week 2024
Nominal intensity:
Notes: Individuare iol mardine da utilizzare (deve essere inferior a un fattore 2)

## Slide 24
Without considering the geometric contribution of the collimators, we are already at the limit of stability. To stabilise we need a feedback system and chromaticity (left plot). If we double the total wake and impedance we have evaluated so far (right plot) despite feedback and chromaticity, the TMCI threshold will be at , below the nominal intensity (). It is therefore essential to optimise the geometric impedance of the collimators and assess its impact on the beam dynamics.
Feedback, chroma 5
Feedback, chroma 5 with double wake
More details in: M. Migliorati et al., FCC-ee single beam collective effects - FCC week 2024
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
TMCI threshold
24
Notes: Individuare iol mardine da utilizzare (deve essere inferior a un fattore 2)

## Slide 25
Introduction
FCC-ee main ring Impedance Model
  Criticality of collimator model
  Effect on single-bunch instabilities
FCC-ee booster stability considerations
Conclusion and next steps
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Outline
FCC-ee booster stability considerations
25

## Slide 26
Challenges in HEB PA31.0 (2023) Design:
  Microwave instabilities
  Transverse mode coupling instabilities
  Transverse coupled bunch instabilities
HEB PA31.3 (2024) Design Enhancements and Solutions:
  Change of pipe diameter
    25 mm  30 mm
  Change of pipe material
    Stainless steel  copper
  Change of momentum compaction factor
More details in: A. Ghribi et al., FCCee high energy booster - FCC week 2024
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee booster stability considerations
High Energy Booster impedance induced effects
26

## Slide 27
Challenges in HEB PA31.0 (2023) Design:
  Microwave instabilities
  Transverse mode coupling instabilities
  Transverse coupled bunch instabilities
HEB PA31.3 (2024) Design Enhancements and Solutions:
  Change of pipe diameter
    25 mm  30 mm
  Change of pipe material
    Stainless steel  copper
  Change of momentum compaction factor
  Transverse feedback
    310 turns
More details in: A. Ghribi et al., FCCee high energy booster - FCC week 2024
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee booster stability considerations
High Energy Booster impedance induced effects
27

## Slide 28
Introduction
FCC-ee main ring Impedance Model
  Criticality of collimator model
  Effect on single-bunch instabilities
FCC-ee booster stability considerations
Conclusion and next steps
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Outline
Conclusion and next steps
28

## Slide 29
Simulations made on Xsuite and PyHEADTAIL
FCC-ee Impedance Model available on GitHub
Codes for the booster available on CERN gitlab
Impedance budget space (common to booster and collider) on CERN gitlab
Calculations made on several computing clusters : LXPLUS (CERN), FEYNMAN (CEA), and with dedicated computing resources on Jean-Zay (IDRIS) and CC IN2P3
Dedicated chat spaces for the high energy booster and the collective effects studies on mattermost
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Conclusion and next steps
Status updates: tools, models, and resources
29

## Slide 30
🔹 Impedance/Wake Model Development for Critical Design Decisions:
  The extremely short bunch length makes impedance and wakefield simulations highly challenging.
  Wall Model: Numerical form factors have been incorporated into the model for both driving and detuning impedance, accounting for vacuum chamber shape.
  Collimators: A step-by-step approach is being adopted to explore computational limits and propose optimized impedance solutions.
  Updated of impedance and models in Xwakes.
  Ensured model flexibility to facilitate impedance and wakefield updates in optics, material choices, coating thickness, geometries, and new machine elements.
  Enabled impedance assessments of different scenarios.
🔹 Beam Dynamics Simulations (Xsuite/PyHEADTAIL):
  Single-bunch beam dynamics simulations.
    Single-bunch TMCI threshold evaluation and impact of machine settings as a key impedance figure of merit.
🔹 Booster Studies:
  Significant design enhancements and solutions strategies have been adopted.
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Conclusion and next steps
Conclusion
30

## Slide 31
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Ongoing activities: example
Having a highly flexible model enables us to provide prompt feedback on the newly proposed collimation optics. For example, the 2025 version of the collimation layout optics can be readily simulated to deliver quantitative impedance assessments.
Courtesy of Giacomo Broggi and the entire collimation team
Conclusion and next steps
31
Notes: Tot CST simulations= Imp. Resistiva dovta al gap che puo essere calcolata analicamnete + geometrica . Dal imp taper.
Per convenienxa (metti formula)

## Slide 32
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Name | Length (m) | gap/2 (mm) | Material | (m) | (m)
tcp.v.b1 | 0.25 | 1.3 | MoGr | 58.78 | 325.49
tcs.v1.b1 | 0.3 | 1.1 | Mo | 137.04 | 136.68
tcp.h.b1 | 0.25 | 4.8 | MoGr | 264.84 | 67.28
tcs.h1.b1 | 0.3 | 3.8 | Mo | 139.99 | 134.95
tcs.v2.b1 | 0.3 | 1.2 | Mo | 90.32 | 156.202
tcs.h2.b1 | 0.3 | 5.3 | Mo | 273.17 | 49.14
tcp.hp.b1 | 0.25 | 13.7 | MoGr | 820.27 | 230.11
tcs.hp1.b1 | 0.3 | 4.6 | Mo | 38.73 | 1211.32
tcs.hp2.b1 | 0.3 | 7.5 | Mo | 101.25 | 1331.31
tct.h.3.b1 | 0.25 | 2.6 | MoGr | 67.78 | 2347.3
tct.v.3.b1 | 0.25 | 7.3 | MoGr | 8.262 | 6002.39
tcr.h.wl.2.b1 | 0.1 | 21.7 | Inermet180 | 3580.09 | 4999.68
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h2.c0.1.b1 | 0.1 | 21.5 | Inermet180 | 3527.07 | 4251.22
Name | Length (m) | gap/2 (mm) | Material |  | 
tcp.v.b1 | 0.25 | 1.3 | MoGr | 58.78 | 325.49
tcs.v1.b1 | 0.3 | 1.1 | Mo | 137.04 | 136.68
tcp.h.b1 | 0.25 | 4.8 | MoGr | 264.84 | 67.28
tcs.h1.b1 | 0.3 | 3.8 | Mo | 139.99 | 134.95
tcs.v2.b1 | 0.3 | 1.2 | Mo | 90.32 | 156.202
tcs.h2.b1 | 0.3 | 5.3 | Mo | 273.17 | 49.14
tcp.hp.b1 | 0.25 | 13.7 | MoGr | 820.27 | 230.11
tcs.hp1.b1 | 0.3 | 4.6 | Mo | 38.73 | 1211.32
tcs.hp2.b1 | 0.3 | 7.5 | Mo | 101.25 | 1331.31
tct.h.3.b1 | 0.25 | 2.6 | MoGr | 67.78 | 2347.3
tct.v.3.b1 | 0.25 | 7.3 | MoGr | 8.262 | 6002.39
tcr.h.wl.2.b1 | 0.1 | 21.7 | Inermet180 | 3580.09 | 4999.68
- | - | - | - | - | -
- | - | - | - | - | -
tcr.h2.c0.1.b1 | 0.1 | 21.5 | Inermet180 | 3527.07 | 4251.22
Ongoing activities: example
Collimators’ parameter from the version 2025 of the collimation layout optics. Importance to highlight the changes on the vertical primary collimator tcp.v.b1, found to play a critical role in the overall collimators’ impedance.
tcp: primary, tcs: secondary, tct: tertiary, tcr: synchrotron radiation, h: horizontal, v: vertical, , , , .
Courtesy of Giacomo Broggi and the entire collimation team
Conclusion and next steps
32
  Compared to the previous scenario for tcp.v.b1, there was a decrease in the half-gap:
  2.4 mm  1.3 mm
  Decrease of :
  756.98 m  325.49 m
Notes: Tot CST simulations= Imp. Resistiva dovta al gap che puo essere calcolata analicamnete + geometrica . Dal imp taper.
Per convenienxa (metti formula)

## Slide 33
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Conclusion and next steps
Next steps and ongoing activities
🔹 Model Updates & Implementation:
  Continuous update of impedance and wakefield models in Xwakes.
  Ensure model flexibility.
  Final assessments for different scenarios.
🔹 Beam Dynamics Simulations (Xsuite):
  Ongoing benchmark studies between PyHEADTAIL and Xsuite, moving toward a full transition to Xsuite.
  Multi-bunch feedback system simulations to assess machine configuration effects.
  Integration of advanced feedback features from PyHEADTAIL multi-bunch into Xsuite.
  Investigating the impact of nonlinear impedance terms.
🔹 Booster Studies:
  Complete impedance model development.
  Further investigations into impedance effects and potential mitigation strategies.
33

## Slide 34
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Conclusion and next steps
Founding statement
34
Project part of FCCIS – The Future Circular Collider Innovation Study. This INFRADEV Research and Innovation Action project receives funding from the European Union’s Horizon 2020 Framework Programme under grant agreement no. 951754.
Project partially supported by EAJADE, the Marie Sklodowska-Curie Research and Innovation Staff Exchange (SE) programme, funded by the EU under Horizon-Europe Grant agreement ID: 101086276.

## Slide 35
Thank you for your attention 
- 70th ICFA Advanced Beam Dynamics Workshop on High-Luminosity Circular e⁺e⁻ Colliders
Tsukuba International Congress Center (EPOCHAL)
Tsukuba, Japan

## Slide 36
Backup
- 70th ICFA Advanced Beam Dynamics Workshop on High-Luminosity Circular e⁺e⁻ Colliders
Tsukuba International Congress Center (EPOCHAL)
Tsukuba, Japan

## Slide 37
The Z configuration has been investigated due to the largest number of bunches (smallest bunch spacing)
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee collider parameters
37

## Slide 38
Dumping mechanisms: propagation losses (taper angle) and resistive losses (conductivity)
Resonating modes in the jaws due to impedance mismatch
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Resonance study
38

## Slide 39
Xwakes provides generic tools to build a Machine Impedance Model
A Model represents the impedance of an accelerator by combining all its elements, while preserving the individual knowledge of each contribution
Wake
Impedance
Wake
Impedance
ABP-CEI Section Meeting (28 November 2024) · Indico
06.03.2025 | eeFACT 2025 | Dora Gibellieri
I/W model with Xwakes
39
Notes: Formula impedenza: somma impedenza singoli elementi pesata per la beta/beta medio
How impedance is calculated: the impedance calculated with CST is multiplied by the specific beta of each collimator and then weighted by the mean beta. For the average beta we use the smooth approximation. i.e. average radius of the machine divided by the tune
Impedance evaluated is multiplied by the specific 𝛽 of each collimator and weighted by 𝛽_smooth
𝛽_𝑠𝑚𝑜𝑜𝑡ℎ= 𝑟𝑎𝑑𝑖𝑢𝑠/𝑡𝑢𝑛𝑒 radius=𝐴𝑣𝑒𝑟𝑎𝑔𝑒 𝑟𝑎𝑑𝑖𝑢𝑠 𝑜𝑓 𝑡ℎ𝑒 𝑚𝑎𝑐ℎ𝑖𝑛𝑒~𝑐𝑖𝑟𝑐/2𝑝𝑖

## Slide 40
The model contains a list of elements
How is the total Impedance of the model computed?
Note that the individual elements can still be accessed through the model
Where is the beta function of the element, is the average beta function of the ring and is the transverse impedance of the element
The total transverse impedance is calculated as follows:
06.03.2025 | eeFACT 2025 | Dora Gibellieri
I/W model with Xwakes
40
Notes: Formula impedenza: somma impedenza singoli elementi pesata per la beta/beta medio
How impedance is calculated: the impedance calculated with CST is multiplied by the specific beta of each collimator and then weighted by the mean beta. For the average beta we use the smooth approximation. i.e. average radius of the machine divided by the tune
Impedance evaluated is multiplied by the specific 𝛽 of each collimator and weighted by 𝛽_smooth
𝛽_𝑠𝑚𝑜𝑜𝑡ℎ= 𝑟𝑎𝑑𝑖𝑢𝑠/𝑡𝑢𝑛𝑒 radius=𝐴𝑣𝑒𝑟𝑎𝑔𝑒 𝑟𝑎𝑑𝑖𝑢𝑠 𝑜𝑓 𝑡ℎ𝑒 𝑚𝑎𝑐ℎ𝑖𝑛𝑒~𝑐𝑖𝑟𝑐/2𝑝𝑖

## Slide 41
06.03.2025 | eeFACT 2025 | Dora Gibellieri
NEG thickness comparison
41
Beam pipe impedance for different thicknesses of the NEG coating.

## Slide 42
Impedance contributions considering a collimators’ taper angle of 15 degrees
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
42

## Slide 43
06.03.2025 | eeFACT 2025 | Dora Gibellieri
FCC-ee main ring impedance model
43
Impedance contributions considering a collimators' taper angle of 15 degrees for horizontal collimators and 2.5 degrees for vertical collimators

## Slide 44
06.03.2025 | eeFACT 2025 | Dora Gibellieri
Impedance elements studied
44
Details on some elements included in the present FCC-ee impedance model:
For the bellows the SuperKEKB model with sliding contacts has been considered.
For the BPMs a scaled model from DA𝛷NE has been considered, with a cylindrical button with a diameter of 15 mm and a thickness of 3 mm. This gives a trapped mode around 6 GHz.