## Slide 1
Status and outlook of FCCee transverse diagnostic systems
Daniele Butti, Stefano Mazzoni, CERN – Beam Instrumentation group
with many thanks to
B. Paroli, M. A. C. Potenza, M. Siano (Università degli Studi di Milano)
U. Iriso, A. A. Nosych, J. Nunez, E. Solano, L. Torino (ALBA-CELLS)
T. Lefevre, G. Trad (CERN)
2025 eeFACT workshop - Tsukuba
3rd February 2025

## Slide 2: Outline
Requirements for FCC-ee transverse diagnostics
Implementation scenarios
Synchrotron Radiation based techniques
pinhole camera
X-ray interferometry and X-ray Heterodyne Near Field speckles
Outlook and conclusion

## Slide 3: Requirements for transverse diagnostics
EFFORT
IMPACT
Precision
±1%
Accuracy
±15%
Single bunch
Redundancy
2x beam
Multiple techniques likely required to meet all specifications
Real-time precise measurement is top priority for commissioning
On-demand accurate measurements required for machine optimization
Synchrotron radiation natural choice for non-invasive transverse diagnostics
Requirements summary from feasibility study report

## Slide 4: Implementation scenarios
Diagnostic challenges
small vertical beam sizes
high photon energy
Integration challenges
high radiation and power load
large bending radius (long extraction lines)
Options for SR source
arc dipoles: maximum flexibility but harsh environmental conditions
exp/tech site dipoles: limited choice but more favorable beam sizes

## Slide 5: Arc dipoles
Challenging radiation conditions
high power load ~8kW/mrad
photon spectrum too hard for diagnostics in higher-energy operation modes
z
ttbar
V24 GHC
Challenging beam conditions
small beam sizes
limited flexibility in machine optics
diagnostics
region

## Slide 6: Region downstream of Interaction Points
V24 GHC
()
More suitable conditions downstream of IPs
“soft” bend dipoles for source
more relaxed beam size constraints
upstream of strong bend, good for fast light-beam separation
→ present baseline for transverse diagnostics

## Slide 7: Synchrotron radiation techniques for transverse diagnostics
optics
SR imaging
Imaging and interferometry often combined in synchrotron radiation diagnostics
imaging provides robust and precise relative measurements
interferometry used for accurate absolute measurements
SR interferometry
interference target
monochromator

## Slide 8: Pinhole camera
Standard for X-ray diagnostics
robust and minimal system
good precision <2%
good accuracy for
possible bunch-by-bunch
typically
Resolution ⟺ pinhole width
large gives large geometric error
small gives large diffraction error
→ optimum pinhole width for a given energy

## Slide 9: Ray tracing simulations of pinhole camera
photon beam
particle beam
(incl. bend)
blocked
diffracted
Effective profile

## Slide 10: Ray tracing simulations of pinhole camera
Horizontal
Vertical
Ray tracing confirms analytical estimation of the resolution around the optimum
Deviations for large because blur is enhanced by large bending radius

## Slide 11: Resolution of pinhole camera
Pinhole camera resolution determined by pinhole width
accurate for working at
Measurements of smaller beam sizes limited by resolution
best resolution
*
*realistic 50 keV photons and
Ultimate resolution of SR diagnostics is diffraction limit

## Slide 12: X-ray interferometry
Variety of targets
apertures/slits
scattering fibers
nanostructured materials
better resolution than pinhole...
Interferometry is complementary technique to imaging
→ assess beam size from contrast of interference fringes
…but with common challenges
require monochromatic light
highly sensitive to distortions
increased setup complexity
filament beam
extended beam
Imaging and interferometry can coexist on same extraction line, often with same detector
interference target
monochromator
detector

## Slide 13: X-ray Heterodyne Near Field Speckles (HNFS)
monochromator
scatterers
single scatterer
many scatterers
power spectrum
Interference target is a dispersion of light-scattering nanospheres
Key features for implementation in FCCee
intrinsically two-dimensional measurement
compact, no need of long distances downstream of target
Silica spheres (500 nm)

## Slide 14: Beam size measurements with x-ray HNFS
Si(111) monochromator
nanospheres
undulator source
%
%
Credit: M. Siano
Measurements at ALBA synchrotron (Spain)
systematic validation at undulator beamline
measured beam size as small as

## Slide 15: Future tests with dipole source
Challenges to deploy technique at FCCee
high energy photons
broadband (dipole) SR source
new dipole line being equipped at ALBA for HNFS tests using dipole synchrotron radiation
In-vacuum multilayer monochromator
Layout of FE21 at ALBA, equipped for HNFS studies
Detector
Scatterers
Credit: U. Iriso

## Slide 16: Development of new target materials
Numerical simulations
(SRW, preliminary)
Credit: J. Nunez
Nanostructured gold target
Credit: S. Mazzoni
Silica nanospheres not usable in regular FCC operation
poor contrast of SiO2 with hard x-rays
stability issues such as sedimentation and aggregation of colloids
need to develop and study novel target materials
Ongoing R&D to design and manufacture gold-based scatterers, optimized for FCC applications, to be tested in new ALBA beamline

## Slide 17: Outlook
Main focus of upcoming pre-TDR stage is engineering of diagnostics systems
technical design and integration of extraction lines
detailed study of thermal loads along the lines
detailed study of critical components (e.g. monochromator)
Ongoing R&D on technological aspects of proposed techniques
production and characterization of novel HNFS targets at ALBA beam-line
study of detector options (e.g. scintillators, TimePix…)
Preserve flexibility on changes of machine design
further optimize present scenarios (e.g. adapt machine optics, tunable magnets…)
consider additional/alternative locations and possible synergies with longitudinal diagnostics extracting UV-VIS radiation

## Slide 18: Conclusion
Baseline scenario for transverse diagnostics at end of feasibility study
synchrotron radiation source downstream of main IPs
pinhole cameras for machine commissioning and precise tuning
interferometric techniques for accurate measurements
X-ray Heterodyne Near Field Speckles successfully tested at ALBA light source, new dedicated line soon ready for tests of novel targets with dipole radiation
Technical implementation is main objective of Technical Design Report phase

## Slide 19: Thank you for your attention!
19

## Slide 20: FCCee machine parameters
Parameter | Unit | Z | WW | HZ | ttbar
synchrotron radiation power | MW | 50 |  |  | 
beam energy | GeV | 45.6 | 80 | 120 | 182.5
beam current | mA | 1270 | 137 | 26.7 | 4.9
number bunches |  | 11200 | 1780 | 440 | 60
horizontal emittance | nm | 0.71 | 2.17 | 0.71 | 1.59
vertical emittance | pm | 1.9 | 2.2 | 1.4 | 1.6
bunch length with SR / BS | mm | 5.6 / 15.5 | 3.5 / 5.4 | 3.4 / 4.7 | 1.8 / 2.2
luminosity | 1034 cm-2s-1 | 140 | 20 | 5.0 | 1.25
integrated luminosity | ab-1/yr/IP | 17 | 2.4 | 0.6 | 0.15
Four operational modes to maximize physics output
→ changing energy (and current) at fixed SR power
4 years
5x1012 Z
LEP x105
2 years
>108 WW
LEP x104
3 years
2x106 H
5 years
2x106 tt pairs
M. Benedikt
FCC week 2024

## Slide 21: Ray tracing
photon beam
particle beam
(incl. bend)
blocked
diffracted
Effective profile

## Slide 22: Ray tracing
Horizontal
Vertical
Ray tracing confirms analytical estimation of the Point Spread Function around the optimum
Deviations for large because blur is enhanced by large bending radius

## Slide 23: Dipole magnets around IPs (ttbar mode)
Example centre of BC7
with for pinhole at
Critical energies of most dipoles too high (>1 MeV) for diagnostics at tt mode
→ working in low frequency tail of spectrum
V23

## Slide 24: Dipole magnets around RF
Example centre of BRI1
with for pinhole at
Pro:
less SR power
Cons:
integration (inside ring and layout changes with mode)
similar beam sizes as arcs
V23

## Slide 25: Dipole magnets around RF (ttbar mode)
Example centre of BI1
with for pinhole at
V23

## Slide 26: Synchrotron radiation extraction geometry
light sampling
detector
If we assume to measure source sizes of , we need at least a factor 2 magnification
→ requires distance from the pinhole, corresponding to transverse distance
beam
light