## Slide 1: Non-elliptical Cavities
Bob Laxdal, TRIUMF
SRF2025 Tutorial

## Slide 2: Outline
Non-elliptical cavities
  Why do we need them
  Low beta evolution
Cavity types
  Figures of merit and parametrization
  Choosing a cavity type
  Examples of TEM cavities
Linac considerations
  Beam dynamics issues for low beta
  Linac design
Cavity production
  Design considerations
  Post-fabrication tuning
  Surface treatment/processing
Cryomodule issues

## Slide 3: Why non-elliptical cavities?

## Slide 4: Accelerating Electrons vs Hadrons
Electron – 0.511MeV/c2
  300kV - γ=1.58, =0.78
  550MeV - γ=1011, =1
Protons – 938 MeV/c2
    300kV - γ=1.003, =0.025
    550MeV - γ=1.58, =0.78
  Electron and hadron linacs are distinctly different due to the mass of the particles
8 gm
160 kgm
ARIEL 300kV e-gun
TRIUMF 500MeV cyclotron

## Slide 5
source
β=0.002
β ~0.02
β ~0.05
β >0.05
β~1
Electron linacs – common building blocks all designed for  =1
Hadron linacs – various building blocks – different technologies each optimized to accelerate a given velocity range
SRF section initial energy is dependent on duty factor – for cw applications it is typical to start after the RFQ
  RF acceleration depends on synchronization between the rf and the particle bunches so is strongly dependent on velocity
  Electron acceleration must be effective at =1 while hadron acceleration must be effective over a very wide velocity range
Linac architecture

## Slide 6: Hadron cavity zoo
Electron linacs – common building blocks all designed for  =1
design has largely converged
Hadron linacs
  various building blocks – different cavity types each optimized to accelerate a given velocity range
  typically short independently phased resonators with broad velocity acceptance
  common building blocks but community still customizing designs

## Slide 7: Velocity limitation of elliptical cavities
0.9

## Slide 8: Why TEM mode cavities?
TEM mode cavities produce accelerating fields transverse to the inner conductor axis
For optimal acceleration the gap to gap distances are /2 where =v/c
For small  then  must be large enough for reasonable gap dimensions – more later
The cavity height is used to adjust  (rf frequency) and the dimensions along the beam axis are scaled to match the velocity
TEM cavities allow us to accelerate low and medium beta particles in a multi-gap structure with good efficiency and mechanical stability
Depending on the cavity type TEM mode cavities are 2-4 times smaller transversally than the same frequency elliptical cavity

## Slide 9: Low beta evolution

## Slide 10: Applications
Traditionally low beta SRF resonators were quarter waves (or split rings) used as boosters for heavy ion tandems (ATLAS, INFN-LNL, IUAC)
Next came low beta cavities for post-accelerators for Radioactive Ion Beams (RIBs) – ISAC-II, NSCL-ReA, HIE-Isolde
High duty cycle driver linacs are now being built with SRF sections beginning at lower beta values (FRIB, SPIRAL-II, PIP-II, C-ADS, IFMIF, …)
  Rise in use of half-wave resonators (HWR) and spoke cavities (SSR, DSR)
  Clean room assembly, HPWR, heat treatments and separated vacuum cryostats are now standard
Deflecting mode cavities have seen a rise in interest due to new high performance, compact designs for applications such as crabbing cavities for Luminosity upgrades in ring colliders (HiLumi@CERN)

## Slide 11
Non-elliptical SRF Community
TRIUMF
FRIB
ANL
Frankfurt
IUAC
SARAF
LNL
Orsay
Saclay
IHEP
RIKEN
ESS
IMP
RISP
ANU
TIFR
FNAL
CERN
BNL
ODU

## Slide 12: Non-elliptical Facilities and Projects
Project | Lab | Driver | Post-accelerator | Particle | Structure
ATLAS | ANL |  |  | HI | Split-ring, QWR
ALPI | LNL |  |  | P, d / HI | QWR (sputter, bulk)
ISAC-II | TRIUMF |  |  | HI | QWR
IUAC | IUAC |  |  | HI | QWR
ReA3/6 | NSCL |  |  | HI | QWR
HIE-Isolde | CERN |  |  | HI | QWR (sputter)
SARAF | SOREQ |  |  | P, d | HWR
SPIRAL-II | GANIL |  |  | P, d, HI | QWR
IFMIF | Saclay |  |  | P,d | HWR
FRIB | NSCL |  |  | HI | QWR, HWR
ESS | ESS |  |  | P | DSR
RAON | RISP |  |  | HI | QWR, HWR, SSR
ADS | IMP,IHEP |  |  | p | HWR, SSR
PIP-2 | FNAL |  |  | P | HWR, SSR
SRILAC | RIKEN |  |  | HI | QWR
Hi-Lumi | CERN |  |  | p | Crab cavities - DQWR, RFD

## Slide 13: Cavity concepts

## Slide 14: Coaxial resonator (TEM mode)
Coaxial geometries support TEM modes - assume inner radius a and outer radius b and height h with grounded plates at the ends
A standing wave occurs with the rdial electric field Er vanishing on the end walls at z=0 and z=h
Magnetic fields loop around the inner conductor with peak fields at the shorted ends
E and B are 90 degrees out of phase
a
b
h
z
Er
B
I
Chart: 
E
B
,t
The voltage on the inner conductor
E
B
z
0
h

## Slide 15: Half Wave Resonator (HWR) p=1
Fundamental mode has p=1 – half wave resonator
a
b
h
z
Er
B
I
Peak surface fields are on the inner conductor
Peak voltage is at the center z=h/2
E
B
z
0
h
With frequency and wavelength

## Slide 16: Acceleration with HWR
V,E
I,B
Example: h = 0.5 m, =1m, f=300MHz
If 0=0.2 then the gap to gap distance must be L=0.1m for synchronism
L
L
h
An accelerating cavity can be made by adding beam ports at the center where the Er field and voltage are maximum
The ion travel time is arranged so that the Er field is maximum when the ion crosses the first gap and undergoes a  phase shift as the ion travels to the 2nd gap
Note for synchronism there is a relation between the gap-to-gap distance, the particle velocity and the rf frequency
The cavity design is based on a reference particle of speed 0 , called the design velocity, that defines the distance between gap centers as /2 with cavity length quoted as

## Slide 17
Quarter Wave Resonator (QWR)
Example: h = 0.5 m, =2m, f0=150MHz
If =0.1 then the gap to gap distance must be L=0.1m for synchronism
h
L
V,E
I,B
Another popular coaxial TEM mode cavity is the quarter wave resonator (QWR)
Here the inner conductor is open at one end with a resonant length of
The typical accelerating mode has
The maximum voltage occurs on the open tip and the maximum current is at the root
A beam tube is arranged near the end of the tip to produce a double gap acceleration geometry similar to the HWR with cavity length quoted as

## Slide 18: Example: Single Spoke Resonator (SSR)
SSR-Top view
SSR – side view
Multi-spoke - MSR
2β0
A single spoke resonator (SSR) is another variant of the half-wave resonator
The SSR has a single inner conductor transverse to the beam direction of length /2 that forms a two gap accelerating device similar to the HWR
Unlike the HWR the outer conductor of the SSR is co-axial with the beam tube with diameter /2.
The cavity operates in pi-mode with the distance between gap centers as β0 /2 with cavity length quoted as .
Can be configured with a few spokes to make a multi-gap cavity with cavity length quoted as where n is the number of gaps
β0
/2
/2

## Slide 19: Figures of merit and parametrization

## Slide 20
Reminder: Figures of merit (FoM)
Parametrization – FoM can be applied to the QWR and HWR using the known magnetic fields over the rf volume and surface

## Slide 21: Assumptions for parametrization
V,E
I,B
V,E
I,B
Coaxial HWR fields can be used to parameterize both the HWR and QWR variants
HWR is represented well by the coaxial fields presented in slide 15
For QWR we assume the fields of half the HWR – not exact due to the open end of IC –justification is that parametrization uses magnetic field that is concentrated away from open end
2a
2b=a
0/2
0/4
Design velocity, 0, can be added to the parameterization by noting the dependence of coaxial geometry and 0

## Slide 22: Figures of Merit for QWR and HWR

## Slide 23
Value | QWR | HWR | Scaling
U |  |  | 
Pc |  |  | 
Q |  |  | 
G |  |  | 
R/Q |  |  | 
Value | QWR | HWR | Scaling
U |  |  | 
Pc |  |  | 
Q |  |  | 
G |  |  | 
R/Q |  |  | 
Choosing

## Slide 24: Model vs actual - G
Comparing the analytic model with actual designs
SSRs larger volume

## Slide 25
Comparing the analytic model with actual designs
Model vs actual – R/Q

## Slide 26: Choosing a cavity type

## Slide 27: Frequency choice – TEM mode
Longitudinal (beam direction) cavity dimensions are dependent on beam velocity (β) – transverse cavity dimensions are dependent on 
Smaller structures are cheaper to fabricate so favour small  (high frequency)
Lower frequencies increase size of stable region in longitudinal phase space
Lower velocities need lower frequencies
  There is β0λ/2 between gap centers (one cell) and the gap length is typically half a cell or g=β0λ/4
  Drift tube aperture should be less than the gap to improve acceleration efficiency ie a/g<0.8
g
a
Quarter Wave - QWR
Half Wave - HWR
/4
/2
β
β
g=gap, a=aperture

## Slide 28
Commonality
The typical building blocks are QWR, HWR, SSR and MSR but the community has not coalesced towards common designs as has happened in the high beta community
The main reason is the large parameter space since each project may have different requirements – final energy, ion, existing infrastructure
  At least design techniques, principles, ancillaries are converging
However at least two frequency series have emerged as being more common

## Slide 29: Actual cavity designs

## Slide 30: QWR vs HWR
QWR is the cavity of choice for low beta applications (<0.15)
  Pros:
    rf power loss is ~50% of HWR for same frequency, energy gain and β0
    Easy tuning at bottom plate
  Cons:
    asymmetric field pattern can add vertical steering - not suitable for high intensity light ion applications and for higher velocities
    less mechanically stable
HWR is chosen in mid-velocity range >0.15 or where beam steering is an issue
  Pros: symmetric field pattern and mechanical stability
  Cons: 2x structure and rf losses compared to QWR

## Slide 31: HWR vs Single Spoke (SSR)
A single spoke resonator (SSR) is another variant of the HWR TEM cavity
HWR – the outer conductor is coaxial with the inner conductor with diameter ~0
SSR – the outer conductor is coaxial with the beam path with diameter /2
For 0 <0.5 the SSR has a larger overall physical envelop than the HWR for the same frequency
For 0 =0.1->0.25 HWRs are typically chosen for ~160MHz while SSRs are built for ~320MHz
For 0 =0.25->0.5 HWRs and SSRs adopt typically ~320MHz – with G slightly larger in SSRs
The spoke geometry allows an extension along the beam depth for multiple gaps in a longer cavity

## Slide 32: Accelerating cavities – cavity type/ velocity/frequency chart
Elliptical
Deflecting mode

## Slide 33: Examples of TEM Cavities

## Slide 34: Cavity types – quarter waves
FRIB β=0.041, 0.085 80.5MHz
ANL β=0.077, 0.085 72.5MHz
TRIUMF ISAC-II Resonators
Spiral-2 β=0.007, 0.12 88.05MHz
RAON β=0.047, 81.25 MHz
Typical range
β~0.04->0.15
f=50MHz->160MHz

## Slide 35: Cavity types – half waves
FRIB β=0.29, 0.53 f=322MHz
IMP β=0.10, f=162.5MHz
ANL β=0.112, f=162.5MHz
FRIB β=0.29, 0.53 f=322MHz
Typical range
β~0.10->0.5
f=140MHz->325MHz
IFMIF β=0.11, f=175MHz

## Slide 36: Cavity types – Single spokes
IHEP β=0.12, f=325MHz
TRIUMF/RISP β=0.3, f=325MHz
FNAL β=0.215, f=325MHz
325 MHz, β0 = 0.82 Single-Spoke Cavity
Typical range
β~0.15->0.7
f=325-700MHz

## Slide 37: Multi-cell
500 MHz, β0 = 1 Double-Spoke Cavity
ESS/IPN β=0.50, f=352MHz
ANL β=0.63, f=345MHz

## Slide 38: Deflecting mode cavities
A sub-set of cavities are designed to provide a phase dependent transverse deflection to the beam using a TE-like (H-mode) dipole electric field
Applications include crab cavities and rf kickers
Deflection from both electric and magnetic fields
Frequency governed by transverse dimension (~ λ/2)
TRIUMF 650MHz H-mode deflecting cavity

## Slide 39: Deflecting mode cavities
TRIUMF 650MHz
double quarter wave (DQW) – 400MHz – BNL/CERN
RF Dipole (RFD) – 400MHz – ODU/CERN
RFD – multi-cell – 953MHz – ODU

## Slide 40
E- field
H- field
Cross bar H mode - CH
Another multi-gap variant is the cross-bar H-mode cavity
Spokes stem from four ridges with opposite ridges having the same voltage and adjacent ridges in anti-phase
Designed to give a high accelerating voltage in a fixed velocity regime
CH 6 cell fabricaated by IMP – 162.5MHz β=0.067
360 MHz, β0~0.1 19 gap CH resonator

## Slide 41: End of Part I Questions?

## Slide 42: Acceleration considerations

## Slide 43: RF Acceleration
cos t
t
z
z, t
Ez (z,t)
Ez (z)
c
Example: Acceleration gap
=0
g
Consider an electric field in an accelerating gap
The ion travels with velocity c on axis and experiences a field that is the product of the spatial variation and the time modulation
  Where  is a constant (the rf phase) that defines the time of arrival of the particle with respect to the rf time modulation.
  A phase of =0 corresponds to the maximum acceleration that can be given to the particle (`on crest’ acceleration)
the accelerating voltage imparted to the ion is given by
For simplicity assume a square profile

## Slide 44: Transit time factor of short (few gap) structures
Veff is called the accelerating voltage or effective voltage – due to the time variation of the fields it is less than integrating through the absolute value of the static field, V0
The transit time factor is the ratio between actual voltage gain, and the absolute magnitude of the total time independent voltage gain,
A convenient voltage gain formula is
A useful figure of merit called the acceleration gradient is given by

## Slide 45
Single Gap Transit time factor (TTF)
Assume an accelerating gap with an accelerating field approximated with a square profile
Here note that as g->0 the TTF -> 1 but small gaps cannot support high fields
The gap geometry is optimized using a number of considerations
  typically the gap is ~half a cell where a cell is /2
  So g=/4
  and 0.9
-g/2
g/2
Energy gain
E0

## Slide 46
Single Gap – Transit time
In reality the field penetrates into the drift tube and reduces the transit time factor (dependent on aperture to gap ratio f=a/g)
This reduces the transit time factor for on axis particles
Where f=a/g and I0 is the modified Bessel function of the first kind
Typically try to limit a/g<0.8 for reasonable efficiency T(0)=0.82
Realistic Single Gap TTF
a=2r0

## Slide 47: Two Gap TTF
0/2
cav
For a two-gap structure the optimum acceleration occurs when the rf gains 180 degree () from gap center to gap center at the design velocity, 0
Slower or faster particles will get less kick due to reduced synchronization with the rf phase
Assuming a square field distribution of field in the gap the combined two-gap transit time factor is given by
VIC
VIC= inner conductor voltage
/0
=0
=0.70
=1.50

## Slide 48: Energy Gain in a Two-gap structure
For = 0 ion is synchronized with the rf
Maximum energy gain in a first gap
=
Maximum energy gain in a second gap
=
Total gain
= 2
where T is the single gap T
For other ion velocities, , the efficiency is reduced
where and 2
The effective voltage is V0T where V0 is the sum of the voltages that could be gained in each gap assuming no TTF and T is the single gap transit time factor
VIC = the voltage on the inner conductor
VIC
L =
g
g
g
g

## Slide 49: Multiple gaps (Normalized Transit time)
For multi-gap structures
Multiple gaps (n) will increase the total voltage gain since and
But the velocity acceptance of the transit time factor is reduced as n increases
β0)
T(β)

## Slide 50: Beam Dynamics Issues for low beta

## Slide 51: Linac longitudinal dynamics
It is important to maintain periodic focusing in both transverse and longitudinal planes
An ion linac (v<c) is designed for the acceleration of a single ideal particle which remains in synchronism with the accelerating fields and is called the synchronous particle – the synchronous particle phase is s
Restoring forces are needed so that an ensemble of particles near the synchronous particle will be accelerated and transported
Longitudinal focusing is provided by an appropriate choice of phase of the synchronous particle
Synchronous particle
Early particle
Late particle
If the synchronous particle crosses the gap center as the field is rising (negative phase), the particle arrives before the peak field is reached
Early particles receive less kick and late particles receive more kick as the field amplitude grows to provide correction

## Slide 52: RF Gaps – Transverse motion
Transverse rf forces exist at gaps from Er components of the off-axis fields
For an accelerating phase Er is focusing at the gap entrance and defocusing at the gap exit.
If the field is rising (negative accelerating phase) the focusing kick is weaker than the defocusing kick and overall defocusing occurs with radial kick given by given by
Leads to a simple transfer matrix of a lens that can be used in simulations – for transverse focusing kr=-abs(kr) so 0<s<90
focus
defocus
Ez (z)
-Er (z)

## Slide 53: Longitudinal and radial stability - summary
To accelerate and focus the beam longitudinally we need a negative synchronous phase -90<ϕs<0 so that there is a restoring force to keep the motion stable
When -90<ϕs<0 the rf gap produces a defocusing force in the transverse dimension
Periodic focussing must be added transversely to counteract the rf defocusing (ie quadrupoles, solenoids)
The rf gap defocusing force is reduced at higher energies and so less transverse focussing is required

## Slide 54: Transverse focussing choices
Two basic transverse focussing choices for TEM SRF linacs
Room temperature quadrupoles
  Positioned between cryomodules as doublets or triplets
  Pros – easier to install, align and replace
  Cons – forces shorter modules especially at low  - electrical power
SC solenoids in CMs
  Placed between cavities with a periodicity required by beam dynamics
  Pros – high electrical efficiency, allows long cryomodules for less static cryo losses
  Cons - Require careful alignment, care must be taken to avoid magnetic pollution in cavities

## Slide 55: QWR steering
QWRs produce a finite vertical electric field and a non-zero azimuthal magnetic field 90 degrees out of phase that steers the beam
At higher beta, β0>0.15, where forces increase, the fields can produce significant vertical steering especially for β < β0
Mitigations include
  Aligning the resonator below the the beam axis to provide a correction from rf defocusing
  Modifying gap geometry to correct the steering by means of additional transverse electric field components

## Slide 56: Linac design

## Slide 57: SRF Hadron Linacs – multiple short cavities
For SRF hadron linacs it is typical to adopt short independently driven TEM cavities:
  Very flexible – each cavity has an independent rf system with adjustable phase and voltage
  Each cavity has a broad velocity acceptance so that only a few unique cavity designs are required with many of each type deployed
  Acceleration can be customized for a particular A/Q value or range of values
  Lower A/Q values can be accelerated to higher velocities than higher A/Q values
  High number of rf systems increases costs but rf units are typically modest

## Slide 58: Linac Design principles
Resonators take time and energy to design and prototype - therefore minimizing the unique number of cavity designs is a design goal
Choosing optimum beta values and frequency based on
  Transit time factor T(β) is efficient over velocities from 0.75β0< β <1.5β0 for a given β0
  For an n-gap structure the cavity voltage is given by Ea*L = Ea*nβ0/2
    for same frequency more voltage for higher β0 values.
    the rf frequency has to be low enough to provide sufficient longitudinal acceptance and gap dimensions while higher frequencies give smaller (cheaper) resonators (and cryomodules) but lower Veff
  For longer linacs a rule of thumb is to maintain a certain cavity type until T(β) lowers the effective voltage below the voltage of the next cavity series
  For β>0.5 it is possible to consider multi-gap spokes since the smaller relative velocity change in this regime reduces the impact of the lower velocity acceptance

## Slide 59: Example: ISAC-II Heavy Ion Linac (post-accelerator)
106.1 MHz β0=5.7%
106.1 MHz β0 =7.1%
141.4 MHz β0 =11%
Consists of 40 QWRs with three different cavity types of β0=5.7%, 7.1% and 11% with N= 8, 12 and 20 cavities of each type
All cavities have same outer and inner conductor diameter to reduce fabrication cost
VIC
V0=2VIC
Ez
z
β0)

## Slide 60: Example – ISAC-II
Choice of values was made to give efficient acceleration for a range of A/Q values
Typically, all cavities run at maximum voltage
The energy gain from one cavity is
where for two gap TTF
The final energy is given by
β0)
ISAC-II – three cavity types with β0=0.057, 0.071 and 0.11 of n = 8, 12 and 20 respectively

## Slide 61: FRIB Heavy ion linac
A/q=7
A/q=3
A/q=3
A/q=2

## Slide 62: Cavity Design

## Slide 63: Cavity design principles
For optimal performance we want to
  Increase Ra/Q – shunt impedance factor
  Increase G – geometry factor
  Reduce Ep/Ea and Hp/Ea – peak surface fields
  Reduce Rs – surface resistance – heat treatments, surface processing
For stability during operation we want to
  Reduce detuning - df/dp (frequency sensitivity with LHe pressure) and microphonics
  Maintain a reasonable rf bandwidth – rf coupling choice
  Supply an effective rf tuner

## Slide 64
Peak Field Limitations in SRF Resonators
Ea is a useful performance metric, but actual performance is limited by peak surface field Ep and peak magnetic field Bp
Cavities are designed to reduce Ep/Ea and Bp/Ea
High surface magnetic fields have high power density (heating) and is fundamentally limited due to SRF state (Bp<~180mT for Nb).
Typical design values for Bp
  For CW applications is Bp = 70mT.
  For pulsed operation is Bp=110mT
High electric surface fields can cause field emission
Typical design values for Ep
  for CW application is Ep = 35MV/m
  for pulsed application is Ep = 50MV/m
Elliptical cavity Ep/Ea~2 and Bp/Ea~4.3mT/MV/m
Coaxial cavity values depend on customization and are velocity dependent: Ep/Ea=3.5-6 and Bp/Ea=6-11mT/MV/m
64

## Slide 65: Ep/Ea – Actual vs model
For
In general Ep/Ea is dominated by the inner conductor tip and beam aperture in QWRs or the beam aperture in HWRs and SSRs and so does not follow the analytical model especially at low beta

## Slide 66
For and
Bp/Ea can be reduced by increasing the inner conductor radius at root end that becomes easier at higher beta
Bp/Ea – Actual vs model

## Slide 67: Cavity design steps
All cavities need care in design and implementation
Good simulation tools exist both on the EM and mechanical aspects (CST, HFSS, COMSOL, Ansys, …)
Goal: Optimize rf parameters while giving a stable mechanical structure at reasonable fabrication cost
RF shape design:
  Achieve rf frequency and β0
  Increase rf efficiency – optimize R/Q and G and minimize peak surface fields
  Check multipacting – simulation tools exist – want to reduce the risk of MP barriers near the operating point where possible
true optimization is a trade-off between practicality/complexity

## Slide 68: Cavity design steps
Mechanical Design
  Baseline mechanical model
    Choose material thickness
    Check all pressure differentials throughout cavity life-cycle – maintain safe limits in terms of stress – pressure vessel code compliance
    Consider df/dp, Lorentz force detuning, mechanical modes
    Consider stiffeners to optimize mechanical performance
  Fabrication design
    Meet with the vendor to discuss design
    Iterate the design for fabrication – variables include performance, complexity, operational requirements, stress analysis, material cost vs machine cost
    Establish fabrication steps, rf frequency trim steps, hold points

## Slide 69: Mitigating Multipacting – Example SSR
Multipacting can be reduced by careful cavity design –
Example – single spoke resonator designed by TRIUMF for RISP project in Korea – 325MHz beta=0.3
A balloon variant reduces serious MP in operating regime – analogy to pill-box vs TM010 elliptical cavity
Other strategies - the SEC can be reduced by baking and rf processing in situ

## Slide 70
With careful design it may be possible to find a geometry that compensates electric and magnetic effects to minimize df/dp

## Slide 71: Microphonics
Driven by mechanical vibration in the environment
QWRs
  pendulum action of the inner conductor -> low mechanical frequencies (50-100Hz)
  need to reduce the RMS detuning to <<10% of the available bandwidth to avoid periodic nuisance unlockings
  Can increase bandwidth through decreasing Qext -> cost implications on rf power
Mitigations
  raise the mechanical frequency of the lowest mechanical modes
  Center the inner conductor by plastic deformation to minimize detuning for given dx
  Add passive dampers in QWR
  Reduce environmental noise in and around the cryomodule

## Slide 72: RF trim steps
RF trim steps are added during manufacture to adjust the final shape to the right rf frequency
A stack-up fixture holds the parts together to allow frequency measurements before welding
Include weld shrinkages, determined through weld samples, in trim calculations
The goal mechanical frequency should be determined by considering
  Final operational frequency
  Tuning pre-load
  Cooldown shrinkage
  External pressure load
  Dielectric adjustment – air->vacuum
  Surface removal during final processing

## Slide 73: Jacket fabrication
Typical jacket materials are Titanium and Stainless steel although reactor grade Nb has been used at ISAC-II and LNL (at least)
Titanium jacket
  For Ti it is typical to use NbTi transitioning material from Nb to Ti
  NbTi material has also been used for flanges – caution: knife edge NbTi flanges are sensitive to wear after several thermal cycles
Stainless steel jacket
  For ss jackets the transition from Nb to SS is typically done through a Cu brazed transition (see for example N. Valverde Alonso, et al, ELECTRON BEAM WELDING AND VACUUM BRAZING CHARACTERIZATION FOR SRF CAVITIES, LINAC2014)
Reactor grade Nb
  Transitions are straightforward
  The material offers the added benefit of being a Meissner shield of the cavity rf surface from active magnetic elements in the cryomodule

## Slide 74: Post-fabrication tuning

## Slide 75: Custom Etching
QWR - ISAC-II - differential etching
  Etch the inductive (root) half by 100 microns
    Δf=-179 kHz
  Etch capacitive (beam port) end by 100 microns
    Δf=+191 kHz
  so differential etch moves the frequency by ~2kHz/µm
  ISAC-II chose to fabricate to a goal frequency 20kHz high and etch at the root to bring the cavity to frequency

## Slide 76
For QWRs with removable tuning plate a Niobium puck can be welded to the tuning plate - reduces cavity resonant frequency by increasing capacity
Puck can be trimmed after final fabrication – watch rf losses on rf joint (B<1mT is safe)
Frequency Compensation
For closed geometries plastic deformation at the beam ports can be done

## Slide 77
Virtual Welding (FRIB)

## Slide 78: Surface treatment / processing

## Slide 79
A Standard Recipe
Variations like 120C bake are time consuming and the effectiveness is dependent on final operating temperature – the effectiveness should be baselined during prototyping

## Slide 80: Q-disease
100K soak test - park the cavity at 100K for four hours and measure any changes in Q
Mitigation is to degas the cavity at 600 – 800C
  Temperature choice can be made based on geometry, material and fabrication details
  SS to Nb braze joints -> limit degas temp to <650C
  Quarter wave treated horizontally -> limit to <650C
Example – heat treatment at FRIB of QWR and HWR is at 600C for 10 hours.
  Total cycle time takes 40 hours
Degassing furnaces are not cheap but for a major project the investment is required

## Slide 81: 120C Bake
Low frequency cavities operating at 4K can benefit from a 120C bake for 24-48 hours in vacuum
The baking lowers the BCS resistance and reduces Q-slope
The treatment tends to slightly degrade the residual resistance – so 4K performance improves and 2K is somewhat degraded
The process only effects the surface so it must be repeated after any etching
Combining the treatment with vertical test can reduce the effects of multipacting by changing SEC
88MHz

## Slide 82: Surface Cleaning and Finish
Two common cleaning/finishing techniques
  Buffered chemical polish (BCP) with 1:1:2 (HF(48%), HNO3(65%), H3PO4(85%)) acid mixture
    Removal rate is ~1m/minute
    Remove typically 120-150 m after fabrication
    Cavity filled during polish and acid recirculated to maintain the temperature
    Straightforward but sludge build-up, bubble and turbulence formation need attention
  Electropolishing (EP) with 85:10 H2SO4 and HF(40%)
    Cavity half-filled and rotated horizontally during polish – aluminum cathode
    ANL has developed a full EP process after final weld
    Development at FRIB showed improved high field performance of EP
FRIB

## Slide 83: High Pressure Water Rinse
8˚
30˚
Clean assembly and HPWR are fundamental to good SRF performance
The geometry of low beta cavities is more complicated than for elliptical cavities
Need to plan during the design stage – require sufficient ports at the right position to guarantee full coverage – also the nozzle design is important
New robotic arm at FRIB is an interesting new innovation

## Slide 84: Cryomodule/Facility Issues

## Slide 85: Magnetic Pollution from Solenoid
Possible cures:
Choose materials that are not easily magnetized
  316LN ss – although this can become susceptible to magnetization after welding or cold working
  Pay attention to hardware – bolts, nuts, especially near high H zones
Develop a degaussing routine
Isolate the cavity from the environment
  Add cold mu metal around the cavity
  Adds to expense and complication of assembly
  Reactor grade Nb jacket can also be used
Isolate the solenoid from the environment
  Add an iron return core
  Add a shield around the magnet
Many low beta linac designs choose superconducting solenoids placed within the cryomodule for periodic transverse focusing – risk of magnetic pollution degrading cavity performance

## Slide 86: ISAC-II perspective
In ISAC-II we chose a minimalist strategy – choose non magnetic materials where possible – no shielding between cavity and solenoid – use procedures
Must do a degaussing of the solenoid before any planned warm-up to erase magnet memory
During cryogenic events (1-2 per year) of more than a few hours if cavities warm above transition then the solenoid is degaussed and then heated above transition to release frozen flux
  30 min to degauss and 30 min to warm to 25K
  60 min to cool everything down
Cavities are insensitive to quench degradation since they have a reactor grade jacket which acts as a Meissner shield

## Slide 87: 2K or 4K for low beta
  4K operation requires less hardware and is three times more efficient than 2K operation
  Since BCS resistance scales with ω2 cavities with frequencies <200MHz should be more efficient to operate at 4K
  However, the Medium Field Q-Slope (MFQS) at 4K may make 2K operation advantageous – 120C bake reduces MFQS
  An advantage to operating at 2K is that the helium bath is much quieter (T<T) than at 4K and more stable in absolute pressure
K. Saito – SRF2015
FRIB 80.5MHz β=0.085 QWR

## Slide 88: Summary
There is now tremendous global interest in non-elliptical SC technology for low to medium energy hadron acceleration as well as for niche applications such as rf deflecting mode cavities
TEM cavities allow acceleration at <0.5 and at lower frequencies due to more compact geometry with the associated larger longitudinal acceptance
Performance of TEM mode low beta resonators now comparable to high beta TM cavities in terms of peak fields achieved
The community is very active and there is room for new ideas and solutions. Enjoy SRF2025 and keep an eye out for non-elliptical cavity advances!

## Slide 89: Questions?

## Slide 90: Useful relations

## Slide 91: MULTI-FREQUENCY COAXIAL RESONATORS
At TRIUMF two custom built coaxial cavities (QWR and HWR) are used to explore and optimize performance over a broad frequency range by exciting the cavities at different harmonics
  Cavities can be excited at fundamental (200MHz) plus higher harmonics to allow direct comparisons of results.
To be answered: What is the dependence of rf surface resistance as a function of frequency and field?
QWR
HWR
RF field distribution of TEM modes