## Slide 1
THE TRISTRON, A NEW PARADIGM IN HIGH-EFFICIENCY RF POWER GENERATION
I. Syratchev , N. Catalan Lasheras, R. Gerard, L. Giezendanner, R. Leuxe, C. Marrelli, W.L. Millar, A. Piccini, A. S. Thakur, European Organization for Nuclear Research, Geneva, Switzerland. G. Burt, Z. Un Nisa, Lancaster University, Lancaster, United Kingdom.

## Slide 2
RF power generation in FCCee.
Improving RF power sources efficiency will not only reduce considerably electricity power consumption but also will reduce installation and operation cost of power converters and cooling system (environmental impact).
https://fcc.web.cern.ch/overview
 | Z | W | H | ttbar2 | booster
400MHz | 100MW | 100MW | 100MW | 21MW | 
800MHz |  |  |  | 79MW | ~1 MW/all poles
FCCee RF power sources must compensate for the beam synchrotron radiation losses in the collider ring:
UHF, 0.3-1MW range, CW klystrons.
Thales (LHC)
2002
CERN target
2028
CERN/Thales
(HL-LHC)
2023
CEPC
2024
CEPC targets
2026/27
Technology turn over
FCCee Tristron/ 2024
Philips (LEP)
1993
Toshiba(TRISTAN)
1990
CPI(HERA)
1996
Single beam
Multi beam
Multi beam + Depressed Collector
CERN TS MBK
2022

## Slide 3
High Efficiency International Klystron Activity (HEIKA) was initiated at CERN in 2014 ( 9 experts worldwide from Europe, Asia and USA). 15 publications over 3 years.
New electrons bunching methods like COM, COM#2D, BAC and CSM (> 80%)
CERN home made code KlyC. A fast and accurate tool to simulate linear beam, devices.
HEIKA was converted into CERN HE klystron project in 2021.
Retro-fit efficiency upgrade of existing commercial klystrons:
X-band Canon 6MW, pulsed tube (41%-> 56%) 2022.
X-band CPI 50MW, pulsed tube (39%-> 65%). To be tested at MPP (former CPI) in 2026.
UHF Thales 0.3MW, CW tube (60%->70%) 2024.
New Two-stage Multi-Beam klystron technology (>85%) 2020. A potential technology of choice for large colliders like CLIC, ILC, FCCee , MuCol…
High efficiency RF power sources development at CERN.
CSM
COM#2D
TH2167 HE
RF power upgrade for HL/LHC
ETD

## Slide 4
High efficiency RF power source for FCCee. Challenges.
In the last 5 years the novel concept of the very efficient 1.0MW multi-beam (MB) Two-Stage (TS) klystron was developed at CERN, and it was ready for the industrialization.
Recent (2024) evolution of the FCCee collider layout reduces the maximum needs RF power from 1MW to below 0.5 MW and suggests operating collider in Reverse Phase Operation regime (RPO) for Z pole.
RPO requires ~25% of RF power transient modulation to compensate for the effect of the beam abort gap in the two families of accelerating cavities:
With such RF power modulation, most of the time klystron will be operated below saturation. Thus, klystron’s operational efficiency will be reduced from 86 % (in saturation) to 67 %.
TS MBK efficiency in saturation
below saturation
at fixed voltage
FCCee 400MHz, 1.0 MW TS MBK

## Slide 5
https://proceedings.jacow.org/ipac2018/papers/wexgbf1.pdf
State of the art
ESS 0.7GHz, 1.2MW Mult-Beam IOT
Gridded tubes, like Inductive Output Tubes (IOT), are another class of electrovacuum devices that are renowned for their ability for efficient operation in a wide range of the output power levels when regulated by the input RF signals.
The practical efficiency in industrial prototypes was limited to ~70%.

## Slide 6
Tristron (A.D. Sushkov et. al., 1967)
400 MHz FCCee tristron power/efficiency performance
simulated by CERN’s home-made code KlyC.
IOT (A. Haeff, 1939)
Alike IOT, Tristron (a hybrid between triode and klystron) is a gridded tube with additional penultimate cavity that can boost the RF power production efficiency from 70% to above 90%.
Tristron concept is almost 60 years old, but it was never commercialized.
MB Tristron RF circuit with beam
RF power
Efficiency

## Slide 7
How Tristron can be so efficient?
Multi-beam technology -> low perveance (K=I/V1.5) per beam: .
Gridded gun provides fully saturated bunches -> 75% (best IOT performance; B class)
Penultimate cavity controls optimal velocity spread (congregation) within the bunch, followed by bunch length compression in the drift -> 85% (basic of the Tristron concept).
Long gap in the output cavity with negative detuning allows electrons bouncing -> 90%.
Hollow beam configuration reduces radial bunch stratification -> 93%.
FCCee TS MBK
Tubes efficiency vs. perveance
FCCee MB tristron
Bouncing electrons
Electron bunches velocity modulation in tristron
Optimal congregation
Penultimate cavity
Output cavity
Drift length provides optimal bunch length compression
Klystrons theoretical limit
Average velocity (0.1Ve/c)
Spent beam
Phase space animation
Ideal bunch + TS MBK output cavity
CEPC CSM klystron

## Slide 8
DC breaker
at HV
at ground
“Open” MB input cavity
Hollow beam
Gridded gun
RF Circuit
Common collector
Output RF Window
FCCee 400MHz MB Tristron on one slide

## Slide 9
Gridded gun for tristron
Flat HEX grid fabricated at CERN using Laser-cut technology on Pyrolytic Graphite wafer sample with 150 microns thickness.
For the design point of 450kW output RF power:
Maximal temperature reaches 426 C0 (T cathode = 1000 C0; T ambient =100 C0; beam intercepted power 58W).
Grid deformation in ‘Z’ direction is +/-1 micron.
Beam optics
0.08T, 3.5 A DC current
Solenoidal field profile
Beam power intercepted on the grid
Bunch generation in the gridded gun (CST 3D PIC)
Cathode – grid gap is 0.3mm.
Grid’s wire cross-section 0.15mm x 0.15 mm
A.S. Thakur poster session MOP7192

## Slide 10
FCCee 400MHz MB Tristron performance simulated in CST 3D PIC
Calculating efficiency in CST 3D PIC#1 (RF efficiency).
RF power measured at the output coupler port.
Calculating efficiency in CST 3D PIC#2 (Balanced efficiency).
Spent beam power measured in the collector
Pin=10.7A x 46kV=492kW
Electronic eff.
Ohmic eff.
KlyC CST
92.66% 93.52%
91.75% 90.5%
“Public” value
Bunches profiles generated in CST 3D PIC gridded gun simulations.
MB tristron efficiency and collector beam power vs. output RF power. CST (circles) and KlyC (thin lines) results.

## Slide 11
avF=88.3%
avDF=88.1%
Temporal tristron efficiency
Accelerating cavities RF power modulation
MB tristron operational efficiency. FCCee Z-pole (RPO).
#1 Nominal operation (46kV)
#2 Single cavity failure mode (46kV)
Accelerating cavities RF power modulation
Cavity failure
avF=89.0%
avDF=87.8%
Temporal tristron efficiency
*By putting two tristrons on a single DC HV power supply, it will see almost constant in time power load.

## Slide 12
Tristron technology for FCCee 800MHz RF power sources
FCCee booster (Z,W,H) : 800MHz, 50kW
FCCee ttbar collider: 800MHz, 220 kW
400MHz gridded gun operated at 800MHz.
800MHz pulses, 1.3A average current. CST 3D PIC results.
800 MHz, 50kW tristron’s Single Beam RF circuit (0.35m long).
46kV
Peak efficiency/RF power vs. HV
88.2%, 56kW (46kV, 1.3A)
400 MHz gridded gun can be used effectively in the higher frequency devices (up to 1.5 GHz).
For the single beam devices, the gridded gun and input cavity particular layouts are not constrained. Thus, IOT vendors can procced with a retro-fit upgrade of the existing devices to boost the efficiency and RF power.
Due to the high bunch quality, tristron can be designed as an efficient frequency multiplier (x3), brining gridded tubes into S-band with an option of the continues wave operation.
Collector
RF power
Efficiency

## Slide 13
The MB tristron is selected now as a baseline for 400MHz 0.5MW, CW RF power source for the FCCee. It provides a high operational efficiency (almost 90%), compact (1.4m high and 1m in diameter) and cost-efficient solution.
Currently the MB tristron is under progressive development as CERN’s internal project, anticipating that the first prototype will be built and tested at CERN in 2028.
FCCee MB tristron is fully compatible/interchangeable with current LHC klystrons with minor modifications of HV circuit.
Tristron could be a technology of choice to improve overall efficiency of the high intensity and high-power proton SRF Linacs like ESS, MYRRHA and various Energy Recovery Linacs.
Summary