## Slide 1
Plasma-Column
Neutralization
in a Cyclotron Injection Line
Motivation • analytical model • WarpX/PIC simulation methods • result comparison plan
Prepared for internal discussion
Plasma-column neutralization in cyclotron injection line
01

## Slide 2
Why neutralization matters for cyclotron injection
Low-energy, high-current transport is dominated by space-charge defocusing.
proton beam
weak residual gas ionization
proton beam
electron–ion plasma column
Without sufficient neutralization
Large radial electric field from the beam core
Emittance growth and envelope mismatch
Aperture losses before the cyclotron inflector
Strong sensitivity to pressure, current, and chopping pattern
With controlled plasma column
Electrons partially cancel positive beam charge
Reduced tune depression and envelope growth
More robust matching into injection optics
A measurable path to model validation
Plasma-column neutralization in cyclotron injection line
02

## Slide 3
Concept: beam-driven ionization creates a local plasma column
The beam is both the source of space-charge and the source of neutralizing plasma.
proton beam
electron–ion plasma column
1
Primary beam
H⁺ beam propagates through H₂ background gas.
2
Ionization source
p + H₂ → p + H₂⁺ + e⁻ creates slow plasma species.
3
Confinement / loss
Electrons respond rapidly; ions and walls set the loss time.
4
Neutralized transport
Effective beam charge is reduced by fₙ.
Eᵣ,eff ≈ (1 − fₙ) Eᵣ,beam
K_eff = (1 − fₙ) K₀
Plasma-column neutralization in cyclotron injection line
03

## Slide 4
Analytical model: neutralized envelope dynamics
Use a reduced model to set scaling laws and sanity checks for PIC results.
Beam envelope with neutralization
R'' + k(s) R − ε²/R³ − K_eff/R = 0
K_eff = (1 − fₙ) K₀
K₀ = 2 I / (I_A β³γ³)
Neutralization build-up
dnₑ/dt = n_b n_g σᵢ(E_b) v_b − nₑ/τ_loss
dfₙ/dt = 1/τᵢ − fₙ/τ_loss
τᵢ = 1 / (n_g σᵢ v_b)
Interpretation
Pressure controls ionization time scale through n_g = P/kBT.
Cross-section table determines the absolute plasma source rate.
Loss mechanisms set the steady-state neutralization fₙ,∞.
Envelope data can infer an effective fₙ before full PIC validation.
Model limits
Assumes quasi-axisymmetric beam/plasma column.
Does not resolve non-neutral sheath, wall losses, or instabilities.
Needs PIC/MCC for transient and kinetic effects.
Plasma-column neutralization in cyclotron injection line
04

## Slide 5
Scaling expectation: pressure sets the neutralization time scale
Representative curves based on fₙ(t) = f∞[1 − exp(−t/τeff)]. Replace with measured or simulated rates.
Chart: Neutralization build-up vs. time
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
low pressure | 0 | 0.079 | 0.149 | 0.212 | 0.268 | 0.317 | 0.362 | 0.401 | 0.436 | 0.467 | 0.495
nominal pressure | 0 | 0.251 | 0.428 | 0.554 | 0.643 | 0.707 | 0.751 | 0.783 | 0.805 | 0.821 | 0.833
high pressure | 0 | 0.549 | 0.771 | 0.86 | 0.896 | 0.91 | 0.916 | 0.918 | 0.919 | 0.92 | 0.92
Design implications
Long injection pulses allow plasma to reach quasi-steady neutralization.
Short pulses or chopped beams can operate in a partially neutralized transient regime.
Pressure optimization is a trade-off: better neutralization versus gas load and beam–gas loss.
Diagnostics should resolve both fast build-up and slow recovery.
Replace with WarpX time histories
Plasma-column neutralization in cyclotron injection line
05

## Slide 6
Simulation hierarchy: three progressively self-consistent methods
A staged workflow separates fast design scans from full collision-model validation.
1. Seeded neutralization
Impose initial plasma or effective neutralization factor fₙ for fast optics scans.
2. Python callback source
Create e⁻/H₂⁺ pairs from local beam density using σᵢ(E) tables.
3. C++ BackgroundMCC
Production-quality ion-impact ionization process inside WarpX MCC.
Increasing physics fidelity
Use the seeded model to bracket possible neutralization factors and optics sensitivity.
Use the callback source to test rates, particle loading, and transient behavior without recompilation.
Use the C++ MCC model for scalable, reproducible simulation campaigns.
Plasma-column neutralization in cyclotron injection line
06

## Slide 7
Method 1 — seeded neutralization model
Fastest route for determining whether neutralization is required and how much is sufficient.
proton beam
electron–ion plasma column
Implementation idea
Initialize electron/ion populations around the beam, or scale the beam self-field by 1 − fₙ.
Scan fₙ = 0, 0.25, 0.5, 0.75, 0.9 to obtain an operating envelope.
No cross-section data are required; therefore this is a calibration and sensitivity model, not a source model.
Outputs
Envelope suppression versus fₙ
Transmission and aperture loss sensitivity
Back-calculated effective neutralization from measured beam sizes
Role in workflow
Defines target neutralization level for source models.
Provides a rapid benchmark for PIC/MCC consistency.
Useful for experiment planning and diagnostics placement.
Plasma-column neutralization in cyclotron injection line
07

## Slide 8
Method 2 — Python callback proton-impact source
Self-consistent particle source in WarpX without modifying the core C++ code.
ΔN_pairs ≈ n_b n_g σᵢ(E_b) v_b Δt ΔV / w
p + H₂ → p + H₂⁺ + e⁻
Algorithm loop
1
Deposit beam density n_b(x,y,z)
2
Read gas density n_g and σᵢ(E_b)
3
Sample ionization events per cell
4
Create e⁻ and H₂⁺ macroparticles
5
Advance all species with self-consistent fields
Strengths
Rapid prototyping
Transparent event-rate control
Good bridge between reduced model and compiled MCC
Risks to check
Particle noise from low-rate rare events
Time-step dependence of source sampling
Load balance when plasma becomes localized
Plasma-column neutralization in cyclotron injection line
08

## Slide 9
Method 3 — C++ ion-impact ionization BackgroundMCC process
Production implementation for reproducible, scalable simulation campaigns.
Input tables
H₂ cross section σᵢ(E)
beam ion species and energy
neutral gas density profile
Collision kernel
sample collision probability
spawn e⁻ and H₂⁺ products
conserve weights and metadata
PIC advance
deposit current/charge
solve fields
advance beam + plasma species
Validation criteria
C++ MCC and Python callback should agree for the same σᵢ(E), n_g, Δt, and particle weights.
Neutralization inferred from fields, species density, and envelope behavior should be mutually consistent.
Energy conservation and particle accounting should be tested in a fixed-cell benchmark before full beamline runs.
Best for final parameter scans and production runs
Plasma-column neutralization in cyclotron injection line
09

## Slide 10
Representative result: neutralization suppresses envelope growth
Illustrative plot for presentation structure — replace with final WarpX/beamline data.
Chart: RMS beam size through injection line
| 0.0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6 | 1.8 | 2.0
fₙ = 0.0 | 4 | 4.35 | 4.76 | 5.23 | 5.76 | 6.35 | 7 | 7.71 | 8.48 | 9.31 | 10.2
fₙ = 0.5 | 4 | 4.16 | 4.34 | 4.53 | 4.74 | 4.97 | 5.22 | 5.48 | 5.76 | 6.06 | 6.38
fₙ = 0.9 | 4 | 4.05 | 4.1 | 4.15 | 4.21 | 4.28 | 4.35 | 4.43 | 4.51 | 4.59 | 4.68
Interpretation
The final RMS size is strongly sensitive to the neutralization fraction.
If measured beam sizes fall between fₙ = 0.5 and 0.9 curves, the effective plasma density is already high enough to matter.
The same plot becomes a practical calibration target for WarpX and diagnostics.
Placeholder result
Plasma-column neutralization in cyclotron injection line
10

## Slide 11
Result comparison: what each method should reproduce
Use the seeded model as a reduced benchmark and test source models against density, field, and beam observables.
Observable
Neutralization fₙ(t)
Plasma density profile
Beam envelope / centroid
Particle accounting
Computational cost
Seeded model
prescribed
initialized
fast scan
not applicable
low
Python source
computed
self-consistent
PIC response
debuggable
medium
C++ MCC
computed
self-consistent
PIC response
production
lowest at scale
Primary comparison metrics
fₙ from charge density: 1 − ⟨nₑ⟩/⟨n_b⟩
fₙ from radial field: 1 − Eᵣ,eff/Eᵣ,beam
beam optics response: rms size, centroid, emittance, loss
Acceptance test
Python and C++ source models agree within statistical PIC noise.
Source rates scale linearly with pressure and cross-section table.
Beam transport agrees with seeded model at matching effective fₙ.
Plasma-column neutralization in cyclotron injection line
11

## Slide 12
Validation strategy: connect simulation outputs to beamline observables
Neutralization is not directly a single measurement; infer it from a consistent set of diagnostics.
Beam diagnostics
profile / wire scanner
slit-scan emittance
current transmission
Plasma diagnostics
residual gas pressure
collector / clearing electrode current
time response after beam on/off
Simulation probes
species density maps
radial electric field
ionization event rate
Effective neutralization target:
fₙ,beam ≈ fₙ,field ≈ fₙ,density
Plasma-column neutralization in cyclotron injection line
12

## Slide 13
Summary and next actions
A staged model hierarchy reduces risk before production-scale WarpX campaigns.
Key messages
Plasma-column neutralization can substantially reduce low-energy beam space-charge defocusing in a cyclotron injection line.
The reduced analytical model provides scaling laws for pressure, ionization rate, and envelope response.
Three simulation methods should be compared using the same cross sections, gas density, and beam parameters.
The final result should be validated using both plasma observables and beam transport observables.
Immediate next steps
1
Finalize H₂ cross-section tables
2
Benchmark single-cell ionization rate
3
Run pressure/current scan in seeded model
4
Compare Python and C++ source rates
5
Replace placeholder plots with simulation outputs
Backup: add detailed WarpX input decks and code snippets
Plasma-column neutralization in cyclotron injection line
13