## Slide 1: Progress towards the CERN Gamma Factory Proof of principle experiment
Aurélien MARTENS (IJCLab Orsay) on behalf of
The Gamma Factory study group

## Slide 2: Gamma Factory: Scientific context

## Slide 3: A striking fact
Weise, LINAC 2006 proceedings;
Few 100’s keV at most

## Slide 4: A striking fact
Weise, LINAC 2006 proceedings;
No bright photon source for nuclear and particle physics applications !
FEL and synchrotron impracticable
Inverse Compton scattering ?
Excellent monochromaticity but
O(1barn) cross-section is low !
10’s keV—100 MeV
ICS lie here
Example : HI𝛾S@Duke, 1010 ph/s, 1-100MeV

## Slide 5: Physics concept
💡: Exploit high cross-section of atomic resonances & existing CERN accelerator complex
E. J. Bessonov & K.J. Kim Phys. Rev. Lett. 76, 431, M.W. Krasny arXiv:1511.07794,
D Winters et al 2015 Phys. Scr. 2015 014048
Very similar with Inverse Compton scattering but O(109) larger cross-section !
PSI: Partially stripped ions
High-energy
Energy upshifting by a factor 4𝛾2
H-like Xenon at LHC (𝛾=3000)  180 MeV
Li-like Calcium at SPS (𝛾=130)  80 keV
For instance

## Slide 6: Physics concept
💡: Exploit high cross-section of atomic resonances & existing CERN accelerator complex
Very similar with Inverse Compton scattering but O(109) larger cross-section !
PSI: Partially stripped ions
High-energy
👍🏻 PSI recycling in ring is very efficient (relative energy loss << beam energy spread)
👍🏻 Energy tunability provided by PSI species choice and ion beam energy (<400MeV w/ LHC)
👎🏻 Laser wavelength must be « tuned » to PSI species and beam energy
👎🏻 Laser must be placed in a harsher environment (compared to e- accelerators)
E. J. Bessonov & K.J. Kim Phys. Rev. Lett. 76, 431, M.W. Krasny arXiv:1511.07794,
D Winters et al 2015 Phys. Scr. 2015 014048

## Slide 7: Beyond a bright photon source
High potential to open new opportunities in many branches of physics
M. W. Krasny et al. SPSC-I-253, M.W. Krasny arXiv:1511.07794, https://indico.mitp.uni-mainz.de/event/214/, https://indico.cern.ch/event/1096767
For a recent review, see Krasny, ICHEP 2025
Integrated in Physics Beyond Colliders initiative

## Slide 8: Laser cooling of ion beam
Potential for the first demonstration of laser cooling of relativistic ions (β ≈ 0.99)
Potential to improve beam quality in LHC-like collider conditions.
Simulation studies ongoing
  see D. Gamba’s presentation
Courtesy, P. Kruyt
Detuned laser spectrum
M. W. Krasny et al. SPSC-I-253

## Slide 9: Gamma Factory: Proof of Principle experiment @ SPS

## Slide 10: Proof of principle experiment location
5 m
LHC
SPS
Gamma Factory PoP
ATLAS
SPS
Laser room
Interaction region

## Slide 11: Optical system in SPS tunnel
M. W. Krasny et al. SPSC-I-253
5mJ 40MHz (200kW) laser system
Laser Room
Challenges:
Laser beam transport
Full remote operation

## Slide 12: Laser beamline
Measured the vibration spectral content during 6 hours with SPS equipment switched ON.
Accuracy was down to few pm in length and up to 10 kHz in frequency.
Largest contributions are acoustics below 1 kHz, with eventual tones at 2.3 kHz.
Avoid the coupling of vibrations to laser beamline and with a Fabry-Perot cavity resembling the future experiments
© Yann Dutheil
Supported by Physics Beyond Colliders at CERN

## Slide 13: Pillar preparation
TI 18
SPS Beam Line
350 mm
Hole between
SPS and TI 18
SPS
GF Laser
Beam Line
Pillar
Busbars
GF Cavities
350 mm
Supported by Physics Beyond Colliders at CERN

## Slide 14: Pillar support simulations
Mismatch to SPS vibration spectrum
Analysis of resonant modes without attachment to ceiling.
All the contacts are bonded. No additional mass on the structure was considered
The modes are mismatched to the existing vibrational modes found in SPS
Fixed supports
Supported by Physics Beyond Colliders at CERN
First element installed in SPS (Jan’25)

## Slide 15: Fabry-Perot preparation
Pre-design was done by IJCLab
CERN is preparing the engineering design, possibly ready for procurement in 2026
Supported by Physics Beyond Colliders at CERN

## Slide 16: Optical Cavity for Gamma Factory PoP
Optical system scheme: 2-mirror optical cavity coupled to the storage ring
Parameter design :
  FSR = 40 MHz
  Cavity Linewidth = 4 kHz
  Finesse = 10,000
  Gain = 5,000
  Amplified power = 50 W
  Coupling efficiency = 70%
  Circulating power = 180 kW
Fully remote operation is needed
M. W. Krasny et al. SPSC-I-253; A. Martens, et al. PRAB 25.10 (2022): 101601.

## Slide 17: Fabry-Perot interferometric filter
Laser frequency must be precisely tuned
And remain stable !
NB: Compare with central frequency of
Metrology-level requirement !
careful choice of laser provider
First difficulty
A. Martens, et al. PRAB 25.10 (2022): 101601.
E. Roikova et al., APL Photonics 10, 070901 (2025)

## Slide 18: Phase noise: choice of provider
Laser provider identified, laser oscillator procured (160MHz)
(Very) good laser
Example of (very) bad laser
A. Martens, et al. PRAB 25.10 (2022): 101601.
Supported by Physics Beyond Colliders at CERN

## Slide 19: Amplifier choice - neoLase
Amplifier procured, delivery end 2025
Requires validation on cavity
Supported by Physics Beyond Colliders at CERN

## Slide 20: 2-mirror cavity demo
Finesse 45,000
Effective enhancement 18,000
700 kW
216 MHz
X.Y. Lu, et al. Appl. Phys. Lett. 124, 251105 (2024)
X.Y. Lu, et al. Optics Letters 49 (2024) 6884
Uses GF-Pop seed laser
Amplifier is R&D
in collaboration with Tsinghua University, Dpt of Engineering Physics
NB: amplifier used not that of GF-PoP

## Slide 21: Coupling difficulties
Transmission camera beam size
Lensing also occurs in input mirror (Suprasil 3001) similarly as in output coupler
Thermo-optic coefficient are similar
Strong mode mismatching at high power
Mode mismatching at low power can improve at high power depending on telescope setting
X.Y. Lu, et al. Optics Letters 49 (2024) 6884
in collaboration with Tsinghua University, Dpt of Engineering Physics
NB: amplifier used not that of GF-PoP
Expect new results from Tsinghua soon (context of SSMBDENG X. presentation later this week)

## Slide 22: Stability
Excellent overall stability
Limited by amplifier pump diodes temperature rise at high power
Limited by the need to manually tune one laser piezo voltage (can be automatized)
X.Y. Lu, et al. Appl. Phys. Lett. 124, 251105 (2024)
in collaboration with Tsinghua University, Dpt of Engineering Physics

## Slide 23: Conclusion/Prospects
The Gamma Factory proof of principle experiment is a laser cooling experiment for the CERN SPS ion beam
Comprehensive physics program beyond the Proof of Principle experiment
Evident progress towards implementation over the past few years
Hardware validation obtained at Orsay with parameters scalable to GF-PoP design
World record in stored laser power in the long term
Expect the laser system to be ready in 2026
Fabry Perot could be procured in 2026
Project on schedule for experiment start in 2028

## Slide 24: Beam size in transmission
Transmission camera beam size
Lensing in transmission of the the output mirror (ULE) !!!
NB: cavity beam mode nearly unaffected.
at 700kW
Cannot be explained simply with a ROC change !!!
Assuming known material parameters (subject to systematic uncertainties) allows to estimate coating absorption ppm
w~0.6mm
X.Y. Lu, et al. Optics Letters 49 (2024) 6884
in collaboration with Tsinghua University, Dpt of Engineering Physics
NB: amplifier used not that of GF-PoP

## Slide 25: Current situation
Parameter | R&D | ThomX | GF-PoP design
Frequency | 160 MHz | 33.3 MHz | 40 MHz
Finesse | 35000 | 30000 | 10000
Linewidth | 4.5kHz | 1.3kHz | 4kHz
Amp. power | 75 W | 16 W* | >50 W
Cavity power | 520 kW | 80 kW | >200 kW
Coupling | 70% | 30 % | 70%
Pulse duration | 160 ps | 5 ps | 1-10 ps
We continue to learn and plan to increase power gradually in 2024-2025. We still learn from operation in accelerator at high power with this 4-mirror geometry:
Drift of cavity length correlated with stacking of pulses in cavity  thermally induced ?
Dynamics is complicated but we manage to preserve lock of laser-cavity-RF by sliding the stepper-motors slowly without loss of lock ! (was not observed at KEK-ATF with 30kW)
It is the main point of attention for GF-PoP (+laser transport)

## Slide 26: R&D setup: 4 mirror cavity
520 kW
in collaboration with Tsinghua University, Dpt of Engineering Physics
NB: amplifier used not that of GF-PoP
Finesse 35,000
Effective enhancement 8,000
ULE mirrors (M234)
Suprasil input mirror (M1)
X.Y. Lu, et al. Appl. Phys. Lett. 124, 251105 (2024)
X.Y. Lu, et al. Appl. Phys. Lett. 124, 251105 (2024)

## Slide 27: Fabry-Perot resonator
Trep=1/Frep
Input laser beam must be matched to the cavity:
Temporal superposition
Transverse mode matching
Resonant at different cavity lengths*
*for a non-degenerate cavity
Input laser beam:
Few ps pulse duration
L
2L/c=Frep

## Slide 28: Back in 2020: modal instabilities
But unstable at high-power
High-order mode instability
Highly sensitive to cavity topology
Rough understanding from simple simulations
 HOM damping with additional D-cut mirrors in cavity
Favier P., Amoudry L. & H. Wang, PhD theses

## Slide 29: Back in 2020: D shape mirrors
But unstable at high-power
High-order mode instability
Highly sensitive to cavity topology
Rough understanding from simple simulations
 HOM damping with additional D-cut mirrors in cavity
Favier P., Amoudry L. & H. Wang, PhD theses
Introducing losses to HOM

## Slide 30: Stability
Excellent overall stability
Limited by amplifier pump diodes temperature rise at high power
Limited by the need to manually tune one laser piezo voltage (can be automatized)
X.Y. Lu, et al. Appl. Phys. Lett. 124, 251105 (2024)
in collaboration with Tsinghua University, Dpt of Engineering Physics

## Slide 31: Beam mode
0.85 mm/MW
0.02 mm/MW
Carstens, Optics letters 39.9 (2014): 2595-2598.
Lower mode size increase
(than legacy work from Munich group)
Much smaller coating’s residual absorption
Can be “tuned” by choosing distance between spherical mirrors
Iterative numerical calculation since w depends on ROC R, which depends on
main approximate effect: ROC change
X.Y. Lu, et al. Appl. Phys. Lett. 124, 251105 (2024)
in collaboration with Tsinghua University, Dpt of Engineering Physics

## Slide 32: Coupling issues
Ideal waist size and position for perfect mode matching strongly evolves with stored power
Acceptable region to obtain small (<10%) residual mode mismatching gets extremely tight at high stored power
 Adaptative telescope ?
X.Y. Lu, et al. Optics Letters 49 (2024) 6884