## Slide 1: A Neutral Hydrogen Monitor for Electron Cooling Studies of H- ions in ELENA
Gérard Alain Tranquille
SY Department, CERN

## Slide 2: Why?
For commissioning at 100 keV with the proton source, optimisation of the electron cooler can be performed by measuring the recombination of electrons with the circulating protons.
The proton source has never been used on ELENA
H- ions are injected for machine studies and commissioning experimental hardware
Stripping of H- ions with the residual gas and cooling electrons gives some insight into machine performance

## Slide 3: Hardware

## Slide 4: Beam Profiler
Chevron mounted MCP detector
MgO coating
Fibreoptic phosphor screen with P43
Direct image of cooled beam on CMOS camera

## Slide 5: Camera System
Raspberry Pi HQ camera module
Sony IMX477 12 megapixels CCD
CS mount lenses: Fujion 25 mm
Rpi 6 mm wide angle

## Slide 6: Controls & Data Acqusition
Raspberry Pi4 8GB micro computer
Direct control of HQ camera
Pi Pico & 10-DOF IMU Sensor Module (B field monitoring)
Control of high voltage power supplies via USB/ethernet

## Slide 7: Software

## Slide 8: Camera & PS Control S/W
Python script for the camera settings and still/video capture
Script for the control of the iSEG high voltage power supply (mcp and P43 settings)

## Slide 9: Offline Analysis S/W
Data analysis s/w in Python:
video playback
frame by frame analysis
position, size & stripping rate evolution
More detailed analysis with FlexPro 8

## Slide 10: Measurements
H- beam scanned in position and angle on the two cooling plateaus
Some scans in electron beam position, intensity and electron beam expansion

## Slide 11: ELENA Magnetic Cycle
AD cycle length 110 s
ELENA cycle length 15 s

## Slide 12
Can insert up to 7 ELENA H- cycles per AD cycle
Stripping due to cooling electrons clearly seen

## Slide 13: A Typical ELENA Cycle
Inj: 100 keV
5.3 MeV
368 keV
100 keV

## Slide 14
Selective analysis is needed to obtain the beam evolution on individual plateaus

## Slide 15: Initial Machine Parameters
H- momentum (MeV/c) | Vcath (V) | Vgrid (V) | Ie (mA) | BUMPH | ANGLEH | BUMPV | ANGLEV
35 | -368.86 | -300 | 4.45 | 3.4 | 1.4 | 4.0 | 0.5
13.75 | -57.62 | -50 | 0.35 | -0.4 | -3.8 | 4.2 | -3.8

## Slide 16
Horizontal Position Scan at 35 MeV/c
Horizontal position of the H- beam bumped in (programmed) 1 mm steps (-5.6 mm to +7.4 mm)

## Slide 17
Revolution frequency vs beam position measured with the longitudinal Schottky monitor
Measured position change vs programmed position bump
Revolution frequency vs measured H0 horizontal position

## Slide 18
Stripping rate as a function of horizontal offset (BUMPH)
Beam size evolution f horizontal offset (BUMPH)

## Slide 19
Measured angle change vs programmed angle bump
Horizontal Angle Scan at 35 MeV/c
Horizontal angle of the H- beam bumped in (programmed) 0.5 mrad steps (3.4 mrad to -0.6 mrad, initial angle = 1.4)
Beam size evolution f horizontal angle (HANGLE)

## Slide 20: Vertical Position Scan at 35 MeV/c
Verticalal position of the H- beam bumped in (programmed) 1 mm steps (-5 mm to +5 mm)
Measured position change vs programmed position bump
Revolution frequency vs measured H0 vertical position

## Slide 21
Stripping rates as a function of vertical offset
Beam size evolution f vertical offset (BUMPV)

## Slide 22: Ie Scan at 13.75 MeV/c
Cooler voltage settings
Vcath (V) | Vgrid (V) | Ie (uA)
-57.62 | -50 | 348
 | -48 | 407
 | -46 | 460
 | -44 | 520
 | -42 | 590
 | -40 | 650
-60.32 | -40 | 750
Beam size evolution for varying electron currents

## Slide 23
Horizontal plane Ie = 348uA
Horizontal plane Ie = 520uA
Vertical plane Ie = 520uA
Vertical plane Ie = 348uA

## Slide 24: Electron Detachment Cross Section of H- Studies
After the end of cooling at 13.7 MeV/c, the beam is bunched (to have an intensity measurement) and then the cooling is switched on again.
e- ON
Ref.
ref

## Slide 25
Scan of Vcath with Vgrid fixed at -50V
Scan of Vgrid (Ie) with Vvath fixed at -127.62V

## Slide 26: Conclusions and Outlook
H0 monitor has been shown to be a useful tool to optimise the ELENA electron cooler
It is the only non-destructive instrument for beam size measurements on ELENA
However, measurements can only be made during dedicated machine experiment sessions due to the non-ppm power supplies used for the cooler
The preliminary measurements on the beam alignment indicate that there is definitely room for improvement
This needs to be confirmed with antiprotons (scraper measurements)
Influence on electron current and beam expansion needs to be further addressed
Electron detachment cross-section measurements will be investigated in more detail
The camera will be replaced with a standard SY/BI system and ported to the main control system during the next shutdown