## Slide 1: Ion machine gun experiment at Hiroshima University
Kento Muroo, Kiyokazu Ito, Hiromi Okamoto, Koichi HosakaA, Yosuke YuriA, Nobumasa MiyawakiA
Graduate School of Advanced Science and Engineering, Hiroshima University
A Takasaki Institute for Advanced Quantum Science (QST)
This work is supported in part by JSPS KAKENHI Grant No. JP24KJ1723 and JP25K15770, and by JST, the establishment of university fellowships towards the creation of science technology innovation, Grant No. JPMJFS2129, and Moonshot R&D Grant No. JPMJMS2062.
COOL’25 @Stony Brook Univ.

## Slide 2: Outline
Introduction
Approach for nanobeam generation
Numerical Simulation
Experiment
  Setup
  Forming a two-component crystal
  Slow extraction
  Single ion extraction
Summary

## Slide 3: Introduction What is the “Ion Machine gun?”

## Slide 4: Microbeams
+
+
+
-
-
-
Biological response to radiation in cells
Errors caused charged particles entering semiconductor
Semiconductor
+
Ion source
Collimator
Focusing lens
Target
To realize “nanobeam”, reducing emittance is important!
Various types of charged particle beams are used depending on their purpose
Microbeams: the beam focused down to the micrometer scale
Application examples

## Slide 5: Coulomb crystal
Ions form a “Coulomb crystal”
Ions confined in a trap are cooled near absolute zero
String（6 Ca⁺ ions）
Zigzag（9 Ca⁺ ions）
Shell（~100 Ca⁺ ions）
High
Low
Images of Coulomb crystals consisting of
Line density
Linear Paul Trap(LPT)
The emittance of a Coulomb crystal is extremely low.
If ions can be extracted without heating, they can be used as an ultra-low emittance ion source!

## Slide 6: Nanobeam generation
By extracting ions from a Coulomb crystal formed in an LPT, a nanobeam can be generated.
If a string crystal is extracted from an ion trap as is, we can obtain a unique beam; ions arrive at almost equal time intervals with high positional precision.…Ion Machine Gun
Even zigzag or shell crystals can also be used as ion sources.
We are conducting research and development to generate a nanobeam applying the Ion Machine Gun idea. （cf. Presentation by Y. Yuri, MOD2）
Linear Paul trap
Focusing Lens
Target
Coulomb crystal

## Slide 7: New approach for nanobeam generation

## Slide 8: How to generate a low emittance beam
Primary method used to cool ions for Coulomb crystallization …Doppler laser cooling
Cool ions by repeating excitation of ions and photon emission from ions
Cool to mK ～μK
Non-destructive measurement by observing the emitted photons is possible.
Directly laser-coolable ion species are limited
Sympathetic cooling
Cool ions through the interaction with already cooled particles
Cool to the same order with laser-cooled ions, through the interaction with them
All ion species can be cooled
By extracting ions from a Coulomb crystal containing sympathetically cooled ions, ultra-low emittance beams of any ion can be generated.
To make non-laser-coolable ions into a Coulomb crystal…

## Slide 9: For the precise extraction of a nitrogen ion
Previous study … ”Fast extraction scheme”
Rapidly lowering the voltage applied to the end plate electrode on the extraction side to eject the ions
[1] K. Groot-Berning et al., New J. Phys. 23, 063067 (2021).
Extraction of the sympathetically cooled nitrogen ions from a two-component Colomb crystal with very low emittance
Why nitrogen？
Potential
  Application for quantum techniques (cf. diamond NV centers)
  Easy to introduce
Ca+ ions
N2+ ion
A previous study[1] has successfully extracted sympathetically cooled nitrogen ions using this method.

## Slide 10: Problems for the fast extraction scheme
Problem
The nitrogen ion will be heated during extraction unless it is put at the head of the crystal
A filtering system is required to remove the coolant calcium ions
Potential
Nitrogen ion
Calcium ion
Ca+ ions
N2+ ion

## Slide 11: To put a nitrogen ion at the head of a crystal
Difficult to intentionally put a nitrogen ion at the head of a string crystal
Extract an ion from a shell crystal
Ions that have the smaller mass-to-charge ratio gather near the trap axis in the two-component Coulomb crystal. [2]
ex. Two-component shell crystal consisting of 40Ca+and 14N2+
[2] L. Hornekær, N. Kjærgaard, A. M. Thommesen, and M. Drewsen, Phys. Rev. Lett. 86, 1994 (2001).
Nitrogen ion is at the head

## Slide 12: Slow extraction scheme
Slow extraction scheme:
“Push out” the head ion from two-component crystal
Potential
Detector
Calcium ion
Nitrogen ion
We have demonstrated this “Slow extraction scheme” in numerical simulation and experiments.
Filtering system is no longer needed
Even a single ion can be extracted

## Slide 13: Numerical Simulation

## Slide 14: Numerical simulation
Conduct simulations using 3D molecular dynamics code
Extract a nitrogen ion from a two-component crystal by raising VA
RF amplitude | 30 V
RF frequency | 2 MHz
End voltage VA | 3.0 V
End voltage VB | 3.0 → 142.35 V
Number of Ca+ | 20
Number of N2+ | 5
Voltage
3.0 V
142.35 V
Detector
10 ms
VB
VA
Similar simulations are conducted in
[3] K. Muroo, H. Okamoto, N. Miyawaki, and Y. Yuri, Pro. Theor. Exp. Phys.(2023),063G01.

## Slide 15: Results of the single ion extraction simulation
Slow extraction scheme enables the extraction of single nitrogen ions with extremely low emittance.
Projected root-mean-square emittance
x: 6.6×10-16 m·rad
y: 5.9×10-16 m·rad
Distribution at the detector

## Slide 16: Experiment

## Slide 17: Overview of experimental system
Laser diodes
Vacuum chamber
CCD camera
Variable leak valve

## Slide 18: Inside the chamber
LPT
Ca atomic oven
Detector (Channeltron)
Lasers
*Similar system is available at QST.

## Slide 19: Formation of a Ca-N2 Coulomb crystal
Procedure
Emit Ca atoms
Ionize and capture calcium and nitrogen
Laser cool Ca ions
Sympathetically cool nitrogen ions
→Form a two-component Coulomb crystal
Introduce nitrogen gas
()
RF amplitude | 20 V
RF frequency | 2 MHz
End voltage | 1.5 V
Ca
atomic oven
e-gun
Cooling Lasers
LPT
Two-component Coulomb crystal
Nitrogen gas
CCD camera

## Slide 20: Process of two-component crystal formation
×4 speed
1.3 mm
Dark ions are inside
→ Ions which do not emit fluorescence and have a smaller mass-to-charge ratio than 40Ca+ ions
→ Nitrogen ions are included
Fluorescence from 40Ca+

## Slide 21: Comparison with simulation
 | Experiment | Simulation
RF amplitude [V] | 20 | 20
RF frequency [MHz] | 2 | 2
End voltage [V] | 1.5 | 1.1
Number of 40Ca+ ions | ? | 80
Number of 14N2+ ions | ? | 30
Distribution |  | 
Formation of a two-component shell crystal was successful
This crystal consists of approximately 80 calcium and 30 nitrogen ions

## Slide 22: Slow extraction experiment of a shell Coulomb crystal
RF amplitude | 30 V
RF frequency | 2 MHz
End voltage VA | 0.5 V
End voltage VB | 0.5 → 30 V
Detector voltage | −2.19 kV
Rump-up time | 10 ms
7.1 mm
20.55 mm
Count the number of detected ions
End electrodes
Detector
1
2
Ion
……
Detector
Applied voltage
30 V
0.5 V
10 ms
VB
VA

## Slide 23: Estimation of the number of ions in a shell crystal
 | Experiment | Simulation
RF amplitude [V] | 30 | 30
RF frequency [MHz] | 2 | 2
End voltage [V] | 0.5 | 0.3
Number of ions | （Detected）47 | 50
The number of ions predicted by simulation matches the number detected.
We confirm successful extraction of all ions in a crystal using the “Slow extraction” scheme.

## Slide 24: Partial extraction of a shell crystal
RF amplitude | 30 V
RF frequency | 2 MHz
End voltage VA | 0.5 V
End voltage VB | 0.5 V → Vstop
Rump-up speed | 2.95 V/ms
Detector voltage | −2.19 kV
End electrodes
7.1 mm
20.55 mm
Detector
Applied voltage
30 V
0.5 V
Vstop
VB
VA
30 V
0.50 V
Time
Vstop =
3.63～6.70 V
2.95 V/ms
Applied voltage
= 1.4~2.9 ms
…
Full
Partial
None
Extraction level
VB
VA

## Slide 25: Control of the number of extracted ions
Detected ions
Final End voltage Vstop [V]
The number of ions ejected from the shell crystal can be controlled by the voltage after raising
Partial extraction from the shell crystal by “pushing-out” has been demonstrated.
Example of an extracted crystal
100 µm
3 experiments at each voltage

## Slide 26: (Preliminary)

## Slide 27: (Preliminary)

## Slide 28: Summary
We are conducting research on methods for generating nanobeams using Coulomb crystals.
Slow extraction scheme —to carefully raise the end plate voltage at the opposite extraction direction — enables a unique beam, which consists of only a single ion with extremely low emittance.
Through numerical simulations, we confirmed that the high-precision extraction of single nitrogen ions is possible using the slow extraction scheme from a two-component shell Coulomb crystal.
Experiments are in progress for proof-of-principle of:
  Formation of a two-component Coulomb crystal
  Partial extraction from a shell crystal
  Single calcium ion extraction from a string crystal
Future plans
  Single nitrogen ion extraction will be conducted.