## Slide 1: Results of the Coherent electron Cooling experiment at RHIC
Vladimir N Litvinenko, for CeC project team:
Nikhil Bachhawat, Jean Clifford Brutus, Yichao Jing, Dmitry Kayran, Jun Ma, Igor Pinayev, and Gang Wang
Stony Brook University and Brookhaven National Laboratory
COOL’25 Workshop, Stony Brook University, NY, USA – October 27, 2025

## Slide 2: What is Coherent electron Cooling (CeC)
It is stochastic cooling of hadron beams with bandwidth at optical wave frequencies: 1 – 1000 THz. All CeC systems are based on the identical principles:
  Hadrons create density modulation in co-propagating electron beam
  Density modulation is amplified using broad-band (microbunching) instability
  Time-of-flight dependence on the hadron’s energy results in energy correction and in the longitudinal cooling.
  Transverse cooling is enforced by coupling to longitudinal degrees of freedom.
Imprint by hadrons
Momentum correction
Amplification

## Slide 3
S. van der Meer
1984 Nobel physics prize
S. van der Meer, Rev. Mod.Phys. 57, (1985) p.689
S. van der Meer, 1972, Stochastic cooling of betatron oscillations is ISR, CERN/ISR-PO/72-31
Critical conditions for the stochastic cooler
Linearity: Amplifier must be linear (no saturation) and low noise
Overlapping: Amplified signal induced by individual particle in the modulator (pick-up, sensor) must overlap with the particle in the kicker
Bandwidth: Cooling decrement per turn can not exceed 1/Ns, where Ns is number of the particles fitting inside the response time of the system: τ~ 1/Δf
Noise: noise in the system should not significantly exceed system signal introduced by shot noise in the hadron beam
RF stochastic cooling is reaching its limits at ~ 10 GHz bandwidth
Notes: Can it work for a bunched beam?

## Slide 4: CeC schemes
Plasma cascade
micro-bunching amplifier
Litvinenko, Derbenev, PRL 2008
Ratner, PRL 2013
Litvinenko, Wang, Kayran, Jing, Ma, 2017
High gain FEL amplifier
Multi- Chicane
Microbunching amplifier
Plasma-Cascade Microbunching amplifier
Can be tested experimentally at RHIC
Cooling test would require significant modification of the RHIC lattice & superconducting magnets
Linearity: Amplifier must be linear (no saturation) and low noise
Overlapping: Amplified signal induced by individual particle in the modulator (pick-up, sensor) must overlap with the particle in the kicker
Bandwidth: Cooling decrement per turn can not exceed 1/Ns, where Ns is number of the particles fitting inside the response time of the system: τ~ 1/Δf
Noise: noise in the system should not significantly exceed system signal introduced by shot noise in the hadron beam

## Slide 5: What is PCA? : Parametric instability caused by strong transverse focusing
Results of 3D simulations
with code SPACE
Current
experiment
CeC for
275 GeV
EIC
“Standard” 4-cell PCA
Optimized PCA cell
Simulations of Coherent Electron Cooling with Two Types of Amplifiers, Jun Ma, Gang Wang, Vladimir Litvinenko, International Journal of Modern Physics A (IJMPA), Vol. 34 (2019) 1942029 (
Plasma-Cascade micro-bunching Amplifier and Coherent electron Cooling of a Hadron Beams, V.N. Litvinenko, G. Wang, D. Kayran, Y. Jing, J. Ma, I. Pinayev, arXiv preprint arXiv:1802.08677, 2018
11
Cell
PCA Gain per cell

## Slide 6: What is Plasma-Cascade Instability (PCI)? How is it different from the previously known micro-bunching instability (MBI)?
MBI
© D. Ratner
Interaction
Drift
Drift
Kick
Kick
Interaction
Drift
Kick
Drift
Kick
Drift
Kick
Dispersion
Dispersion
Dispersion
R 56 =Ld/γ2
R56=Lbθ2
Modulate beam density by
changing beam radius
a(s)
MBI: modulate effective mass (s-mobility) by bending beam trajectory (θ)
PCI
CeC
accelerator
PCI experiment
LCLS
Both instabilities can be used a broad-band amplifier in CeC
Longitudinal position, psec
0
5
5
8

## Slide 7: CeC X at RHIC
2014-2017: built cryogenic system, SRF accelerator and FEL for CeC experiment
2018: started experiment with the FEL-based CeC. It was not completed: 28 mm aperture of the helical wigglers was insufficient for RHIC program with low energy 3.85 GeV/u Au ion beams
We discovered microbunching Plasma Cascade Instability - new type of instability in linear accelerators. Developed design of Plasma Cascade Amplifier (PCA) for CeC
In 2019-2020 a PCA-based CeC with seven solenoids and vacuum pipe with 75 mm aperture was built and commissioned. During Run 20, we demonstrated high gain Plasma Cascade Amplifier (PCA) and observed presence of ion imprint in the electron beam
We observed regular e-cooling in Run 21, but CeC cooling was washed out by large timing jitter of the seed laser and resulting 0.35% RMS e-beam energy jitter

## Slide 8: Unique SRF accelerator and CeC amplifier
1.25 MV SRF
photoelectron gun
10-20X
ballistic bunch compression
13 MV SRF linac
Time-resolved diagnostics beamline
CeC section – common with RHIC ion beam
4-cell Plasma-Cascade Amplifier
Modulator
Kicker
Bunching cavity

## Slide 9: Main results obtained up to the date
We observed high gain in FEL system used for early version of CeC
We observed imprint of ion beam in the electron beam radiation
We observed high PCA gain at frequencies between 5 and 10 THz
We observed regular electron cooling – albeit very week – of 26.5 GeV/u ion beam – the highest energy electron cooling
We observed recombination between elections from CeC accelerator and 26.5 GeV/u ions
Beam parameters are either on the target – we are ready for CeC demonstration
Imprint of ion beam
Exponential rise of PCA gain
Recombination signal

## Slide 10: New mode of operation for Run 25
To maximize chances for success, we developed new mode of operation below the RHIC transition energy.
Lower energy of operation would provide for better quality of ion beam, easier choice for electron beam parameters and better stability
This mode of operation would also provide for significantly faster cooling
We plan to cool low intensity ion bunches to speed-up the studies
Simulation of cooling on the bunch with 2x108 ions
after 4 minutes
after 8 minutes

## Slide 11: Simulations are goon but experimental data is more important: CeC operates with electron beam beam parameters equal to better than the requirements: sample from September 18, 2025
Δγ/γ =3.5 10-4
Time, psec
0
70
γ
Δγ/γ=10-4
Required: εnorm < 1.25 μm
0.807 μm
0.903 μm
0.946 μm
Peak current: >20 A

## Slide 12: CeC guts: Plasma-Cascade Amplifier (PCA)
Plasma-Cascade Amplifier
Modulator
Kicker
RHIC Yellow
Ion beam
Electrons
RHIC Yellow
Ion beam
Electrons
THz radiation
Plasma-Cascade Amplifier is a parametric amplifier: strong focusing solenoids caused periodic modulation of the beam radius and corresponding modulation of plasma frequency. It results in exponential growth of density modulation induced by ions in the modulator.
Classical PCA: changing strength of PCA solenoids result in dramatic increase of the THz radiation: September 22, 2025
Current in PCA
solenoids
Measured THz power a.u.

## Slide 13: Conclusions
Demonstration of Coherent electron Cooling remains a very challenging endeavor
All main components of the CeC process were successfully demonstrated:
  Ion’s imprint into the e-beam density modulation
  High gain Plasma-Cascade Amplification of the e-beam noise (and ion imprint)
  Recombination of ions and electrons with matched relativistic factors
All beam parameters necessary for CeC demonstration are demonstrated
  More details are in THA1, THA2 and THA3 talk on Thursday morning by Yichao Jing, Jun Ma and Gang Wang
The CeC accelerator performance is sufficiently stable
We are ready for CeC demonstration
The main challenge is allocation of dedicated time with ion beam for CeC project
  In last 3 years CeC has 3.5 hours of time with ion beam at CeC energy
  This is the last RHIC run and CeC system will be taken apart after the run ends
  Two detectors are completing their physics program and ego to use every hour of RHIC operation
  We are not giving up hope and exploring every possibility for a limited number of shifts for CeC demonstration
I want to thank everybody who participated and participating in CeC project: RHIC operators, colleagues from Accelerator Physics, RF, Vacuum, Instrumentation, Cryogens, Control, Mechanical systems and ES&F division, cathode team from Instrumentation Department, as well as the CeC operation team, for their dedicated and steadfast support of our attempt to demonstrate this stubbornly resisting phenomenon

## Slide 14: Thanks to all involved in the CeC project
… never can get all of your photos…

## Slide 15: Back-ups

## Slide 16
No overlap (50 ns, 2 mV per division)
e-beam
Synchronization was achieved by observation of the signal from the BPM pick-up electrode in the FEL section.
Overlap (20 ns, 10 mV per division)
Ion beam
e-beam
Ion beam

## Slide 17: The Ion Imprint studies: Run 2020
Typical “good” measurement:
4 cycles with 500 measurements each
Upstream
Downstream
Downstream IR diagnostics
10 m from the radiation point
We observed clear presence of the ion imprint in the electron beam resulting in increase of the e-beam radiation at 35 μm with average imprint of
We applied PCA to boost radiation at 35 μm at the level detectable by current IR detectors after the spectrometer
✔

## Slide 18: Recombination of electrons with Au ions: Run 2021
Experiment
FWHM, 4%
Resolution
Triangular shape of the measured dependence allows to define matching of the relativistic factors with accuracy ~ 0.2%, which is significantly smaller than 4% FWHM.
This finding will reduce the range where we need to search for the CeC signature by 5-to-10 fold.
(γe-γi)/γi
Calculations
© of G. Wang
This results include convolution of the exact formula recombination cross-section (in the commoving frame) with distributions of two beams

## Slide 19: Diagnostics undulator and cryo-cooled IR detector
Parameter | Value | Units
Period | 8 | cm
Gap | 7.9 | cm
Peak field | 0.6 | kGs
Radiated power at 50% beam current | 4 | nW
Fundamental wavelength @ γ=19.57 | 115 | μm
Central frequency @ γ=19.57 | 2.6 | THz
Third harmonic | 7.8 | THz
F3/F1 | 0.04 | 
Cryo-cooled and Golay IR detectors
Undulator generates radiation at 7.8 THz harmonic frequency, which is within the bandwidth of the Plasma-Cascade Amplifier (PCA)
This system allow us to optimize the PCA gain

## Slide 20: Time-resolve diagnostics beam-line: the key for accurate measurements of beam parameters

## Slide 21: Search for CeC signature and observation of regular bunched electron cooling of 26.5 GeV/u Au ion beam
Changing e-beam energy requires multiple adjustments
120 μA
SRF linac voltage
No cooling
e- cooling
cooling
Ion beam trajectory radius
Bunch length
Adjusting ion beam energy – 1 mm xmean corresponds to 0.1% change in the ion beam energy.
There was no attempt of improving regular non-magnetized electron cooling – we used the lattice optimized for PCA CeC - and the best electron cooling rate was ~ 100 hours. It is consistent with cooling rate estimation made by Dmitry Kayran and 90 hours cooling rate simulated by He Zhao
There is one exception – on the 4th of July CeC evening shift we observed cooling rate of 16 hours: this event is possibly a first indication of the CeC cooling, but it is not conclusive

## Slide 22: PCA CeC simulations: slice by slice, ion by ion
Simulations of electron beam are down using Impact T/Z code (Y. Jing, K. Shih) provide distribution of electron beam at the entrance of the CeC section
This information is used to simulate interaction of ions with individual slices: PCA gain and kick to ions is calculated as function arrival time and transverse position of ion (SPACE code, J. Ma)
This information is used used to simulate evolution of cooled ion bunch (G. Wang and his code) and compare it with reference (non-interacting) bunch
This is work in progress and preliminary findings will be reported at C-AD MAC next week by Dr. Gang Wang

## Slide 23: How PCA gain is measured?
IR Mirror
We used IR radiation from the bending magnet at the exit of the CeC section. Critical frequency of synchrotron radiation from the bending magnet is 0.4 THz
PCA gain peaks at 12THz and there is no gain below 3 THz
IR radiation is intercepted by 2” mirror 10 meters downstream
For there measurements, the radiation was delivered to two most sensitive IR detectors: broad-band Golay cell or cryo-cooled Bolometer.
IR filter with passband of 3.5-10 THz was used in front of the Golay cell to improve sensitivity at high frequencies (see next slide)
Signal from Golay cell was detected by lock-in amplifier synched with the electron bunch pattern (typically 5 Hz, five 100 msec bunch trains per second). We used 3rd order modulation-demodulation (MDM) technique to remove background unrelated to IR radiation, by periodically blocking IR using Mirror 1.
Signal from Bolometer was delivered in unsynchronous mode (140 kilo-samples per second) with respect to electron beam pattern. Analog signal was not available. We developed MatLab application for asynchronous detection of this digital pattern.
PCA gain was evaluated by comparing radiated power in the PCA lattice (strong solenoids) with relaxed lattice (weak solenoids) using the same setting of the CeC accelerator and the electron beam
Mirror 1
IR filter
Bolometer
Golay cell
10 meters

## Slide 24: Search for CeC signature and observation of regular bunched electron cooling of 26.5 GeV/u Au ion beam
Changing e-beam energy requires multiple adjustments
120 μA
SRF linac voltage
No cooling
e- cooling
cooling
Ion beam trajectory radius
Bunch length
Adjusting ion beam energy – 1 mm xmean corresponds to 0.1% change in the ion beam energy.
There was no attempt of improving regular non-magnetized electron cooling – we used the lattice optimized for PCA CeC - and the best electron cooling rate was ~ 100 hours. It is consistent with cooling rate estimation made by Dmitry Kayran and 90 hours cooling rate simulated by He Zhao
There is one exception – on the 4th of July CeC evening shift we observed cooling rate of 16 hours: this event is possibly a first indication of the CeC cooling, but it is not conclusive

## Slide 25
Δx = 0.75σx
zero energy kick at 0.4σδ
Wrong sign of displacement Δx = -0.75σx
x/σx
x/σx
δ/σδ
δ/σδ
Excessive shifting of zero-kick point to δ = 0.6σδ
Kick
δ
Kick
δ
Kick
δ
x/σx
x/σx
δ/σδ
δ/σδ
Distribution of cooling between longitudinal and transverse degrees of freedom – real kick

## Slide 26: Distribution of cooling between longitudinal and transverse degrees of freedom – linearized kick
r = 0
r = 0.5
r = -0.5
r = -1
r = -1.5

## Slide 27: Linearized case: cooling decrements
Can use a non-achromatic transport (time of flight dependence)
or transverse beam separation to couple longitudinal and transverse cooling
Sorry for repeating trivial formulae from my AP class
We will neglect transverse kicks, which are very weak in CeC

## Slide 28: Encountered challenges
In Run 2018, while operating with FEL amplifier, we discovered that electron beam in the low energy (ballistic compression) section was developing very strong longitudinal instability. Detailed studies showed that this was Plasma-Cascade Instability caused by strong transverse focusing. We developed lattice of the CeC accelerator suppressing this instability and providing quiet electron beam with noise comparable with that of the shot-noise.
In Run 2021, we attempted to demonstrate CeC, but 5x10-4 relative beam energy jitter - caused by 15 psec RMS time jitter of the seed laser pulses - prevented us from observing CeC. It simply was washed away.
Two additional challenges are coming from 113 MHz SRF gun axis offset from the CeC accelerator beam-line and from presence of transverse field components in 500 MHz bunching cavity. Time-dependent variation of beam centroid create additional complications in beam diagnostics as well as in creating compact e-beam
In Run 2022, a new seed laser with 3 psec RMS time jitter was incorporated, and we achieved beam parameters sufficient for observation of the CeC cooling. Unfortunately, two major failures, both caused by human errors, consumed 71% of the run time and we were unable to complete the experiment – we simply run out of time
Run 2023 had additional challenges: it was in the Summer and systems suffered from overheating and AC failures. It also was cut short by a accident with LiHe system in late June.
Main remaining challenge is large (5% RMS) jitter in the energy of the laser pulses and corresponding variations of the electron bunch charge. This jitter causes significant variation in space-charge dominated dynamics of the electron beam and should be eliminated for reliable measurements and demonstration of CeC