## Slide 1: 25 years of RHIC Achieved performance and the role of stochastic and electron cooling
31 October 2025
Wolfram Fischer Deputy ALD for Accelerators, Nuclear and Particle Physics Chair, Collider-Accelerator Department
Notes: 30 min including questions => 25 slides

## Slide 2
Relativistic Heavy Ion Collider
New York City

## Slide 3: Contents
Before RHIC
The RHIC design
  Ions
  Polarized protons
Performance evolutions
  Luminosity, polarization
  Species and “exotic runs”

## Slide 4: Life cycle of a large accelerator facility
RHIC (this talk)
EIC (Mon talk MOA1 Sergei Nagaitsev)
Pre-project R&D [few decades]
Operation annual ops cost ~10% construction cost [few decades]
Re-use for next facility or shut-down
Construction [~decade]

## Slide 6
[Y.Y. Lee, ”50 years of the BNL AGS”, 14th Intl. Conf. on Accelerator and Beam Utilization, Gyeongju, Korea (2010).]
No 200 MeV Linac yet (1970) No 1.5 GeV Booster yet (1990)
1959: CERN PS

## Slide 7: ISABELLE
Early 1970 studies for 200+200 GeV proton-proton collider superconducting magnets
3.8 km circumference, 6 intersection, AGS as injector
At the same time Fermilab started working on the Tevatron
Tunnel, office building, He cryo plant built (updated and still in use today)
Only one working dipole prototype (Mark V) – sc cable issues
1983 canceled in favor of SSC (itself canceled in 1993)
BNL quickly build a heavy ion physics program with AGS
Ernest Courant 1920-2020
[Ernest D. Courant, “Accelerators, colliders, and snakes”, Annu. Rev. Nucl. Sci. 2003. 53:1-37]

## Slide 8: Relativistic Heavy Ion Collider
1984 began to think about heavy ion collider
~100 GeV/nucleon, dipoles ~3.5 T (5 T for ISABELLE)
transfer line from Tandem, develop heavy ion beams in AGS, with heavy ion experiments
1991 construction begins
2000 first collisions
[Ernest D. Courant, “Accelerators, colliders, and snakes”, Annu. Rev. Nucl. Sci. 2003. 53:1-37]
Satoshi Ozaki
Mike Harrison
Tom Ludlam

## Slide 9: Relativistic Heavy Ion Collider – main parameters
RF
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
(s)PHENIX
(PHOBOS) Electron lenses
Polarized Jet Target
(BRAHMS) Electron cooling
EBIS
BLIP
TPL
Start operation : 2000
Circumference : 3.8 km
Max dipole field : 3.5 T Energy : 255 GeV polarized p : 100 GeV/nucleon Au
Species : ph to U (incl. asymmetric) Experiments : BRAHMS, PHOBOS (complete) STAR, PHENIXgsPHENIX

## Slide 10: RHIC Design Manual
reached Lavg = 88×1026 cm-2s-1 (44x design)
reached Lavg = 24.8×1031 cm-2s-1 (25x design) with Pavg = 57%

## Slide 11: RHIC Design Manual (July 1998)
IR design with beam splitting DX dipoles first
DX dipole
D0,Q1—Q3
DX dipoles
Lmag = 3.7 m, Bmax = 4.3 T
large aperture (18 cm coil ID)
only magnets that need training (~5 for IR6/8 only)
 Interaction Point
Notes: MAKE REAL CALCULATION FOR DX MOVE

## Slide 12: Transition crossing – with sc magnets
[M. Harrison, S. Peggs, and T. Roser, “The RHIC accelerator”, Annu. Rev. Nucl. Sci. 2002. 52:425-369]
Did limit intensity for some time:
Initially no gamma-t quads
Electron clouds
Instabilities

## Slide 13
Claudia Ratti,
University of Houston
RHIC CDR, 1986

## Slide 15: Configuration Manual Polarized Proton Collider, 2006
reached Lavg = 2.5×1032 cm-2s-1
reached Pavg = 57% (avg. over 3D distribution and time)
Notes: A little sloppy with 10% effects

## Slide 16: Early interest in cooling for RHIC
Simon Van der Meer, 1984

## Slide 17: RHIC performance evolutions
Au+Au luminosity at 100 GeV/nucleon
p+p luminosity and polarization (100 and 255 GeV)
Medium heavy (Cu+Cu, O+O)
Asymmetric collisions (p+Au, d+Au, h+Au, Cu+Au)
U+U (non-spherical), Zr+Zr / Ru+Ru (same A = 95, max different DZ = 4)
Au+Au luminosity at 3.85 to 9.8 GeV/nucleon (Beam Energy Scan, including a fixed target program)
New detector for 2023 to 2025: sPHENIX
only ion combination shared between
RHIC and LHC is O+O (except for p)

## Slide 18
RHIC Au+Au / U+U operation at full energy
can now be done in 1/2 day (200x faster)

## Slide 19: Performance limits – RHIC ions, high energy
Bunch intensity Nb, limited by injectors EBIS, bunch merges in Booster and AGS transition instability luminosity lifetime aim for >2x109 in store ultimately
Intrabeam scattering => stochastic cooling
Lattice with small b* and large off-momentum dynamic aperture with hourglass factor ≈0.5 at end of store, need large b* reduction any lattice change must not result in additional beam losses dynamic b* reduction after emittance decreased by cooling
Goal is to have burn-off as the dominant beam loss mechanism.

## Slide 20: RHIC Run-14 Delivering RHIC-II luminosity
2007, Beginning of RHIC-II upgrade
2014, End of RHIC-II upgrade
Increase in initial luminosity result of larger bunch intensity
Increase in luminosity lifetime result of 3D cooling, >90% burn-off

## Slide 21: 3D stochastic cooling for heavy ions
M. Brennan, M. Blaskiewicz, F. Severino, PRL 100 174803 (2008); K. Mernick PRSTAB, PAC, EPAC
longitudinal kicker cavity (half side with waveguides)
horizontal kicker (open)
horizontal and vertical pickups
longitudinal pickup
5-9 GHz, cooling times ~1 h
vertical kicker (closed)
Notes: Frequency range: 5-8 GHz transverse, 6-9 GHz longitudinal

## Slide 22: Operation at burn-off limit in U+U
97% of intensity burned off at Lmax
Burn-off dominated operation allows for determination of total U+U cross section – and comparison with calculation (mostly QED) (published in Phys. Rev. C) =>

## Slide 23: Au bunch intensity evolution
main limits: - injectors output - e-cloud in RHIC
- transition instability in RHIC
Today, Run-25
AGS 12g6g2 merge
EBIS, Booster 4g2g1, AGS 8g4g2 merge
scrubbing with protons
111 bunches
43 bunches
gt-jump, octupoles at transition

## Slide 24: Run-18 Zr+Zr/Ru+Ru – same A, different Z (CME) Zr-96/Ru-96
Extraordinary help from DOE, ORNL, RIKEN for source material and preparation
Ru isotopes

## Slide 25: Run-18 Zr+Zr/Ru+Ru at 100 GeV/nucleon
Run Coordinator: Greg Marr paper: IPAC 2019
Zr+Zr
Ru+Ru
Zr+Zr
Ru+Ru
Ru+Ru
Zr+Zr
Ru+Ru
Zr+Zr
CeC PoP dedicated
scheduled maintenance
Store-by-store species change and flat luminosity of 21.5×1026 cm-2s-1
20 h nominal store length (WEEK: 30-Apr-18 to 07-May-18)

## Slide 26: How did stochastic cooling change heavy ion collider operation?
Increased in luminosity lifetime from ~2.5 h Au+Au up to infinite
Allowed for increase in bunch intensity L ~ Nb2
Increased optimum store length from 4 to 8 h for Au+Au, resulting in more time in collision, less time refilling
Can tolerate emittance growth during acceleration (from IBS, transition instabilities) as long as no intensity is lost
Operation close to burn-off limit, full use of accelerated intensity
Allowed flat luminosity for alternating species (Ru+Ru/Zr+Zr)

## Slide 27: Low-Energy RHIC electron Cooling (LEReC) for the Beam Energy Scan I and II (BES-I, II)
[2015 NSAC Long Range Plan for Nuclear Science]
BES-I in 2010/11/14
BES-II: 10x increase in the number of events
Au+Au collisions down to 3.85 GeV/n (40% of CoM energy at nominal injection)
Luminosity really low
  Space charge
  Intrabeam scattering
  Magnetic field errors (also time dependent)
  Large beam with losses
BES-II goal of 4x luminosity over 3.85 – 9.8 GeV/n (highest energy is nominal injection)
Designed cooler for 2 lowest energies
Notes: Picture from 2015 NSAC long-range plan

## Slide 28: LEReC Accelerator (100 meters of beamlines with the DC Gun, high-power fiber laser, 5 RF systems, including one SRF, many magnets and instrumentation)
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
High-Power Beam Dump
Extraction beam line
DC e- Gun
704 MHz SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Injection beam dump
RF Diagnostic Beamline
RHIC TRIPLET
RHIC DX
180°
Bending
Magnet
e-
e-
e-
* NOT to scale
Cathode
loading system
LF solenoid
HF solenoid
Transport solenoid
ERL solenoid
Quad corrector
Trim corrector
Corrector 3.8 ID
Corrector 6.0 ID
BPM 2.4 ID
BPM 4.8 ID
Bellows
Ion pump
Merger
Beamline
Transport
Beamline
704 MHz Cu Deflector Cavity

## Slide 29: Low Energy RHIC electron Cooler
A.V. Fedotov et al., “Experimental demonstration of hadron beam … “, PRL 124, 084801 (2020)]
LEReC operational electron cooler:
  utilizes RF-accelerated electron bunches
  uses non-magnetized electron beam (no magnetization at the cathode and no continuous solenoidal field in cooling section)
LEReC approach to cooling is directly scalable to high-energies – pre-cooler in EIC at injection

## Slide 30: First LEReC cooling observation 5 Apr 2019
Notes: 5 Apr 2025

## Slide 31: BES-I vs BES-II luminosity
Run Coordinator: Chuyu Liu (Run-19 to 21)
3rd year
1st year
2nd year
Goal was
Lavg (BES-II) = 4x Lavg (BES-I)

## Slide 32: R&D for high-energy cooling in EIC
CeC Experiment at RHIC
V. Litvinenko, “Results on the Coherent electron Cooling experiment at RHIC” (MOD3)
Y. Jing, “Electron beam dynamics simulation in CeC performance with low beam current” (THA2)
G. Wang, “Simulation of the ion bunch in the presence of the CeC for the new energy scheme” (THA3)
Design studies for EIC
A. Fedotov, “Hadron beam cooling and cooler design status for the EIC” (TUA1)
E. Wang, “Electron Ion Collider Strong Hadron Cooling design summary” (TUA2)
W. Bergan, “EIC luminosity models for various hadron cooling scenarios” (TUA3)
S. Seletskiy, “Development of storage ring electron cooler for high energy applications” (TUB1)
D. Kayran, “Electron cooler for high-energy hadrons based on ERL” (TUB2)
M. Blaskiewicz, “Stochastic cooling for the EIC” (TUB3)
K. Deitrick, “Design of a microbunched electron cooler ERL” (THB1)
J. Kewisch, “Optics design for a storage ring based electron cooler for cooling at high energies” (THB2)
S. Setiniyaz, “BBU threshold and digital feedback suppression for frequency-scaled BNL cavities in the EIC ERL” (THC2)
I. Pinayev, “Beam position monitoring for low energy cooling section” (THC3)

## Slide 33: CeC experiment – Vladimir Litvinenko
[V. Litvinenko, “Results on the Coherent electron Cooling experiment at RHIC” (MOD3)]

## Slide 34
RHIC p+p operation at 100 / 255 GeV
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
Solenoid Partial Siberian Snake
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS Polarimeters
Spin flipper

## Slide 35
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
Solenoid Partial Siberian Snake
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS Polarimeters
Spin flipper
Special devices for polarized protons: source, polarimeters, snakes, rotator, flipper

## Slide 36: p bunch intensity and polarization
FOM = LP4 ~ Nb2P4
main limits: - injectors output - polarization - e-cloud in RHIC - beam-beam in RHIC
beam-beam compensation
polarized source upgrade with Atomic Beam Source
AGS tune jumps, RHIC 9 MHz RF
AGS cold snake
polarized source upgrade with sc solenoid
AGS warm snake
A. Zelenski, H. Huang, K. Gardner, K. Zeno, RF, et al.
(double-spin experiments)

## Slide 37: Head-on bb compensation
tune distribution measured with BTF and p+Al collisions proton beam: (Qx,Qy) = (.685,.695); Al beam: (Qx,Qy) = (.685,.695); DQx, DQy >> x => no coherent modes
no bb
2x bb
DQ reduction from e-lens
Can only reduced BB tune spread (black curve is limit)
Tune footprint compression with a Gaussian electron beam
[W. Fischer, et al., ”Operational head-on beam-beam compensation with electron lenses in the Relativistic Heavy Ion Collider", Phys. Rev. Lett. 115, 264801 (2015).]

## Slide 38: Run-25
short in superconducting bus
repair required partial warm-up
opened several cryostats
65 days
damaged 69 kV power line
repair shut off Central Cryo Plant
required managing helium inventory
15 days
unsynchronized beam abort
Yellow abort vacuum repair
14 days
Run Coordinator: Travis Shrey

## Slide 39
L design
nominal injection
L design
Used stochastic or electron cooling in 1 or 2 beams

## Slide 40: RHIC after 25 years of physics …
Full energy Au+Au Lavg = 44x design enabled by stochastic cooling
Only p+p collider, Lavg = 1.3x design, P ~ 57% (70% design)
Many species and combinations, incl. asymmetric and low natural abundance some only possible with stochastic cooling
Extended energy range slightly above; and significantly below nominal injection enabled by electron cooling
Developed technology for evolving program: polarized beams, sources, cooling
Most of RHIC complex will be re-used for the Electron-Ion Collider demonstration of RF accelerated electron cooling used for proton pre-cooling
Nominal injection

## Slide 41
COOL’25, Stony Brook University, 26-31 October 2025

## Slide 42: Abstract
The Relativistic Heavy Ion Collider (RHIC) at Brookhaven National Laboratory began operation 25 years ago, initiating a program of high-energy ion collisions that has since evolved in remarkable ways. Within a few years, polarized proton collisions were introduced, and over the following decades RHIC continuously expanded its capabilities—achieving higher luminosity, greater polarization, and a wide range of ion species and operating modes. As RHIC now enters its final physics run, its hadron injectors, one of its collider rings, and its technical infrastructure are being prepared to support the next major facility, the Electron-Ion Collider. We reflect on 25 years of RHIC operations and highlight the key performance advances that made its success possible, particularly the impact of stochastic and electron cooling.
Notes: ~45 min, ~40 slides

## Slide 43: What made 25 years possible?
Facility remains priority of science community, science program evolved in new directions, detector upgrades
Evolving physics program needs could be met with evolving accelerator developments (L, P, flexibility)
  Stochastic cooling enabled heavy ion L increases
  Rare species (Ru-96/Zr-96) => required ORNL for Run-96 enrichment (with DOE support), existing BNL sources, help from RIKEN, stochastic cooling
  Electron cooling (LEReC) enabled operation far below nominal injection energy
Strong funding agency commitment – DOE Office of Nuclear Physics